Technical Specifications for TAXI

(Web Services using tML)

Implementation

Version 4.3

Disclaimer:  The Technical Specification document provides Verizon’s rules regarding TAXI xML implementation.  Based off industry standards, this document is non-binding but is the basis for all customer implementation.  Updates/edits may occur at anytime, but not without notice to the TAXI customer base.

Table 1.  Document Revision History

| Date | Version | Description |
| --- | --- | --- |
| 6/9/2010 | 4.3 Final | Added Disclaimer to the title page. |
| 6/3/2010 | 4.3 Draft | Removed ManagedObjectInstanceItem from Table 17 for Retrieve Trouble Report Attributes Response. Updated §6.8.2.1 and §6.8.2.2 examples for Retreive Trouble Report Attributes to have ActivityDuration instead of ActivityDurationList |
| 5/13/2010 | 4.3 Draft | Updated CannotVerifyOrDeniedAtThisTime to have length 1+ under VerifyRepairCompletionResponse. Updated TABase XSD. |
| 5/1/2010 | 4.3 Draft | §4.4.1 Notify Request sample soap message Removed <string> in notify method invocation because TAXI does not send <string> in production. |
| 3/12/10 | 4.3 Draft | Added Explainatory Diagram for Annex F Escalation Annex G Authorization Annex H Close Out Verification (EBV) Added MultiCreate definition in XSD Added RequestId in all transactions in XSD. |
| 2/2/2010 | 4.3 Draft | Table 9 P73 “However, TroubleReportChangeDenied does not have ExceptionList aggregate.” §6.3.3 Partial Success Sample XML Replaced ChangedDeniced with Process Failure as an exception condition §6.3.4 Modification Response Exception Added TroubleReportChangeDenied exception. |
| 11/18/09 | 4.2 Final | Updating header/footer to finalize version 4.2. |
| 9/1/2009 | 4.2 Draft | § 5.2 Create Request, Fixed P44 AuthPerson and AuthTime are optional fields. Clarify: ManagedObjectInstanceAliasList should only contain only one ManagedObjectInstanceAliasListItem § 5.6 Retrieve Trouble Report Attributes Request, Fixed: changed parent tag from “AttributeList” to “RetrieveAttributes” to reflect T1.278 standard. §6.8.1.1 & § 6.8.2.1 Retrieve TroubleReport Attributes Request sample XML Clarified: the request could be sent in three different formats, with the first one preferred over the other two. |
| 8/20/2009 | 4.1 | Designate as final version |
| 5/25/2009 | 4.1 Draft | 1. Added mapping table for “Retrieve Technician Notes Request & Response” §5.15 2. Added sample tML for Retrieve Technician Notes Request & Response §6.15 |
| 10/29/2008 | 4.0 | Designatng as Official |
| 10/1/2008 | 4.0 Draft | Changed document title to “Technical Specifications for TAXI Implementation” from “Technical Specifications for TAXI Wholesale Implementation” Added “Service offered” colume section 3.4 table to indicate transactions and services they are offered in, e.g. Local, Access or Retail. See table on page 20 Changed heading from “Access Carriers Customers” to “Access Carriers and/or Retail Customers” in sample tML headings, see heading in table of content, e.g. 6.2.2, 6.6.2, 6.8.2, and 7.4.2. Added top-attribute heading for data definition table, clarified conditional/required field definition, see footnote 7 on Page 39. |
| 9/25/2008 | 4.0 Draft | Phone field in all transactions are changed from length of 10 digit, to 18 characters of alpha numeric. E.g. phone field length definition at page 41, 43. |
| 4/3/2008 | 3.5 | Added New Transaction RetrieveLocalContactByTroubleIdRequest / RetrieveLocalContactByTroubleIdResponse |
| 11/6/2007 | 3.4 | Fixed typos Table 26 Performance Monitoring Request, Row Interval: Changed valid values from “0-7” to “1-7”, from “0 to 32” to “1 to 32” Table 29 SetLoopbackRequest, Row Direction, fixed typos from “Dircetion” Row Duration, fixed valid value “0-120” to “1-120” |
| 8/12/2007 | 3.4 Final | Inserted descriptions for transaction §5.10 QuickTest §5.11 PerformanceMonitoring, §5.12 SetLoopback §5.13 ReleaseLoopback, |
| 4/23./2007 | 3.4 Draft | Table 8, Added usage for top level TA attribute in ModifyRequest §6.3.1 Added description on how to use ModifyRequest. |
| 4/15/2007 | 3.4 Draft | Annex E Trouble Ticket Late Bonding section. Added mention of RetreiveTroubleReprot might return FULL TAXI trouble report number instead of abbreviated trouble report number in the request. Changed length of TroubleReportID from 64 max to 32 max throughout the document. Table 3, 4, 6, 7. NetworkID value on POTSServiceTestResponse and RequestTroubleCreationResponse is maximum 5 characters. |
| 3/26/2007 | 3.4 Draft | Added Annex E Trouble Ticket Late Bonding section. Added reference to Annex E in §5.2 Trouble Report Create §5.6 Retrieve Trouble Report Attributes §5.9 Multiple Trouble Report Create §6.2.1.3 Trouble Report Create Response – Exception (Trouble Report Already Exists) §6.2.2.3 Trouble Report Create Response – Exception (Trouble Report Already Exists) §6.8 Sample tML for Retrieve Trouble Report Attributes §6.9.1.3 Multiple Trouble Report Create Response – Exception (Trouble Report Already Exists) |
| 3/26/2007 | 3.3 draft | 1. <tML-ServiceTestBase:ErrorMessage> & <tML-ServiceTestBase:InfoMessage> are optionals. Updated in 3.3 Mapping Section for QuickTest, PerformanceMonitoring, SetLoopBack, ReleaseLoopBack 2. <tML-TABase:Disposition> is optional. Updated in 3.3 Mapping Section for QuickTest, PerformanceMonitoring, SetLoopBack, ReleaseLoopBack 3. <tML-TABase:DispositionNumber> doesn't appear in response. Deleted from in 3.3 Mapping Section and Sample for QuickTest, PerformanceMonitoring, SetLoopBack, ReleaseLoopBack 4. <tML-TABase:DescriptorsNumber> comes under the root tag <tML-ServiceTestBase:Descriptors>. Updated in 3.3 Mapping Section and Sample for QuickTest, PerformanceMonitoring, SetLoopBack, ReleaseLoopBack 5. <tML-ServiceTestBase:Index> comes under the root tag <tML-ServiceTestBase:Descriptor> Updated in 3.3 Mapping Section and Sample for QuickTest, PerformanceMonitoring, SetLoopBack, ReleaseLoopBack Changed table header formating in Section 5.1 POTS Line Test |
| 3/19/2007 | 3.3 draft | Deleted reference in 3.4 for following transactions (will not implement) QuickTestNotification PerformanceMonitoringNotification ReleaseLoopbackNotification Corrected typo in 6.11.1 Sample XML for PerformanceMonitoringRequest Changed <tML-ServiceTestBase:Duration> tag to <tML-ServiceTestBase:Frequency>Tag. |
| 3/1/2007 | 3.3 draft | Corrected Name Space in sample XMLs for QuickTest, PerformanceMonitoring, SetLoopback, ReleaseLoopback. The previous name space was exclusively tML-TABase, and the new sample changed XML body tags to tML-ServiceTestBase, while retaining tML-TABase name space for transaction headers. (Customer node, ManagedObjectInstance node). |
| 2/15/2007 | 3.3 draft | Added tags “JobType” and “DispatchAuth” to QuickTestRequest |
| 1/20/07 | 3.3 draft | Special Line test transaction are added. The new transactions are: 1. QuickTest Request, Response and Notification (intermediate status), 2. PerformanceMonitoring, Request, Response and Notification (intermediate status) 3. SetLoopback Request and Response 4. ReleaseLoopback, Request, Response (for ITS initiated) and Notification (for Delphi initiated). |
| 11/20/06 | 3.2 final | Added transaction for MultiTroubleReportCreationRequest MultiTroubleReportCreationResponse |
| 11/06/06 | 3.1 final | AdditionalTroubleInfoListItem Added note to indicate only first 3 elements will be processed. Page 167 Added alternative serial circuit format. A.k.a double slashes. e.g. 24/HCGS/123456//NY |
| 08/30/06 | 3.1 | Updated correct URLs in section 7.4.1.1.1 and 7.4.1.1.2 Corrected spelling of AttributeValueChangeNotification in multiple places Updated sample request and response SOAP structures in Section 4 |
| 03/31/06 | 3.1 | ManagerContactPerson.Phone is required field when ManagerContactPerson attribute is present. Update circuit format definition for Carrier Facility circuit to accomondate fGTE circuits Escalation level support has been changed from 1-6 to 1-4. For synchronous transactions, there is a two minutes (120 seconds) time out from Verizon side. If a customer is unable to receive Verizon’s response after two minutes, Verizon TAXI Web Service will time out. New WSDLs added for Access Carriers and CLECs on page 11, Section 3.3.1 Added updated WSDLs on page 169, Section 7.1 |
| 03/28/06 | 3.1 | 1. Modify and Notification contract definition change. Escalation Level attribute changed from 6 Levels to 4 levels. 2. Escalation Levels in Sample XML changed from level 6 to level 2 |
| 12/23/05 | 3.0 | Added support for RPC style WSDL |
| 07/27/05 | 2.9 | 1. Version changes to 2.9 2. Remove contact information Pg. #2 3. Remove most of Document Revision History, Pgs. #3,4, leaving only revision note for this update 4. Review the Trouble Report Cancellation Policy, Page #62 (check spelling - see technitian - should be technician and cancle should be cancel) 5. Correct spelling of "Inbound" in para. 7.3.1, Page #164 6. Remove section 7.5 <Customer > URLs Pg.#166 7. Change references of "CTE Testing" to "TAPP Testing". 8. Change references of "web services" to "TAXI web services" 9. Create Acronyms List in document. 10. Run spell checker. |
| 08/22/05 | 2.10 | Add a footnote in §8 regarding the value of “36” for Trouble Report Status defined in ANSI T1.227: Status Code 36 was approved 3/2001 by the Standard's organization, but has not been formally added to T1.227 yet. Verizon will insure that Status Code 36 is included in the next T1.227 update. Definition for Status Code 36 - Repaired Pending Validation - refers to the state where the Central Office Technician has Cleared a problem in the network and sent the ticket back to the Test Center where it is pending on the work list until a Tester is available. |
| 08/30/05 | 2.11 | Update Inbound Digital Certificate section per request from Verizon Connectivity Management |
| 09/09/05 | 2.12 | Added WS-I compliant WSDLs for TA, callback, and notify. |

Table of Contents

1	Introduction	12

1.1	TAXI  (Web Services using tML)	12

1.2	Scope	12

1.3	System Requirements	12

2	TAXI  Architecture	13

2.1	Overview	13

2.2	TAXI Security	13

3	Web Services Description Language (WSDL) for TAXI	14

3.1	General Guideline	14

3.2	Protocol for Web Services	14

3.3	WSDL Files	14

3.3.1	Document Style	14

3.3.1.1	Synchronous Request/Response and Asynchronous Request Services WSDL	14

3.3.1.2	Callback Service WSDL	15

3.3.1.3	Notification Service WSDL	16

3.3.2	RPC Style	17

3.3.2.1	Synchronous Request/Response and Asynchronous Request Services WSDL	17

3.3.2.2	Callback Service WSDL	18

3.3.2.3	Notification Service WSDL	18

3.4	Operation Names of TAXI WSDLs	20

3.5	Exception Handling	21

4	SOAP Structure for TAXI	22

4.1	Synchronized Request/Response	22

4.1.1	Sample SOAP Request	22

4.1.2	Sample SOAP Response	22

4.1.3	Sample SOAP fault message	22

4.2	One-way Send Only	23

4.2.1	Sample SOAP Request	23

4.2.2	Sample SOAP Response	23

4.2.3	Sample SOAP fault message	23

4.3	Callback Service	24

4.3.1	Sample SOAP Request	24

4.3.2	Sample SOAP Response	24

4.3.3	Sample SOAP fault message	24

4.4	Notification  Service	25

4.4.1	Sample SOAP Request	25

4.4.2	Sample SOAP Response	25

4.4.3	Sample SOAP fault message	25

4.5	Sample Soap Message	26

5	tML Specification	28

5.1	POTS Service Test	28

5.2	Trouble Report Create	37

5.3	Trouble Report Modification	59

5.4	Trouble Report Cancellation	75

5.5	Trouble Report Close Out Verification	82

5.6	Retrieve Trouble Report Attributes	89

5.7	Trouble Report AVC Event Notification	115

5.8	Trouble Report Close Out Notification	125

5.9	Multiple Trouble Report Create	129

5.10	Quick Test	152

5.11	Performance Monitoring	158

5.12	Set Loopback	162

5.13	Release Loopback	166

5.14	Retrieve Local Contact by Trouble Report Id	169

5.15	Retrieve Technician Notes By Trouble Report Id	176

6	Sample tML	180

6.1	Sample tML for POTS Service Test	180

6.1.1	Request	180

6.1.2	Response – Normal (Full – TestRequestType is 1)	180

6.1.3	Response – Normal (Quick Test RequestType is 2)	181

6.1.4	Response – Normal (Central Office TestRequestType is 3)	182

6.1.5	Response – Normal (Loop TestRequestType is 4)	183

6.1.6	Response – Error (Case 1)	184

6.1.7	Response – Error (Case 2)	185

6.2	Sample tML for Trouble Report Create	186

6.2.1	Local Customers	186

6.2.1.1	Trouble Report Create Request	186

6.2.1.2	Trouble Report Create Response – Normal	189

6.2.1.3	Trouble Report Create Response – Exception (Trouble Report Already Exists)	190

6.2.1.4	Trouble Report Create Response – Exception (Req Attributes Missing)	191

6.2.1.5	Trouble Report Create Response – Exception (Fall Back Reporting)	191

6.2.1.6	Trouble Report Create Response – Exception (Invalid Data Received)	192

6.2.1.7	Trouble Report Create Response – Exception (Processing Failure)	193

6.2.2	Access Carrier and/or Retail Customers	193

6.2.2.1	Trouble Report Create Request	193

6.2.2.2	Trouble Report Create Response – Normal	196

6.2.2.3	Trouble Report Create Response – Exception (Trouble Report Already Exists)	197

6.2.2.4	Trouble Report Create Response – Exception (Req Attributes Missing)	198

6.2.2.5	Trouble Report Create Response – Exception (Fall Back Reporting)	199

6.2.2.6	Trouble Report Create Response – Exception (Invalid Data Received)	199

6.2.2.7	Trouble Report Create Response – Exception (Processing Failure)	200

6.3	Sample tML for Trouble Report Modification	201

6.3.1	Trouble Report Modification Request	201

6.3.2	Trouble Report Modification Response – Normal	204

6.3.3	Trouble Report Modification Response – Partial Success	205

6.3.4	Trouble Report Modification Response – Exception	206

6.4	Sample tML for Trouble Report Cancellation	207

6.4.1	Trouble Report Cancellation Request	207

6.4.2	Trouble Report Cancellation Response – Normal	208

6.4.3	Trouble Report Cancellation Response – Exception	208

6.5	Sample tML for Trouble Report Close Out Verification	209

6.5.1	Trouble Report Close Out Verification Request	209

6.5.2	Trouble Report Close Out Verification Response	210

6.5.3	Trouble Report Close Out Verification Response – Exception	210

6.6	Sample tML for Trouble Report AVC Event Notification	211

6.6.1	Local Customers	211

6.6.2	Access Carrier and/or Retail Customers	213

6.7	Sample tML for Trouble Report Close Out Notification	215

6.7.1	Trouble Report Close Out Notification	215

6.8	Sample tML for Retrieve Trouble Report Attributes	217

6.8.1	Local Customers	217

6.8.1.1	Retrieve Trouble Report Attributes Request	217

6.8.1.2	Retrieve Trouble Report Attributes Response	221

6.8.1.3	Retrieve Trouble Report Attributes Response – Partial Success	225

6.8.1.4	Retrieve Trouble Report Attributes Response – Exception	230

6.8.2	Access Carrier and/or Retail Customers	231

6.8.2.1	Retrieve Trouble Report Attributes Request	231

6.8.2.2	Retrieve Trouble Report Attributes Response	235

6.8.2.3	Retrieve Trouble Report Attributes Response – Partial Success	239

6.8.2.4	Retrieve Trouble Report Attributes Response – Exception	244

6.9	Sample tML for Multiple Trouble Report Create	245

6.9.1	Multiple Trouble Report Create Request	245

6.9.2	Multiple Trouble Report Create Response – Normal	248

6.9.3	Multiple Trouble Report Create Response – Exception (Trouble Report Already Exists)	249

6.9.4	Multiple Trouble Report Create Response – Exception (Req Attributes Missing)	250

6.9.5	Multiple Trouble Report Create Response – Exception (Fall Back Reporting)	250

6.9.6	Multiple Trouble Report Create Response – Exception (Invalid Data Received)	251

6.9.7	Multiple Trouble Report Create Response – Exception (Processing Failure)	251

6.10	Sample tML for Quick Test	252

6.10.1	Request	252

6.10.2	Acknowledgement	253

6.10.3	Intermediate Status	253

6.10.4	Final Response	254

6.10.5	Quick Test Response (Exception)	256

6.11	Performance Monitoring	257

6.11.1	Request	257

6.11.2	Acknowledgement	258

6.11.3	Intermediate Status	258

6.11.4	Final Response	260

6.11.5	Final Response (Exception)	261

6.12	Set Loopback	262

6.12.1	Set Loopback Request	262

6.12.2	Acknowledgement	263

6.12.3	Final Response (Success)	263

6.12.4	Set Loopback Response (Exception)	265

6.13	Release Loopback	266

6.13.1	Request	266

6.13.2	Acknowledgement	267

6.13.3	Release Loopback Response (Success)	267

6.13.4	Release Loopback Response (Exception)	269

6.14	Retrieve Local Contact by TroubleReportId	269

6.14.1	RetrieveLocalContactByTroubleReportIdRequest	269

6.14.2	RetrieveLocalContactByTroubleReportIdResponse  (Normal)	270

6.14.3	RetrieveLocalContactByTroubleReportIdRequest  (Exception)	271

6.15	Sample tML for Retrieve Technician Notes	272

6.15.1.1	RetrieveTechnicianNotesByTroubleReportIdRequest	272

6.15.1.2	RetrieveTechnicianNotesByTroubleReportIDResponse  (Normal)	272

6.15.1.3	RetrieveTechnicianNotesByTroubleReportIDResponse  (Exception)	273

7	Environment Parameters	274

7.1	SOAP	274

7.2	WSDL	274

7.3	Digital Certificate	274

7.3.1	Inbound Digital Certificate for Verizon Customers (Telecommunications Companies)	274

7.3.2	Outbound Digital Certificate	274

7.3.3	Verify Distinguish Name in Callback Message by Customers	274

7.4	Verizon TAXI URLs	274

7.4.1	Local Customers	274

7.4.1.1	Document Style WSDL	274

7.4.1.1.1	End Point URL	274

7.4.1.1.2	WSDL URL	274

7.4.1.2	RPC  Style WSDL	275

7.4.1.2.1	End Point URL	275

7.4.1.2.2	WSDL URL	275

7.4.2	Access Carrier and/or Retail Customers	275

7.4.2.1	Document Style WSDL	275

7.4.2.1.1	End Point URL	275

7.4.2.1.2	WSDL URL	275

7.4.2.2	RPC Style WSDL	275

7.4.2.2.1	End Point URL	275

7.4.2.2.2	WSDL URL	275

8	References	276

Annex A	TR <XX> <YY> Construction Rules	277

A.1	<XX> vs. Test Result Code	277

A.2	<YY> vs. Dispatch Decision Chart	277

Annex B	Circuit Format Definition for Designed and Non-Designed Circuits	279

Annex C	Trouble Code Definition for POTS Service Test with FTTP Infrastructure	281

C.1	Trouble Code	281

C.2	Fault Category	281

C.2	Fault Entity	281

C.3	Fault Code	282

C.3.1	GR909 Tests Fault Codes	282

C.3.2	PON Alarm Fault Codes	282

C.3.3	Gateway Router Fault Codes	283

C.3.4	Wavesmith ATM Switch Alarms Fault Codes	283

Annex D	Acronym List	286

Annex E	Trouble Ticket Late Bonding	287

Annex F  Escalation	290

Annex G  Authorization	291

Annex H  Close Out Verification	292

List Of Tables

Table 1.  Document Revision History	2

Table 2.  POTS Service Test Request	25

Table 3.  POTS Service Test Response – Normal	27

Table 4.  POTS Service Test Response – Exception	31

Table 5.  Trouble Report Create Request	34

Table 6.  Trouble Report Create Response – Normal	50

Table 7.  Trouble Report Create Response – Exception	53

Table 8.  Trouble Report Modification Request	57

Table 9.  Trouble Report Modification Response	68

Table 10.  Trouble Report Cancellation Request	73

Table 11.  Trouble Report Cancellation Response - Normal	76

Table 12.  Trouble Report Cancellation Response - Exception	78

Table 13.  Trouble Report Close Out Verification Request	81

Table 14.  Trouble Report Close Out Verification Response – Normal	83

Table 15.  Trouble Report Close Out Verification Response – Exception	85

Table 16.  Retrieve Trouble Report Attributes Request	88

Table 17.  Retrieve Trouble Report Attributes Response	91

Table 18.  Retrieve Trouble Report Attributes Response - Exception	109

Table 19.  Trouble Report AVC Event Notification	113

Table 20.  Trouble Report Close Out Notification	123

Table 21.  Multiple Trouble Report Create Request	127

Table 22.  Multiple Trouble Report Create Response  (Normal)	142

Table 23.  Multiple Trouble Report Create Response – Exception	146

Table 24.  Quick Test Request	150

Table 25 Quick Test Response	152

Table 26.  Performance Monitoring Request	156

Table 27 Performance Monitoring Response	157

Table 28.  Set Loopback Request	160

Table 29 SetLoopback Response	162

Table 30.  ReleaseLoopback Request	164

Table 31 Release Loopback Response	165

Table 32.  Retrieve Local Contact Request	167

Table 33.  Retrieve Local Contact Response	168

Table 34.  Retrieve Local Contact Response - Exception	173

Table 35.  tML Retrieve Technician Notes  Request	174

Table 36.  tML Retrieve Technician Notes Response	175

Table 35.  <YY> Value Mapping to Verizon Dispatch Decision Chart	268

Table 36.  Fault Category for Trouble Code	272

Table 37.  Fault Entity for Trouble Code	272

Table 38.  GR909 Tests Fault Codes	273

Table 39.  PON Alarm Fault Codes	273

Table 40.  Gateway Router Fault Codes	274

Table 41.  Wavesmith ATM Switch Alarms Fault Codes	274

List Of Figures

Figure 1 TA Webservice Architecture Diagram	14

Figure 2 Late Bond after receiving error "Trouble Report Already Exist" during a TAXI Create Request	288

Figure 3 Direct Late Bond	289

Figure 4 Escalation Process Diagram	291

Figure 5 Authorization Processing Diagram	292

Figure 6 Close Out Verification (EBV) Processing	293

# Introduction

## TAXI  (Web Services using tML)

This document provides the following information:

- WSDL

- SOAP

- tML specifications

- Environment Parameters

- Sample tMLs

## Scope

The implementation for Trouble Administration will cover the following services:

- Service Test (POTS only)

- Trouble Report Create

- Trouble Report Modification

- Trouble Report Cancellation

- Trouble Report Close Out Verification

- Retrieve Trouble Report Attributes

- Retrieve Trouble Report Technician Notes

- Trouble Report AVC Event Notification

- Trouble Report Close Out Event Notification

- Trouble Report Retrieval and Late Bonding Process

- Special Circuit Test:Quick Test

- Special Circuit Test: Performance Monitoring (Special Circuits)

- Special Circuit Test: Set Loopback and Release Loopback

The intended Verizon customers for using the above mentioned services are:

- Inter Exchange Carriers (IECs – Access Carrier Customers)

- Competitive Local Exchange Carriers (CLECs – Local Customers)

## System Requirements

- Web Services with Digital Certificate (see §7.3 for detailed information)

- SOAP version  1.1

- WSDL 1.1

# TAXI  Architecture

## Overview

TA web service architecture will follow B2B integration mode between service partners. They represent the TA service requester and TA service provider. Verizon Wholesale will be the service provider Service Test (POTS Only) service. Verizon customers such as a CLEC will be the TA service requester.

Figure 1 TA Webservice Architecture Diagram

As shown above, the SOAP request from IEC/CLEC will flow through Verizon firewall system, and get to the TA web service platform. The following is the message flow between TA web service requester and service provider:

- The IEC/CLEC application sends SOAP request through the Verizon firewall system using HTTPS connection and two-way certificate handshaking.

- Verizon firewall system authenticates and authorizes IEC/CLEC SOAP requests and routes IEC/CLEC SOAP requests to TAXI platform.

- TAXI platform gets SOAP requests, process the SOAP request, and the send back the SOAP response to the IEC/CLECs.

- In case of callback, TAXI platform component will invoke IEC/CLEC web services to send asynchronous SOAP message back to IEC/CLEC application.

Service Test (POTS Only) web service will be using asynchronous interaction mode. The actual response for the Service Test (POTS Only) will be provided through the callback web service IEC/CLEC will provide for the service provider to invoke to send the Service Test (POTS Only) response back to the IEC/CLEC.

Multiple Trouble Report Create web service will be using asynchronous interaction mode. The actual response for the Multiple Trouble Report Create  will be provided through the callback web service IEC/CLEC will provide for the service provider to invoke to send the Multiple Trouble Report Create response back to the IEC/CLEC.

## TAXI Security

Message sent by the IEC/CLEC will be SOAP message, with tML in the SOAP body as the payload. The response messages IEC/CLEC gets will be either the normal response with tML as the payload, or soap fault message. Message flow from IEC/CLEC applications to Verizon firewall system will use HTTPs with two-way verification. Message flow from Verizon firewall system and TAXI  platform will be normal HTTP message. TA web service requests will be authenticated and authorized in Verizon firewall layer

# Web Services Description Language (WSDL) for TAXI

## General Guideline

TAXI will support both Document and RPC style Web services at this point.  The service can be either synchronized or asynchronized.  For both Document and RPC style web services, only one input argument will be taken per service, and it is in xml format.  The response is also in the format of xml string. Verizon strongly encourage both local and access customers to use Document style web service since it is recommended by WS-I as a standard.

## Protocol for Web Services

The potential protocol that can be used for web service is HTTPS. The end point to the external IEC/CLEC is the Verizon firewall system URL, where Verizon firewall system will use soap junction to route to the actual TAXI.

## WSDL Files

The interface for a service customer is a WSDL file. WSDL is an XML format for describing network services as a set of endpoints operating on messages containing either document-oriented or procedure-oriented information. The operations and messages are described abstractly, and then bound to a concrete network protocol and message format to define an endpoint.

The synchronized request/response WSDL supports one synchronous operation: processSync, which takes one string parameter, and return one string of response. The parameter it takes, and the response it returns, will be the actual tML request and response messages. At this point, both Document and RPC style web services are supported. Verizon strongly encourage both local and access customers to use Document style WSDL since it is recommended by WS-I as a standard.

The one-way send WSDL will be used by local customers to send long transactions like Service Test (POTS Only), where a local customer needs to use the one-way send WSDL to send SOAP request with tML as payload to us. When the tML response is ready, we will use the callback service the local customer provided to send the SOAP response back. In both sendonly and callback cases, no tML acknowledge is provided from the peer. The SOAP fault message will indicate the transaction fails due to communication failures, timeout, or bad-formed tML, etc.

### Document Style

The following WSDLs are WS-I compliant.

#### Synchronous Request/Response and Asynchronous Request Services WSDL

<?xml version="1.0" encoding="UTF-8"?>

<definitions xmlns:tns="java:com.verizon.webservices.adapter.proxy" xmlns:wsr="http://www.openuri.org/2002/10/soap/reliability/" xmlns:mime="http://schemas.xmlsoap.org/wsdl/mime/" xmlns:soap12="http://schemas.xmlsoap.org/wsdl/soap12/" xmlns:http="http://schemas.xmlsoap.org/wsdl/http/" xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/" xmlns:soap12enc="http://www.w3.org/2003/05/soap-encoding" xmlns:conv="http://www.openuri.org/2002/04/wsdl/conversation/" xmlns:soap="http://schemas.xmlsoap.org/wsdl/soap/" xmlns:s="http://www.w3.org/2001/XMLSchema" xmlns="http://schemas.xmlsoap.org/wsdl/" targetNamespace="java:com.verizon.webservices.adapter.proxy">

<types>

<xsd:schema xmlns:xsd="http://www.w3.org/2001/XMLSchema" xmlns:stns="java:com.verizon.webservices.adapter.proxy" elementFormDefault="qualified" attributeFormDefault="qualified" targetNamespace="java:com.verizon.webservices.adapter.proxy">

<xsd:element type="xsd:string" name="processSync" nillable="true"/>

<xsd:element type="xsd:string" name="processSyncResponse" nillable="true"/>

<xsd:element type="xsd:string" name="send" nillable="true"/>

</xsd:schema>

</types>

<message name="processSync">

<part xmlns:partns="java:com.verizon.webservices.adapter.proxy" name="string" element="partns:processSync"/>

</message>

<message name="processSyncResponse">

<part xmlns:partns="java:com.verizon.webservices.adapter.proxy" name="result" element="partns:processSyncResponse"/>

</message>

<message name="send">

<part xmlns:partns="java:com.verizon.webservices.adapter.proxy" name="string" element="partns:send"/>

</message>

<message name="sendResponse"/>

<portType name="doctaservicePort">

<operation name="processSync">

<input message="tns:processSync"/>

<output message="tns:processSyncResponse"/>

</operation>

<operation name="send">

<input message="tns:send"/>

<output message="tns:sendResponse"/>

</operation>

</portType>

<binding type="tns:doctaservicePort" name="doctaservicePort">

<soap:binding style="document" transport="http://schemas.xmlsoap.org/soap/http"/>

<operation name="processSync">

<soap:operation style="document" soapAction=""/>

<input>

<soap:body use="literal"/>

</input>

<output>

<soap:body use="literal"/>

</output>

</operation>

<operation name="send">

<soap:operation style="document" soapAction=""/>

<input>

<soap:body use="literal"/>

</input>

<output>

<soap:body use="literal"/>

</output>

</operation>

</binding>

<service name="doctaservice">

<port name="doctaservicePort" binding="tns:doctaservicePort">

<soap:address location="<Verizon_Service_URL>"/>

</port>

</service>

</definitions>

#### Callback Service WSDL

<?xml version="1.0" encoding="UTF-8"?>

<definitions xmlns:tns="java:com.verizon.webservices.adapter.clecclient" xmlns:wsr="http://www.openuri.org/2002/10/soap/reliability/" xmlns:mime="http://schemas.xmlsoap.org/wsdl/mime/" xmlns:soap12="http://schemas.xmlsoap.org/wsdl/soap12/" xmlns:http="http://schemas.xmlsoap.org/wsdl/http/" xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/" xmlns:soap12enc="http://www.w3.org/2003/05/soap-encoding" xmlns:conv="http://www.openuri.org/2002/04/wsdl/conversation/" xmlns:soap="http://schemas.xmlsoap.org/wsdl/soap/" xmlns:s="http://www.w3.org/2001/XMLSchema" xmlns="http://schemas.xmlsoap.org/wsdl/" targetNamespace="java:com.verizon.webservices.adapter.clecclient">

<types>

<xsd:schema xmlns:xsd="http://www.w3.org/2001/XMLSchema" xmlns:stns="java:com.verizon.webservices.adapter.clecclient" elementFormDefault="qualified" attributeFormDefault="qualified" targetNamespace="java:com.verizon.webservices.adapter.clecclient">

<xsd:element type="xsd:string" name="receive" nillable="true"/>

</xsd:schema>

</types>

<message name="receive">

<part xmlns:partns="java:com.verizon.webservices.adapter.clecclient" name="string" element="partns:receive"/>

</message>

<message name="receiveResponse"/>

<portType name="taservicePort">

<operation name="receive">

<input message="tns:receive"/>

<output message="tns:receiveResponse"/>

</operation>

</portType>

<binding type="tns:taservicePort" name="taservicePort">

<soap:binding style="document" transport="http://schemas.xmlsoap.org/soap/http"/>

<operation name="receive">

<soap:operation style="document" soapAction=""/>

<input>

<soap:body namespace="java:com.verizon.webservices.adapter.clecclient" use="literal"/>

</input>

<output>

<soap:body namespace="java:com.verizon.webservices.adapter.clecclient" use="literal"/>

</output>

</operation>

</binding>

<service name="taservice">

<port name="taservicePort" binding="tns:taservicePort">

<soap:address location="<Service_Customer_Callback_URL>"/>

</port>

</service>

</definitions>

#### Notification Service WSDL

<?xml version="1.0" encoding="UTF-8"?>

<definitions xmlns:tns="java:com.verizon.webservices.adapter.notifyclient" xmlns:wsr="http://www.openuri.org/2002/10/soap/reliability/" xmlns:mime="http://schemas.xmlsoap.org/wsdl/mime/" xmlns:soap12="http://schemas.xmlsoap.org/wsdl/soap12/" xmlns:http="http://schemas.xmlsoap.org/wsdl/http/" xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/" xmlns:soap12enc="http://www.w3.org/2003/05/soap-encoding" xmlns:conv="http://www.openuri.org/2002/04/wsdl/conversation/" xmlns:soap="http://schemas.xmlsoap.org/wsdl/soap/" xmlns:s="http://www.w3.org/2001/XMLSchema" xmlns="http://schemas.xmlsoap.org/wsdl/" targetNamespace="java:com.verizon.webservices.adapter.notifyclient">

<types>

<xsd:schema xmlns:xsd="http://www.w3.org/2001/XMLSchema" xmlns:stns="java:com.verizon.webservices.adapter.notifyclient" elementFormDefault="qualified" attributeFormDefault="qualified" targetNamespace="java:com.verizon.webservices.adapter.notifyclient">

<xsd:element type="xsd:string" name="notify" nillable="true"/>

</xsd:schema>

</types>

<message name="notify">

<part xmlns:partns="java:com.verizon.webservices.adapter.notifyclient" name="string" element="partns:notify"/>

</message>

<message name="notifyResponse"/>

<portType name="ntaservicePort">

<operation name="notify">

<input message="tns:notify"/>

<output message="tns:notifyResponse"/>

</operation>

</portType>

<binding type="tns:ntaservicePort" name="ntaservicePort">

<soap:binding style="document" transport="http://schemas.xmlsoap.org/soap/http"/>

<operation name="notify">

<soap:operation style="document" soapAction=""/>

<input>

<soap:body namespace="java:com.verizon.webservices.adapter.notifyclient" use="literal"/>

</input>

<output>

<soap:body namespace="java:com.verizon.webservices.adapter.notifyclient" use="literal"/>

</output>

</operation>

</binding>

<service name="ntaservice">

<port name="ntaservicePort" binding="tns:ntaservicePort">

<soap:address location="<Service_Customer_Notification_URL>"/>

</port>

</service>

</definitions>

### RPC Style

#### Synchronous Request/Response and Asynchronous Request Services WSDL

<?xml version="1.0" encoding="UTF-8"?>

<definitions xmlns:tns="java:com.verizon.webservices.adapter.proxy" xmlns:wsr="http://www.openuri.org/2002/10/soap/reliability/" xmlns:mime="http://schemas.xmlsoap.org/wsdl/mime/" xmlns:soap12="http://schemas.xmlsoap.org/wsdl/soap12/" xmlns:http="http://schemas.xmlsoap.org/wsdl/http/" xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/" xmlns:soap12enc="http://www.w3.org/2003/05/soap-encoding" xmlns:conv="http://www.openuri.org/2002/04/wsdl/conversation/" xmlns:soap="http://schemas.xmlsoap.org/wsdl/soap/" xmlns:s="http://www.w3.org/2001/XMLSchema" xmlns="http://schemas.xmlsoap.org/wsdl/" targetNamespace="java:com.verizon.webservices.adapter.proxy">

<message name="processSync">

<part xmlns:partns="http://www.w3.org/2001/XMLSchema" type="partns:string" name="string"/>

</message>

<message name="processSyncResponse">

<part xmlns:partns="http://www.w3.org/2001/XMLSchema" type="partns:string" name="result"/>

</message>

<message name="send">

<part xmlns:partns="http://www.w3.org/2001/XMLSchema" type="partns:string" name="string"/>

</message>

<message name="sendResponse"/>

<portType name="rpctaservicePort">

<operation name="processSync">

<input message="tns:processSync"/>

<output message="tns:processSyncResponse"/>

</operation>

<operation name="send">

<input message="tns:send"/>

<output message="tns:sendResponse"/>

</operation>

</portType>

<binding type="tns:rpctaservicePort" name="rpctaservicePort">

<soap:binding style="rpc" transport="http://schemas.xmlsoap.org/soap/http"/>

<operation name="processSync">

<soap:operation style="rpc" soapAction=""/>

<input>

<soap:body namespace="java:com.verizon.webservices.adapter.proxy" encodingStyle="http://schemas.xmlsoap.org/soap/encoding/" use="encoded"/>

</input>

<output>

<soap:body namespace="java:com.verizon.webservices.adapter.proxy" encodingStyle="http://schemas.xmlsoap.org/soap/encoding/" use="encoded"/>

</output>

</operation>

<operation name="send">

<soap:operation style="rpc" soapAction=""/>

<input>

<soap:body namespace="java:com.verizon.webservices.adapter.proxy" encodingStyle="http://schemas.xmlsoap.org/soap/encoding/" use="encoded"/>

</input>

<output>

<soap:body namespace="java:com.verizon.webservices.adapter.proxy" encodingStyle="http://schemas.xmlsoap.org/soap/encoding/" use="encoded"/>

</output>

</operation>

</binding>

<service name="rpctaservice">

<port name="rpctaservicePort" binding="tns:rpctaservicePort">

<soap:address location="<Verizon_Service_URL>"/>

</port>

</service>

</definitions>

#### Callback Service WSDL

<?xml version="1.0" encoding="UTF-8"?>

<definitions xmlns:tns="java:com.verizon.webservices.adapter.clecclient" xmlns:wsr="http://www.openuri.org/2002/10/soap/reliability/" xmlns:mime="http://schemas.xmlsoap.org/wsdl/mime/" xmlns:soap12="http://schemas.xmlsoap.org/wsdl/soap12/" xmlns:http="http://schemas.xmlsoap.org/wsdl/http/" xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/" xmlns:soap12enc="http://www.w3.org/2003/05/soap-encoding" xmlns:conv="http://www.openuri.org/2002/04/wsdl/conversation/" xmlns:soap="http://schemas.xmlsoap.org/wsdl/soap/" xmlns:s="http://www.w3.org/2001/XMLSchema" xmlns="http://schemas.xmlsoap.org/wsdl/" targetNamespace="java:com.verizon.webservices.adapter.clecclient">

<message name="receive">

<part xmlns:partns="http://www.w3.org/2001/XMLSchema" type="partns:string" name="string"/>

</message>

<message name="receiveResponse"/>

<portType name="taservicePort">

<operation name="receive">

<input message="tns:receive"/>

<output message="tns:receiveResponse"/>

</operation>

</portType>

<binding type="tns:taservicePort" name="taservicePort">

<soap:binding style="rpc" transport="http://schemas.xmlsoap.org/soap/http"/>

<operation name="receive">

<soap:operation style="rpc" soapAction=""/>

<input>

<soap:body namespace="java:com.verizon.webservices.adapter.clecclient" encodingStyle="http://schemas.xmlsoap.org/soap/encoding/" use="encoded"/>

</input>

<output>

<soap:body namespace="java:com.verizon.webservices.adapter.clecclient" encodingStyle="http://schemas.xmlsoap.org/soap/encoding/" use="encoded"/>

</output>

</operation>

</binding>

<service name="taservice">

<port name="taservicePort" binding="tns:taservicePort">

<soap:address location="<Service_Customer_Callback_URL>"/>

</port>

</service>

</definitions>

#### Notification Service WSDL

<?xml version="1.0" encoding="UTF-8"?>

<definitions xmlns:tns="java:com.verizon.webservices.adapter.notifyclient" xmlns:wsr="http://www.openuri.org/2002/10/soap/reliability/" xmlns:mime="http://schemas.xmlsoap.org/wsdl/mime/" xmlns:soap12="http://schemas.xmlsoap.org/wsdl/soap12/" xmlns:http="http://schemas.xmlsoap.org/wsdl/http/" xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/" xmlns:soap12enc="http://www.w3.org/2003/05/soap-encoding" xmlns:conv="http://www.openuri.org/2002/04/wsdl/conversation/" xmlns:soap="http://schemas.xmlsoap.org/wsdl/soap/" xmlns:s="http://www.w3.org/2001/XMLSchema" xmlns="http://schemas.xmlsoap.org/wsdl/" targetNamespace="java:com.verizon.webservices.adapter.notifyclient">

<message name="notify">

<part xmlns:partns="http://www.w3.org/2001/XMLSchema" type="partns:string" name="string"/>

</message>

<message name="notifyResponse"/>

<portType name="ntaservicePort">

<operation name="notify">

<input message="tns:notify"/>

<output message="tns:notifyResponse"/>

</operation>

</portType>

<binding type="tns:ntaservicePort" name="ntaservicePort">

<soap:binding style="rpc" transport="http://schemas.xmlsoap.org/soap/http"/>

<operation name="notify">

<soap:operation style="rpc" soapAction=""/>

<input>

<soap:body namespace="java:com.verizon.webservices.adapter.notifyclient" encodingStyle="http://schemas.xmlsoap.org/soap/encoding/" use="encoded"/>

</input>

<output>

<soap:body namespace="java:com.verizon.webservices.adapter.notifyclient" encodingStyle="http://schemas.xmlsoap.org/soap/encoding/" use="encoded"/>

</output>

</operation>

</binding>

<service name="ntaservice">

<port name="ntaservicePort" binding="tns:ntaservicePort">

<soap:address location="<Service_Customer_Notification_URL>"/>

</port>

</service>

</definitions>

## Operation Names of TAXI WSDLs

The following table lists the operation names of TA Web Service WSDL files for the corresponding TA services.

| TA Service Name | XML Message Delivery Category | Type of Services Offered | XML Message Type | XML Message Orientation | Operation Name in WSDL File | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| Service Test (POTS only) | Asynchronous send | Local | Request | Service customer to Verizon | send |  |
| Service Test (POTS only) | Asynchronous callback | Local | Response | Verizon to service customer | receive |  |
| Trouble Report Create | Synchronous send | Local, Access, Retail | Request | Service customer to Verizon | processSync |  |
| Trouble Report Create | Synchronous receive | Local, Access, Retail | Response | Verizon to service customer | processSync | There is a two minutes (120 seconds) time out from Verizon side. If a customer is unable to receive Verizon’s response after two minutes, Verizon TAXI Web Service will time out. |
| Trouble Report Modification | Synchronous send | Local, Access, Retail | Request | Service customer to Verizon | processSync |  |
| Trouble Report Modification | Synchronous receive | Local, Access, Retail | Response | Verizon to service customer | processSync | There is a two minutes (120 seconds) time out from Verizon side. If a customer is unable to receive Verizon’s response after two minutes, Verizon TAXI Web Service will time out. |
| Trouble Report Cancellation | Synchronous send | Local, Access, Retail | Request | Service customer to Verizon | processSync |  |
| Trouble Report Cancellation | Synchronous receive | Local, Access, Retail | Response | Verizon to service customer | processSync | There is a two minutes (120 seconds) time out from Verizon side. If a customer is unable to receive Verizon’s response after two minutes, Verizon TAXI Web Service will time out. |
| Trouble Report Close Out Verification | Synchronous send | Local, Access, Retail | Request | Service customer to Verizon | processSync |  |
| Trouble Report Close Out Verification | Synchronous receive | Local, Access, Retail | Response | Verizon to service customer | processSync | There is a two minutes (120 seconds) time out from Verizon side. If a customer is unable to receive Verizon’s response after two minutes, Verizon TAXI Web Service will time out. |
| Retrieve Trouble Report Attributes | Synchronous send | Local, Access, Retail | Request | Service customer to Verizon | processSync |  |
| Retrieve Trouble Report Attributes | Synchronous receive | Local, Access, Retail | Response | Verizon to service customer | processSync | There is a two minutes (120 seconds) time out from Verizon side. If a customer is unable to receive Verizon’s response after two minutes, Verizon TAXI Web Service will time out. |
| Trouble Report AVC Event Notification | Unsolicited send | Local, Access, Retail | Notification | Verizon to service customer | notify |  |
| Trouble Report Close Out Event Notification | Unsolicited send | Local, Access, Retail | Notification | Verizon to service customer | notify |  |
| Multiple Trouble Report Create | Asynchronous send | Local | Request | Service customer to Verizon | send |  |
| Multiple Trouble Report Create | Asynchronous callback | Local | Response | Verizon to service customer | receive |  |
| Quick Test | Asynchronous send | Access | Request | Service customer to Verizon | send | . |
| Quick Test | Asynchronous callback | Access | Response | Verizon to service customer | receive |  |
| Performance Monitoring | Asynchronous send | Access | Request | Service customer to Verizon | send |  |
| Performance Monitoring | Asynchronous callback | Access | Response | Verizon to service customer | receive |  |
| Set Loopback | Asynchronous send | Access | Request | Service customer to Verizon | send |  |
| Set Loopback | Asynchronous callback | Access | Response | Verizon to service customer | receive |  |
| Release Loopback | Asynchronous send | Access | Request | Service customer to Verizon | send |  |
| Release Loopback | Asynchronous callback | Access | Response | Verizon to service customer | receive |  |
| Retrieve Local Contact by Trouble Report Id | Synchronous send | Local | Request | Service customer to Verizon | processSync | There is a two minutes (120 seconds) time out from Verizon side. If a customer is unable to receive Verizon’s response after two minutes, Verizon TAXI Web Service will time out. |
| Retrieve Local Contact by Trouble Report Id | Synchronous receive | Local | Response | Verizon to service customer | processSync |  |
| Retrieve Technician Notes by Trouble Report Id | Synchronous send | Access | Request | Service customer to Verizon | processSync | There is a two minutes (120 seconds) time out from Verizon side. If a customer is unable to receive Verizon’s response after two minutes, Verizon TAXI Web Service will time out. |
| Retrieve Technician Notes by Trouble Report Id | Synchronous receive | Access | Response | Verizon to service customer | processSync |  |

## Exception Handling

Message flows from IEC/CLEC to Verizon firewall system, and then to TAXI platform for the TA service provider to process. Failures in the authentication, authorization, and routing in Verizon firewall system side will be handled by the Verizon firewall system, the details of error/fault messages will be documented separately.

Failures in TAXI platform, including invoking business services, translating SOAP/tML, etc, will result into a standard SOAP fault message. Sample fault message will be given in the next section.

Errors in business services processing, such as data validation, OSS system integration, etc, will result a tML error message. The tML error message is documented in the tML schemas. The tML error message, or partial failure error message will be returned to the IEC/CLEC as the normal SOAP response message.

# SOAP Structure for TAXI

SOAP request header will provide standard information about routing information, message security, etc. It will be reserved for Web Service integration. SOAP request body will have tML Request. SOAP Response body will have tML response or fault message.

SOAP Response will have the same information as the request Header, except different timestamp. SOAP response body will echo back tML request, and application specific request data, and also have tML response, application specific response data.

We will use XML Namespace to avoid name conflicts between tML definitions and application specific definitions.

## Synchronized Request/Response

### Sample SOAP Request

<?xml version='1.0' encoding='UTF-8'?>

<env:Envelope xmlns:env="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:xsi=http://www.w3.org/2001/XMLSchema-instance

xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/"

xmlns:xsd="http://www.w3.org/2001/XMLSchema">

<env:Body env:encodingStyle="http://schemas.xmlsoap.org/soap/encoding/">

<m:processSync xmlns:m="java:com.verizon.webservices.adapter.proxy">

<string xsi:type="xsd:string">

tML request goes here!!!

</string>

</m: processSync >

</env:Body>

</env:Envelope>

### Sample SOAP Response

<?xml version='1.0' encoding='UTF-8'?>

<env:Envelope xmlns:env="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:xsi=http://www.w3.org/2001/XMLSchema-instance

xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/"

xmlns:xsd="http://www.w3.org/2001/XMLSchema">

<env:Body env:encodingStyle="http://schemas.xmlsoap.org/soap/encoding/">

<m: processSyncResponse xmlns:m="java:com.verizon.webservices.adapter.proxy">

<m:return xsi:type=”xsd:string”>

tML response goes here!!

</ return >

</m: processSyncResponse>

</env:Body>

</env:Envelope>

### Sample SOAP fault message

<?xml version='1.0' encoding='UTF-8'?>

<SOAP-ENV:Envelope

xmlns:SOAP-ENV="http://schemas.xmlsoap.org/soap/envelope/">

<SOAP-ENV:Body>

<SOAP-ENV:Fault>

<faultcode>SOAP-ENV:Server</faultcode>

<faultstring>Server Error</faultstring>

<detail>

<e:tafaultdetails xmlns:e="http://ta.verizon.com/taservices" >

<message>transformation error</message>

<errorcode>1001</errorcode>

</e:tafaultdetails>

</detail>

</SOAP-ENV:Fault>

</SOAP-ENV:Body>

</SOAP-ENV:Envelope>

## One-way Send Only

### Sample SOAP Request

<?xml version='1.0' encoding='UTF-8'?>

<env:Envelope xmlns:env="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:xsi=http://www.w3.org/2001/XMLSchema-instance

xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/"

xmlns:xsd="http://www.w3.org/2001/XMLSchema">

<env:Body env:encodingStyle="http://schemas.xmlsoap.org/soap/encoding/">

<m:send xmlns:m="java:com.verizon.webservices.adapter.proxy">

<string xsi:type="xsd:string">

tML request goes here!!!

</string>

</m:send>

</env:Body>

</env:Envelope>

### Sample SOAP Response

<?xml version='1.0' encoding='UTF-8'?>

<env:Envelope xmlns:env="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:xsi=http://www.w3.org/2001/XMLSchema-instance

xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/"

xmlns:xsd="http://www.w3.org/2001/XMLSchema">

<env:Body env:encodingStyle="http://schemas.xmlsoap.org/soap/encoding/">

<m: sendResponse xmlns:m="java:com.verizon.webservices.adapter.proxy">

// no response data here

</m: sendResponse>

</env:Body>

</env:Envelope>

### Sample SOAP fault message

<SOAP-ENV:Envelope

xmlns:SOAP-ENV="http://schemas.xmlsoap.org/soap/envelope/">

<SOAP-ENV:Body>

<SOAP-ENV:Fault>

<faultcode>SOAP-ENV:Server</faultcode>

<faultstring>Server Error</faultstring>

<detail>

<e:tafaultdetails xmlns:e="http://ta.verizon.com/taservices" >

<message>transformation error</message>

<errorcode>1001</errorcode>

</e:tafaultdetails>

</detail>

</SOAP-ENV:Fault>

</SOAP-ENV:Body>

</SOAP-ENV:Envelope>

## Callback Service

### Sample SOAP Request

<?xml version='1.0' encoding='UTF-8'?>

<env:Envelope xmlns:env="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:xsi=http://www.w3.org/2001/XMLSchema-instance

xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/"

xmlns:xsd="http://www.w3.org/2001/XMLSchema">

<env:Body env:encodingStyle="http://schemas.xmlsoap.org/soap/encoding/">

<m: receive xmlns:m=" java:com.verizon.webservices.adapter.clecclient ">

<string xsi:type="xsd:string">

tML response goes here!!!

</string>

</m:send>

</env:Body>

</env:Envelope>

### Sample SOAP Response

<?xml version='1.0' encoding='UTF-8'?>

<env:Envelope xmlns:env="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:xsi=http://www.w3.org/2001/XMLSchema-instance

xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/"

xmlns:xsd="http://www.w3.org/2001/XMLSchema">

<env:Body env:encodingStyle="http://schemas.xmlsoap.org/soap/encoding/">

<m: receiveResponse xmlns:m="java:com.verizon.webservices.adapter.clecclient">

// no response data from callback

</m: receiveResponse>

</env:Body>

</env:Envelope>

### Sample SOAP fault message

<SOAP-ENV:Envelope

xmlns:SOAP-ENV="http://schemas.xmlsoap.org/soap/envelope/">

<SOAP-ENV:Body>

<SOAP-ENV:Fault>

<faultcode>SOAP-ENV:Server</faultcode>

<faultstring>Server Error</faultstring>

<detail>

<e:tafaultdetails xmlns:e="http://ta.verizon.com/taservices" >

<message>transformation error</message>

<errorcode>1001</errorcode>

</e:tafaultdetails>

</detail>

</SOAP-ENV:Fault>

</SOAP-ENV:Body>

</SOAP-ENV:Envelope>

## Notification  Service

### Sample SOAP Request

<?xml version='1.0' encoding='UTF-8'?>

<env:Envelope xmlns:env="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:xsi=http://www.w3.org/2001/XMLSchema-instance

xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/"

xmlns:xsd="http://www.w3.org/2001/XMLSchema">

<env:Body env:encodingStyle="http://schemas.xmlsoap.org/soap/encoding/">

<m: notify xmlns:m=" java:com.verizon.webservices.adapter.clecclient ">

tML response goes here!!!

</m: notify >

</env:Body>

</env:Envelope>

### Sample SOAP Response

<?xml version='1.0' encoding='UTF-8'?>

<env:Envelope xmlns:env="http://schemas.xmlsoap.org/soap/envelope/"

xmlns:xsi=http://www.w3.org/2001/XMLSchema-instance

xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/"

xmlns:xsd="http://www.w3.org/2001/XMLSchema">

<env:Body env:encodingStyle="http://schemas.xmlsoap.org/soap/encoding/">

<m: notifyResponse xmlns:m="java:com.verizon.webservices.adapter.clecclient">

// no response data from callback

</m: notifyResponse>

</env:Body>

</env:Envelope>

### Sample SOAP fault message

<SOAP-ENV:Envelope

xmlns:SOAP-ENV="http://schemas.xmlsoap.org/soap/envelope/">

<SOAP-ENV:Body>

<SOAP-ENV:Fault>

<faultcode>SOAP-ENV:Server</faultcode>

<faultstring>Server Error</faultstring>

<detail>

<e:tafaultdetails xmlns:e="http://ta.verizon.com/taservices" >

<message>transformation error</message>

<errorcode>1001</errorcode>

</e:tafaultdetails>

</detail>

</SOAP-ENV:Fault>

</SOAP-ENV:Body>

</SOAP-ENV:Envelope

## Sample Soap Message

Following soap message are provided to give reader an approximate sense of actual soap messages.   Actual soap message might be different depending on choice made during implementation of webservice clients.

A webservice request might look like the following. POST /TA-Access-st/taservice/docstyleserviceuri HTTP/1.0 Host: swholesalegwit.verizon.com:80 Connection: Keep-Alive Content-Length: 3033 Content-Type: text/xml SOAPAction: "" <env:Envelope xmlns:env="http://schemas.xmlsoap.org/soap/envelope/" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/" xmlns:xsd="http://www.w3.org/2001/XMLSchema"><env:Body><n1:processSync xmlns:n1="java:com.verizon.webservices.adapter.proxy">&lt;?xml version="1.0" encoding="UTF-8" standalone="yes"?&gt;&lt;RetrieveAttributesByTroubleReportIdRequest xmlns="http://www.ansi.org/tML/TA/tML-TA" xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA tML-TA.xsdhttp://www.ansi.org/tML/TA/tML-TABase tML-TABase.xsd" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase" xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA" xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase" xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"&gt; &lt;RequestId&gt;124734&lt;/RequestId&gt; &lt;Customer&gt; &lt;tML-TABase:UserId&gt;WSAMCIX03&lt;/tML-TABase:UserId&gt; &lt;tML-TABase:ServiceProfile&gt;Carrier&lt;/tML-TABase:ServiceProfile&gt; &lt;/Customer&gt; &lt;TargetObjectName&gt; &lt;tML-TABase:DistinguishedName&gt; &lt;tML-TABase:RDNSequenceItem&gt; &lt;tML-TABase:Type&gt;networkID&lt;/tML-TABase:Type&gt; &lt;tML-TABase:Assertion&gt;VZC&lt;/tML-TABase:Assertion&gt; &lt;/tML-TABase:RDNSequenceItem&gt; &lt;tML-TABase:RDNSequenceItem&gt; &lt;tML-TABase:Type&gt;accountName&lt;/tML-TABase:Type&gt; &lt;tML-TABase:Assertion&gt;MCI&lt;/tML-TABase:Assertion&gt; &lt;/tML-TABase:RDNSequenceItem&gt; &lt;tML-TABase:RDNSequenceItem&gt; &lt;tML-TABase:Type&gt;troubleReportID&lt;/tML-TABase:Type&gt; &lt;tML-TABase:Assertion&gt;WNYTR019189&lt;/tML-TABase:Assertion&gt; &lt;/tML-TABase:RDNSequenceItem&gt; &lt;/tML-TABase:DistinguishedName&gt; &lt;/TargetObjectName&gt; &lt;TroubleReportId&gt;WNYTR019189&lt;/TroubleReportId&gt; &lt;RetrieveAttributes&gt; &lt;tML-TABase:AgentContactPerson&gt;true&lt;/tML-TABase:AgentContactPerson&gt; &lt;tML-TABase:AuthorizationList&gt;true&lt;/tML-TABase:AuthorizationList&gt; &lt;tML-TABase:CancelRequestedByManager&gt;true&lt;/tML-TABase:CancelRequestedByManager&gt; &lt;tML-TABase:CommitmentTime&gt;true&lt;/tML-TABase:CommitmentTime&gt; &lt;tML-TABase:EscalationList&gt;true&lt;/tML-TABase:EscalationList&gt; &lt;tML-TABase:MaintServiceCharge&gt;true&lt;/tML-TABase:MaintServiceCharge&gt; &lt;tML-TABase:TroubleReportState&gt;true&lt;/tML-TABase:TroubleReportState&gt; &lt;tML-TABase:TroubleReportStatus&gt;true&lt;/tML-TABase:TroubleReportStatus&gt; &lt;tML-TABase:TroubleReportStatusTime&gt;true&lt;/tML-TABase:TroubleReportStatusTime&gt; &lt;/RetrieveAttributes&gt;&lt;/RetrieveAttributesByTroubleReportIdRequest&gt;</n1:processSync></env:Body></env:Envelope>

A webservice response might look like the following. StatusCode : 200 Headers : CONNECTION = keep-alive CONTENT-LENGTH = 1754 CONTENT-TYPE = text/xml P3P = CP="NON CUR OTPi OUR NOR UNI" SET-COOKIE = PD-S-SESSION-ID=2_bzucXJfYUPJo2yVqQjNNrcYJgDKQk4etMnA9SxQxR0Illa5t; Path=/; Secure DATE = Thu, 18 Jun 2009 164232 GMT <env:Envelope xmlns:env="http://schemas.xmlsoap.org/soap/envelope/" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xmlns:soapenc="http://schemas.xmlsoap.org/soap/encoding/" xmlns:xsd="http://www.w3.org/2001/XMLSchema"><env:Body><n1:processSyncResponse xmlns:n1="java:com.verizon.webservices.adapter.proxy">&lt;?xml version="1.0" encoding="UTF-8"?&gt; &lt;RetrieveAttributesByTroubleReportIdResponse xmlns="http://www.ansi.org/tML/TA/tML-TA" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase" xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA tML-TA.xsd"&gt; &lt;RequestId&gt;124734&lt;/RequestId&gt; &lt;TargetObjectName&gt; &lt;tML-TABase:DistinguishedName&gt;&lt;tML-TABase:RDNSequenceItem&gt;&lt;tML-TABase:Type&gt;networkID&lt;/tML-TABase:Type&gt;&lt;tML-TABase:Assertion&gt;VZC&lt;/tML-TABase:Assertion&gt;&lt;/tML-TABase:RDNSequenceItem&gt;&lt;tML-TABase:RDNSequenceItem&gt;&lt;tML-TABase:Type&gt;accountName&lt;/tML-TABase:Type&gt;&lt;tML-TABase:Assertion&gt;MCI&lt;/tML-TABase:Assertion&gt;&lt;/tML-TABase:RDNSequenceItem&gt;&lt;tML-TABase:RDNSequenceItem&gt;&lt;tML-TABase:Type&gt;troubleReportID&lt;/tML-TABase:Type&gt;&lt;tML-TABase:Assertion&gt;WNYTR019189&lt;/tML-TABase:Assertion&gt;&lt;/tML-TABase:RDNSequenceItem&gt;&lt;/tML-TABase:DistinguishedName&gt; &lt;/TargetObjectName&gt; &lt;Exception&gt; &lt;tML-TABase:NotFound&gt; &lt;tML-TABase:ExceptionList&gt; &lt;tML-TABase:Tag&gt;0008&lt;/tML-TABase:Tag&gt; &lt;tML-TABase:Value&gt;Ticket does not exist.&lt;/tML-TABase:Value&gt; &lt;/tML-TABase:ExceptionList&gt; &lt;/tML-TABase:NotFound&gt; &lt;/Exception&gt; &lt;/RetrieveAttributesByTroubleReportIdResponse&gt; </n1:processSyncResponse></env:Body></env:Envelope>

# tML Specification

## POTS Service Test

This transaction is available only to Local customers

Table 2.  POTS Service Test Request

| tML POTS Service Test Request |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | POTSUncontrolledTestRequest | 36 Max. | AN | Req | 1,1 |  | Test request correlation id |
| UserId | Customer | POTSUncontrolledTestRequest | 10 | AN | Req | 1,1 |  | Refer to §7.3 for detailed informational. |
| ServiceProfile | Customer | POTSUncontrolledTestRequest | 8 Max. | AN | Req | 1,1 |  | Valid Values are: CLEC, RESELLER. |
| TestRequest | TestRequest | POTSUncontrolledTestRequest | 1 | N | Req | 1,1 |  | Valid values are 1,2,3, and 4. 1 is for FULL, 2 is for QUICK, 3 is for CENTRAL OFFIC, and 4 is for LOOP. |
| Type | RDNSequenceItem | POTSUncontrolledTestRequest.ManagedObjectInstance. DistingushedName |  | AN | Req | 1,1 |  | Hard code to networkID |
| Assertion | RDNSequenceItem | POTSUncontrolledTestRequest.ManagedObjectInstance. DistingushedName | 5 | AN | Req | 1,1 |  | Assertion::= State value followed by SP Network ID Value. SP Network ID Value is either VZL or VZC. VZL for a local customer (CLEC, RESELLER) For example, a local customer would send an Assertion tag with the value NYVZL if the reported circuit id’s customer end is located in New York state. |
| Type | RDNSequenceItem | POTSUncontrolledTestRequest.ManagedObjectInstance. DistingushedName |  | AN | Req | 1,1 |  | Hard code it to accountName |
| Assertion | RDNSequenceItem | POTSUncontrolledTestRequest.ManagedObjectInstance. DistingushedName | 4 | AN | Req | 1,1 |  | Service Consumer account Name. ECC for local |
| Type | RDNSequenceItem | POTSUncontrolledTestRequest.ManagedObjectInstance. DistingushedName |  | AN | Req | 1,1 |  | Hardcode it to serviceID |
| Assertion | RDNSequenceItem | POTSUncontrolledTestRequest.ManagedObjectInstance. DistingushedName | 10 | N | Req | 1,1 |  | POTS TN |

Table 3.  POTS Service Test Response – Normal

| tML POTS Service Test Response |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | POTSUncontrolledTestResponse | 36 Max | AN | Req | 1,1 |  | Test request correlation id |
| Type | RNDSequenceItem | POTSUncontrolledTestResponse.ManagedObjectInstance. DistingushedName |  | AN | Req | 1,1 |  | Hard code it to networkID |
| Assertion | RNDSequenceItem | POTSUncontrolledTestResponse.ManagedObjectInstance. DistingushedName | 5 | AN | Req | 1,1 |  | networkID sent in the request will be echoed back. |
| Type | RNDSequenceItem | POTSUncontrolledTestResponse.ManagedObjectInstance. DistingushedName |  | AN | Req | 1,1 |  | Hardcode it to account Name |
| Assertion | RNDSequenceItem | POTSUncontrolledTestResponse.ManagedObjectInstance. DistingushedName | 4 | AN | Req | 1,1 |  | account Name sent in the request will be echoed back. |
| Type | RNDSequenceItem | POTSUncontrolledTestResponse.ManagedObjectInstance. DistingushedName |  | AN | Req | 1,1 |  | serviceID |
| Assertion | RNDSequenceItem | POTSUncontrolledTestResponse.ManagedObjectInstance. DistingushedName | 10 | N | Req | 1,1 |  | POTS TN sent in the request will be echoed back. |
| AdditionalText | AdditionalText | POTSUncontrolledTestResponse. PotsTestResponse | * | AN | Opt | 0,1 |  | AdditionalText is an optional field. When it is present, AdditionalText may contain data for FEP, Test Result Code (commonly referred as VER code), and/or, Short Repair Recommendation, Long Repair Recommendation, and TroubleCode. The exact syntax is the following: <tML-ServiceTestBase:AdditionalText>FEP::=…~~TestResultCode::=…~~ShortRepairRecommendation::=…LongRepairRecommendation::=…~~TroubleCode::=… </tML-ServiceTestBase:AdditionalText> Where … are the data for corresponding fields, and FEP::=; TestResultCode::=; ShortRepairRecommendation::=; LongRepairRecommendation::=; TroubleCode::=; ~~ will each serve as field delimiters. The above mentioned five fields within an AdditionalText may or may not appear together for a given response. |
| Summary | Normal | POTSUncontrolledTestResponse. PotsTestResponse | * | AN | Req | 1,1 |  |  |
| TipToRingResistance | DcSignature | POTSUncontrolledTestResponse. PotsTestResponse.Normal.Results | 8 Max | N | Opt | 0,1 |  | In Kohms |
| TipToGroundResistance | DcSignature | POTSUncontrolledTestResponse. PotsTestResponse.Normal.Results | 8 Max | N | Opt | 0,1 |  | In Kohms |
| TipToGroundVolts | DcSignature | POTSUncontrolledTestResponse. PotsTestResponse. Normal.Results | 4 Max | N | Opt | 0,1 |  | In Volts |
| RingToGroundResistance | DcSignature | POTSUncontrolledTestResponse.Normal.Results | 8 Max | N | Opt | 0,1 |  | In Kohms |
| RingToGroundVolts | DcSignature | POTSUncontrolledTestResponse. PotsTestResponse. Normal.Results | 4 Max | N | Opt | 0,1 |  | In Volts |
| TipToRingResistance | AcSignature | POTSUncontrolledTestResponse. PotsTestResponse.Normal.Results | 8 Max | N | Opt | 0,1 |  | In Kohms |
| TipToGroundResistance | AcSignature | POTSUncontrolledTestResponse. PotsTestResponse.Normal.Results | 8 Max | N | Opt | 0,1 |  | In Kohms |
| RingToGroundResistance | AcSignature | POTSUncontrolledTestResponse. PotsTestResponse.Normal.Results | 8 Max | N | Opt | 0,1 |  | In Kohms |
| Ringers | AcSignature | POTSUncontrolledTestResponse. PotsTestResponse.Normal.Results | 4 Max | N | Opt | 0,1 |  | It will be always ZERO. |
| LineCircuitStatus | CentralOffice | POTSUncontrolledTestResponse. PotsTestResponse.Normal.Results | 3 Max | AN | Opt | 0,1 |  |  |
| DialToneStatus | CentralOffice | POTSUncontrolledTestResponse. PotsTestResponse.Normal.Results | 3 Max | AN | Opt | 0,1 |  |  |
| Capacitive | Balance | POTSUncontrolledTestResponse. PotsTestResponse.Normal.Results | 3 Max | N | Opt | 0,1 |  | Capacitive balance in percentage. |
| Longitudinal | Balance | POTSUncontrolledTestResponse. PotsTestResponse.Normal.Results | 7 Max | N | Opt | 0,1 |  | Long Balance in DB. |
| TotalLoop | Loop | POTSUncontrolledTestResponse. PotsTestResponse.Normal.Results | * | N | Opt | 0,1 |  | For Loop aggregate, only one value will be present at given time. If DELPHI returns both TotalLoop and OpenDistanceFromCentralOffice, then only TotalLoop will be sent back as response. In FT. |
| OpenDistanceFromCentralOffice | Loop | POTSUncontrolledTestResponse. PotsTestResponse.Normal.Results | * | N | Opt | 0,1 |  | For Loop aggregate, only one value will be present at given time. If DELPHI returns both TotalLoop and OpenDistanceFromCentralOffice, then only TotalLoop will be sent back as response. In FT. |

Table 4.  POTS Service Test Response – Exception

| tML POTS Service Test Response (Exception) |
| --- |
| Tag | Agggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | POTSUncontrolledTestResponse | 36 Max | AN | Req | 1,1 |  | Test request correlation id |
| Type | RNDSequenceItem | POTSUncontrolledTestResponse.ManagedObjectInstance. DistingushedName |  | AN | Req | 1,1 |  | Hard code it to networkID |
| Assertion | RNDSequenceItem | POTSUncontrolledTestResponse.ManagedObjectInstance. DistingushedName | 5 | AN | Req | 1,1 |  | networkID sent in the request will be echoed back. |
| Type | RNDSequenceItem | POTSUncontrolledTestResponse.ManagedObjectInstance. DistingushedName |  | AN | Req | 1,1 |  | Hardcode it to account Name |
| Assertion | RNDSequenceItem | POTSUncontrolledTestResponse.ManagedObjectInstance. DistingushedName | 4 | AN | Req | 1,1 |  | account Name sent in the request will be echoed back. |
| Type | RNDSequenceItem | POTSUncontrolledTestResponse.ManagedObjectInstance. DistingushedName |  | AN | Req | 1,1 |  | serviceID |
| Assertion | RNDSequenceItem | POTSUncontrolledTestResponse.ManagedObjectInstance. DistingushedName | 10 | N | Req | 1,1 |  | POTS TN sent in the request will be echoed back. |
| Tag Value | ExceptionList | POTSUncontrolledTestResponse. PotsTestResponse.Exception.AccessDenied |  | AN | Opt | 0,1 |  | If this exception occurs, no other exception will appear. Tag=0001 Value=<error message> |
| Tag Value | ExceptionList | POTSUncontrolledTestResponse.PotsTestResponse.Exception. InvalidDataReceived |  | AN | Opt | 0,1 |  | If this exception occurs, no other exception will appear. Tag=0002 Value=<error message> |
| Tag Value | ExceptionList | POTSUncontrolledTestResponse. PotsTestResponse.Exception. ProcessingFailure |  | AN | Opt | 0,1 |  | If this exception occurs, no other exception will appear. Tag=0003 Value=<error message> |
| Tag Value | ExceptionList | POTSUncontrolledTestResponse. PotsTestResponse.Exception. DuplicatedInvocation |  | AN | Opt | 0,1 |  | If this exception occurs, no other exception will appear. Tag=0004 Value=<error message> |
| Tag Value | ExceptionList | POTSUncontrolledTestResponse. PotsTestResponse.Exception. ResourceLimitation |  | AN | Opt | 0,1 |  | If this exception occurs, no other exception will appear. Tag=0005 Value=<error message> |
| Tag Value | ExceptionList | POTSUncontrolledTestResponse. PotsTestResponse.Exception. NotFound |  | AN | Opt | 0,1 |  | If this exception occurs, no other exception will appear. Tag=0006 Value=<error message> |
| Tag Value | ExceptionList | POTSUncontrolledTestResponse. PotsTestResponse.Exception. MissingData |  | AN | Opt | 0,1 |  | If this exception occurs, no other exception will appear. Tag=0007 Value=<error message> |
| ServiceInUse | Exception | POTSUncontrolledTestResponse. PotsTestResponse. |  | AN | Opt | 0,1 |  | If this exception occurs, no other exception will appear. |
| TroubleRepairInProgress | Exception | POTSUncontrolledTestResponse. PotsTestResponse |  | AN | Opt | 0,1 |  | If this exception occurs, no other exception will appear. |

## Trouble Report Create

Table 5.  Trouble Report Create Request

| tML Trouble Report Create Request |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | RequestTroubleReportCreationRequest | 36 Max. | AN | Req | 1,1 |  | Create request correlation id |
| UserId | Customer | RequestTroubleReportCreationRequest | 10 | AN | Req | 1,1 |  | Refer to §7.3 for detailed informational. |
| ServiceProfile | Customer | RequestTroubleReportCreationRequest | 8 Max | AN | Req | 1,1 | RESELLER CLEC Carrier | “RESELLER” or “CLEC” for Verizon Local Customers “Carrier” for Verizon Access Customers |
| NameBindingId | NameBindingId | RequestTroubleReportCreationRequest | 20 | N | Opt | 0,1 | 1.2.840.10015.0.6.24 1.2.840.10015.0.6.25 1.2.840.10015.0.6.26 1.2.840.10015.0.6.27 | NameBindingId is an optional field. |
| Type | RDNSequenceItem | RequestTroubleReportCreationRequest.ManagedObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | RequestTroubleReportCreationRequest.ManagedObjectInstance. DistinguishedName | 5 | AN | Req | 1,1 | Assertion::= State value followed by SP Network ID Value. SP Network ID Value is either VZL, or VZC VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) | For example, a local customer would send an Assertion tag with the value NYVZL if the reported circuit id’s customer end is located in New York state. |
| Type | RDNSequenceItem | RequestTroubleReportCreationRequest.ManagedObjectInstance. DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | RequestTroubleReportCreationRequest.ManagedObjectInstance. DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | RequestTroubleReportCreationRequest.ManagedObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | serviceID |  |
| Assertion | RDNSequenceItem | RequestTroubleReportCreationRequest.ManagedObjectInstance. DistinguishedName | 64 Max | AN | Req | 1,1 | Service ID Value | Use an appropriate circuit id to populate this field – for definition of circuit ids, refer to Annex B Circuit Format Definition for Designed and Non-Designed Circuits |
|  | TroubleType |  |  |  | Req |  |  |  |
| Number | TroubleType | RequestTroubleReportCreationRequest | 4 Max | N | Req | 1,1 |  |  |
|  | AdditionalTroubleInfoList |  |  |  | Req |  |  |  |
| AdditionalTroubleInfoItem | AdditionalTroubleInfoList | RequestTroubleReportCreationRequest | 256 Max | AN | Req | 1,n |  | If a service test has been performed prior to a customer invoking a Trouble Report Create request for a given circuit and the customer would like Verizon to perform a desired dispatch option, the customer may place a text string with syntax of “TR <XX> <YY>” at the very beginning of the first instance of AdditionalTroubleInfoItem, where the exact contents of <XX> and <YY> are provided in Annex A TR <XX> <YY> Construction Rules |
| TroubleReportFormatId | AdditionalCreateInfo | RequestTroubleReportCreationRequest | 1 | N | Opt | 0,1 |  |  |
|  | AdditionalTroubleInfoList |  |  |  | Req |  |  |  |
| AdditionalTroubleInfoItem | AdditionalTroubleInfoList | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 256 Max | AN | Opt | 0,n |  | AdditionalTroubleInfoList is optional This field is served as overflow field for RequestTroubleReportCreationRequest/AdditionalTroubleInfoList, text in this node will be appended to text in RequestTroubleReportCreationRequest/AdditionalTroubleInfoList |
|  | ALocationAccessAddress |  |  |  | Conditional |  |  | Required for Serial, Telephone, and POT circuits; Optional for Trunk and Message circuits. |
| PremisesName | ALocationAccessAddress | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Conditional/Required | 1.1 |  | Business Name ALocationAccessAddress is an optional field |
| CivicAddress | PremisesAddress | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessAddress | 64 Max | AN | Conditional/Required | 1,1 |  |  |
| City | PremisesAddress | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessAddress | 64 Max | AN | Conditional/Required | 1,1 |  |  |
| State | PremisesAddress | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessAddress | 64 Max | AN | Conditional/Required | 1,1 |  |  |
| Zip | PremisesAddress | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessAddress | 64 Max | N | Conditional/Required | 1,1 |  |  |
|  | ALocationAccessHours |  |  |  | Conditional |  |  | Required for Serial, Telephone, and POT circuits; Optional for Trunk and Message circuits. |
| Sunday | DaysOfWeek | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Conditional/Required | 1,1 | True False | LocationAccessHoursItem can appear multiple times |
| Monday | DaysOfWeek | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Conditional/Required | 1,1 | True False |  |
| Tuesday | DaysOfWeek | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Conditional/Required | 1,1 | True false |  |
| Wednesday | DaysOfWeek | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Conditional/Required | 1,1 | True false |  |
| Thursday | DaysOfWeek | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Conditional/Required | 1,1 | True false |  |
| Friday | DaysOfWeek | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Conditional/Required | 1,1 | True false |  |
| Saturday | DaysOfWeek | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Conditional/Required | 1,1 | True false |  |
| IntervalStart | IntervalsOfDayItem | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem . IntervalsOfDay | 8 | AN | Conditional/Required | 1,n |  | Premises' Local Time Military Format: HH:MM:SS |
| IntervalEnd | IntervalsOfDayItem | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem . IntervalsOfDay | 8 | AN | Conditional/Required | 1,n |  | Premises' Local Time Military Format: HH:MM:SS |
|  | ALocationAccessPerson |  |  |  | Conditional |  |  | Required for Serial, Telephone, and POT circuits; Optional for Trunk and Message circuits. |
| Name | ALocationAccessPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Conditional/Required | 1,1 |  |  |
| Phone | ALocationAccessPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 18 | AN | Conditional/Required | 1,1 |  |  |
| CivicAddress | Loc | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessPerson | 64 Max | AN | Opt | 0,1 |  |  |
| City | Loc | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessPerson | 64 Max | AN | Opt | 0,1 |  |  |
| State | Loc | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessPerson | 64 Max | AN | Opt | 0,1 |  |  |
| Zip | Loc | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessPerson | 64 Max | N | Opt | 0,1 |  |  |
| Email | ALocationAccessPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | ALocationAccessPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | ALocationAccessPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | ALocationAccessPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 |  |  |
|  | AuthorizationList |  |  |  | Opt |  |  |  |
| State | AuthorizationItem | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList | 1 | N | Cond/Req | 1,1 | 2 3 | AuthorizationItem can appear multiple times 2 – provided 3 – denied Once an activity (Type) of authorization has been set to provided (State=2), it (Type) cannot be subsequently denied. |
| AfterHoursRepair | Type | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Cond/Req | 1,1 | true false |  |
| Standby | Type | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Cond/Req | 1,1 | true false |  |
| AfterHoursStandby | Type | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Cond/Req | 1,1 | true false |  |
| Test | Type | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Cond/Req | 1,1 | true false |  |
| ManagerInitiatedTest | Type | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Cond/Req | 1,1 | true false |  |
| Dispatch | Type | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Cond/Req | 1,1 | true false |  |
| NoAccess | Type | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Cond/Req | 1,1 | true false |  |
| DelayedMaintenance | Type | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Cond/Req | 1,1 | true false |  |
| Release | Type | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Cond/Req | 1,1 | true false |  |
| DeregulatedWork | Type | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Cond/Req | 1,1 | true false |  |
| AuthTime | AuthorizationItem | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList | 14 - 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
|  | AuthPerson |  |  |  | Opt | 0,1 |  |  |
| Name | AuthPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 64 Max | AN | Cond/Req | 1,1 |  |  |
| Phone | AuthPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem.AuthPerson | 64 Max | AN | Opt | 0,1 |  |  |
| City | Loc | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem.AuthPerson | 64 Max | AN | Opt | 0,1 |  |  |
| State | Loc | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem.AuthPerson | 64 Max | AN | Opt | 0,1 |  |  |
| Zip | Loc | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem.AuthPerson | 64 Max | AN | Opt | 0,1 |  |  |
| Email | AuthPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | AuthPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | AuthPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | AuthPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 64 Max | AN | Opt | 0,1 |  |  |
| CalledNumber | AdditionalCreateInfo | RequestTroubleReportCreationRequest | 64 Max | N | Opt | 0,1 |  |  |
| OnsiteTime | CommitmentTimeRequest | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 14 - 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ CommitmentTimeRequest will not be supported for Access Customers with designed circuits (type “3”, “S”, “T”, “C”, and “M”). |
| CustomerTroubleTickNum | AdditionalCreateInfo | RequestTroubleReportCreationRequest | 64 Max | AN | Opt | 0,1 |  |  |
| CustomerWorkCenter | AdditionalCreateInfo | RequestTroubleReportCreationRequest | 64 Max | AN | Opt | 0,1 |  |  |
|  | EscalationList |  |  |  | Opt |  |  |  |
| State | EscalationItem | RequestTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList | 1 | N | Cond/Req | 1,1 | 1 | 1 – requested |
| EscTime | EscalationItem | RequestTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList | 14 - 20 | AN | Cond/Req | 1,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Name | RequestPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem | 64 Max | AN | Cond/Req | 1,1 |  |  |
| Phone | RequestPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | RequestTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem. RequestPerson | 64 Max | AN | Opt | 0,1 |  |  |
| City | Loc | RequestTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem. RequestPerson | 64 Max | AN | Opt | 0,1 |  |  |
| State | Loc | RequestTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem. RequestPerson | 64 Max | AN | Opt | 0,1 |  |  |
| Zip | Loc | RequestTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem. RequestPerson | 64 Max | N | Opt | 0,1 |  |  |
| Email | RequestPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | RequestPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | RequestPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | RequestPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Level | EscalationItem | RequestTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList | 1 | N | Opt | 0,1 | 0 1 | 0 - No Escalation 1 - first-level |
|  | ManagedObjectAccessHour |  |  |  | Cond |  |  | ManagedObjectAccessHours is optional for non-designed circuits. It is required for designed circuits. |
| Sunday | DaysOfWeek | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Cond/Req | 1,1 | true false | ManagedObjectAccessHoursItem can appear multiple times |
| Monday | DaysOfWeek | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Cond/Req | 1,1 | true false |  |
| Tuesday | DaysOfWeek | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Cond/Req | 1,1 | true false |  |
| Wednesday | DaysOfWeek | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Cond/Req | 1,1 | true false |  |
| Thursday | DaysOfWeek | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Cond/Req | 1,1 | true false |  |
| Friday | DaysOfWeek | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Cond/Req | 1,1 | true false |  |
| Saturday | DaysOfWeek | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Cond/Req | 1,1 | true false |  |
| IntervalStart | IntervalsOfDayItem | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem. IntervalsOfDay | 8 | AN | Cond/Req | 1,1 |  | Local time in HH:MM:SS format |
| IntervalEnd | IntervalsOfDayItem | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem.IntervalsOfDay | 8 | AN | Cond/Req | 1,1 |  | Local time in HH:MM:SS format |
| ManagedObjectInstanceAliasItem | ManagedObjectInstanceAliasList | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 |  |  |
|  | ManagerContactPerson |  |  |  | Cond |  |  | ManagerContactPerson is conditional – it is required for “S” (including “3”), “T”, “C” and “M” type circuits; not applicable for “P” type circuit. |
| Name | ManagerContactPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Cond/Req | 1,1 |  |  |
| Phone | ManagerContactPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 18 | AN | Cond/Req | 1,1 |  |  |
| CivicAddress | Loc | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ManagerContactPerson | 64 Max | AN | Opt | 0,1 |  |  |
| City | Loc | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ManagerContactPerson | 64 Max | AN | Opt | 0,1 |  |  |
| State | Loc | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ManagerContactPerson | 64 Max | AN | Opt | 0,1 |  |  |
| Zip | Loc | RequestTroubleReportCreationRequest.AdditionalCreateInfo. ManagerContactPerson | 64 Max | N | Opt | 0,1 |  |  |
| Email | ManagerContactPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | ManagerContactPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | ManagerContactPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | ManagerContactPerson | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 |  |  |
| Number | PerceivedTroubleSeverity | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 1 | N | Opt | 0,1 | 0 1 2 3 | 0 – out of service 1 – back in service 2 – service impairment 3 – non service affecting trouble |
| PreferredPriority | AdditionalCreateInfo | RequestTroubleReportCreationRequest | 1 | N | Opt | 0,1 | 0 1 2 3 | 0 – undefined 1 – minor 2 – major 3 – serious |
| RepeatReport | AdditionalCreateInfo | RequestTroubleReportCreationRequest | 1 | N | Opt | 0,1 | 0 1 2 3 4 5 | 0 – unspecified 1 – recent installation 2 – repeat 3 – both installation & repeat 4 – chronic 5 – both installation & chronic |
| TroubleDetectionTime | AdditionalCreateInfo | RequestTroubleReportCreationRequest | 14 - 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
|  | TroubleReportStatusWindow |  |  |  | Opt |  |  |  |
| Day | TroubleReportStatusWindow | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 2 Max | N | Cond/Req | 1,1 | From "0" to "31" |  |
| Hour | TroubleReportStatusWindow | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 2 Max | N | Cond/Req | 1,1 | From "0" to "23" |  |
| Minute | TroubleReportStatusWindow | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 2 Max | N | Cond/Req | 1,1 | From "0" to "59" |  |
| Second | TroubleReportStatusWindow | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 2 Max | N | Opt | 0,1 | From "0" to "59" |  |
| Msec | TroubleReportStatusWindow | RequestTroubleReportCreationRequest.AdditionalCreateInfo | 3 Max | N | Opt | 0,1 | From "0" to "999" |  |
| TspPriority | AdditionalCreateInfo | RequestTroubleReportCreationRequest | 2 | AN | Opt | 0,1 |  | TSP = Telecom Service Priority |

Table 6.  Trouble Report Create Response – Normal

| tML Trouble Report Create Response - Normal |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | RequestTroubleReportCreationResponse | 36 Max | AN | Req | 1,1 |  | Create request correlation id |
| Type | RDNSequenceItem | RequestTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | RequestTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 5 | AN | Req | 1,1 | SP Network ID Value (First 2 chars will be state code and then remaining will be the last three characters mentioned below) VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) | First two characters will be the state code that was supplied in the create request. |
| Type | RDNSequenceItem | RequestTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | RequestTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | RequestTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 9 | AN | Req | 1,1 | serviceID |  |
| Assertion | RDNSequenceItem | RequestTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 64 Max | AN | Req | 1,1 | Service ID Value |  |
| InitiatingMode | Normal | RequestTroubleReportCreationResponseCreateResponse | 1 | N | Req | 1,1 | "0" |  |
| ReceivedTime | Normal | RequestTroubleReportCreationResponseCreateResponse | 14 - 20 | AN | Req | 1,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| TroubleReportId | Normal | RequestTroubleReportCreationResponse.CreateResponse | 32 Max | AN | Req | 1,1 |  | The maximum length supported by Verizon for TroubleReportId value is 18 characters |
| TroubleReportState | Normal | RequestTroubleReportCreationResponseCreateResponse | 1 | N | Req | 1,1 |  |  |
| Number | TroubleReportStatus | RequestTroubleReportCreationResponseCreateResponse.Normal | 3 Max | N | Req | 1,1 |  |  |
| TroubleReportStatusTime | Normal | RequestTroubleReportCreationResponseCreateResponse | 14 - 20 | AN | Req | 1,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
|  | AgentContactPerson |  |  |  | Req |  |  |  |
| Name | AgentContactPerson | RequestTroubleReportCreationResponseCreateResponse.Normal | 64 Max | AN | Cond/Req | 1,1 |  | AgentContactPerson is conditional. For designed circuits owned by Access Carrier customers (type “3”, “S”, “T”, “C”, and “M”), the name of the work center that owns the trouble report as well we the center telephone number will be provided. |
| Phone | AgentContactPerson | RequestTroubleReportCreationResponseCreateResponse.Normal | 18 | AN | Opt | 0,1 |  |  |
|  | Loc |  |  |  | Opt |  |  |  |
| CivicAddress | Loc | RequestTroubleReportCreationResponseCreateResponse.Normal. AgentContactPerson | 64 Max | AN | Cond/Req | 1,1 |  |  |
| City | Loc | RequestTroubleReportCreationResponseCreateResponse.Normal. AgentContactPerson | 64 Max | AN | Cond/Req | 1,1 |  |  |
| State | Loc | RequestTroubleReportCreationResponseCreateResponse.Normal. AgentContactPerson | 64 Max | AN | Cond/Req | 1,1 |  |  |
| Zip | Loc | RequestTroubleReportCreationResponseCreateResponse.Normal. AgentContactPerson | 64 Max | N | Cond/Req | 1,1 |  |  |
| Email | AgentContactPerson | RequestTroubleReportCreationResponseCreateResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | AgentContactPerson | RequestTroubleReportCreationResponseCreateResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | AgentContactPerson | RequestTroubleReportCreationResponseCreateResponse.Normal | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | AgentContactPerson | RequestTroubleReportCreationResponseCreateResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| OnsiteTime | CommitmentTime | RequestTroubleReportCreationResponseCreateResponse.Normal | 14 - 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ CommitmentTimes will not be provided on designed circuits owned by Access Carrier customers (type “3”, “S”, “T”, “C”, and “M”). As the trouble report process progresses, the Verizon center will provide estimated time to repair through AVC messages. |

Table 7.  Trouble Report Create Response – Exception

| tML Trouble Report Create Response (Exception) |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | RequestTroubleReportCreationResponse | 36 Max | AN | Req | 1,1 |  | Create request correlation id |
| Type | RDNSequenceItem | RequestTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | RequestTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 5 | AN | Req | 1,1 | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) | Value sent in the request will be echoed back. |
| Type | RDNSequenceItem | RequestTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | RequestTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value | Value sent in the request will be echoed back. |
| Type | RDNSequenceItem | RequestTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 9 | AN | Req | 1,1 | serviceID |  |
| Assertion | RDNSequenceItem | RequestTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 64 Max | AN | Req | 1,1 | Service ID Value |  |
| Type | RDNSequenceItem | RequestTroubleReportCreationResponseCreateResponse. Exception. TroubleReportAlreadyExists.ManagedObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | RequestTroubleReportCreationResponseCreateResponse. Exception. TroubleReportAlreadyExists.ManagedObjectInstance. DistinguishedName | 5 | AN | Req | 1,1 | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) | Value sent in the request will be echoed back. |
| Type | RDNSequenceItem | RequestTroubleReportCreationResponseCreateResponse. Exception. TroubleReportAlreadyExists.ManagedObjectInstance. DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | RequestTroubleReportCreationResponse.CreateResponse. Exception. TroubleReportAlreadyExists.ManagedObjectInstance. DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | RequestTroubleReportCreationResponse.CreateResponse. Exception. TroubleReportAlreadyExists.ManagedObjectInstance. DistinguishedName | 15 | AN | Req | 1,1 | troubleReportID |  |
| Assertion | RDNSequenceItem | RequestTroubleReportCreationResponse.CreateResponse. Exception. TroubleReportAlreadyExists.ManagedObjectInstance. DistinguishedName | 32 Max | AN | Req | 1,1 | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters For further processing regarding TroubleReportAlreadyExists exception, please refer to Annex E Trouble Ticket Late Bonding |
|  |  | RequestTroubleReportCreationResponse.CreateResponse. Exception |  |  |  |  |  | Every tag at aggregate level under “Exception” tag is optional. However, for an error response case, at least one aggregate will be present. The usage column merely indicates the child tag usage situation for a given aggregate. |
| AttributeIDItem | TRMustBePresentAttributeMissing | RequestTroubleReportCreationResponse.CreateResponse. Exception | * | AN | Req | 1,n |  | Req trouble report attribute name(s) |
| FallBackReporting | FallBackReporting | RequestTroubleReportCreationResponse.CreateResponse. Exception | * | AN | Req | 1,1 |  |  |
| Tag | ExceptionList | RequestTroubleReportCreationResponse.CreateResponse. Exception.AccessDenied | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | RequestTroubleReportCreationResponse.CreateResponse. Exception.AccessDenied | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | RequestTroubleReportCreationResponse.CreateResponse. Exception.ResourceLimitation | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | RequestTroubleReportCreationResponse.CreateResponse. Exception.ResourceLimitation | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | RequestTroubleReportCreationResponse.CreateResponse. Exception.InvalidDataReceived | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | RequestTroubleReportCreationResponse.CreateResponse. Exception.InvalidDataReceived | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | RequestTroubleReportCreationResponseCreateResponse. Exception.ProcessingFailure | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | RequestTroubleReportCreationResponseCreateResponse. Exception.ProcessingFailure | * | AN | Req | 1,1 |  | Error message |

## Trouble Report Modification

Table 8.  Trouble Report Modification Request

| tML Trouble Report Modification Request |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | ModifyAttributesRequest | ModifyAttributesRequest | 36 max | AN | Req | 1,1 |  |  |
| UserId | Customer | ModifyAttributesRequest | 10 | AN | Req | 1,1 |  | Refer to §7.3 for detailed informational. |
| ServiceProfile | Customer | ModifyAttributesRequest | 8 max | AN | Req | 1,1 | RESELLER CLEC Carrier | “RESELLER” or “CLEC” for Verizon Local Customers “Carrier” for Verizon Access Customers |
| Type | RDNSequenceItem | ModifyAttributesRequest.TargetObjectName.DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | ModifyAttributesRequest.TargetObjectName.DistinguishedName | 3 | AN | Req | 1,1 | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) |  |
| Type | RDNSequenceItem | ModifyAttributesRequest.TargetObjectName.DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | ModifyAttributesRequest.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | ModifyAttributesRequest.TargetObjectName.DistinguishedName | 15 | AN | Req | 1,1 | troubleReportID |  |
| Assertion | RDNSequenceItem | ModifyAttributesRequest.TargetObjectName.DistinguishedName | 32 max | AN | Req | 1,1 | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |
|  |  | ModifyAttributesRequest.ModifyRequest |  |  |  |  |  | Every tag on the data aggregate level has marked as “Optional”. However, at least one aggregate must be present under the Parent Aggregate “ModifyRequest”. The usage column merely indicates the child tag usage situation if a given aggregate is present. |
|  |  | ModifyAttributesRequest. ModifyRequest. AdditionalTroubleInfoList |  |  | Opt | 0,1 |  | This attribute is optional; if it is present in the request, its child nodes follows the REQ/OPT rule in Usage colume. |
| AdditionalTroubleInfoItem | AdditionalTroubleInfoList | ModifyAttributesRequest.ModifyRequest | 256 max | AN | Cond/Req | 0,n |  |  |
|  |  | ModifyAttributesRequest. ModifyRequest. ALocationAccessAddress |  |  | Opt | 0,1 |  | This attribute is optional; if it is present in the request, its child nodes follows the REQ/OPT rule in Usage colume. |
| PremisesName | ALocationAccessAddress | ModifyAttributesRequest.ModifyRequest | 64 max | AN | Opt | 0,1 |  |  |
| CivicAddress | PremisesAddress | ModifyAttributesRequest.ModifyRequest.ALocationAccessAddress | 64 max | AN | Cond/Req | 1,1 |  |  |
| City | PremisesAddress | ModifyAttributesRequest.ModifyRequest.ALocationAccessAddress | 64 max | AN | Cond/Req | 1,1 |  |  |
| State | PremisesAddress | ModifyAttributesRequest.ModifyRequest.ALocationAccessAddress | 64 max | AN | Cond/Req | 1,1 |  |  |
| Zip | PremisesAddress | ModifyAttributesRequest.ModifyRequest.ALocationAccessAddress | 64 max | N | Cond/Req | 1,1 |  |  |
|  |  | ModifyAttributesRequest. ModifyRequest. ALocatioAccessHours |  |  | Opt | 0,1 |  | This attribute is optional; if it is present in the request, its child nodes follows the REQ/OPT rule in Usage colume. |
| Sunday | DaysOfWeek | ModifyAttributesRequest.ModifyRequest.ALocatioAccessHours.LocationAccessHoursItem | 5 max | AN | Cond/Req | 1,1 | true false | LocationAccessHoursItem can appear multiple times |
| Monday | DaysOfWeek | ModifyAttributesRequest.ModifyRequest.ALocatioAccessHours.LocationAccessHoursItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Tuesday | DaysOfWeek | ModifyAttributesRequest.ModifyRequest.ALocatioAccessHours.LocationAccessHoursItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Wednesday | DaysOfWeek | ModifyAttributesRequest.ModifyRequest.ALocatioAccessHours.LocationAccessHoursItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Thursday | DaysOfWeek | ModifyAttributesRequest.ModifyRequest.ALocatioAccessHours.LocationAccessHoursItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Friday | DaysOfWeek | ModifyAttributesRequest.ModifyRequest.ALocatioAccessHours.LocationAccessHoursItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Saturday | DaysOfWeek | ModifyAttributesRequest.ModifyRequest.ALocatioAccessHours.LocationAccessHoursItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| IntervalStart | IntervalsOfDayItem | ModifyAttributesRequest.ModifyRequest.ALocatioAccessHours.LocationAccessHoursItem.IntervalsOfDay | 8 | AN | Cond/Req | 1,1 |  |  |
| IntervalEnd | IntervalsOfDayItem | ModifyAttributesRequest.ModifyRequest.ALocatioAccessHours.LocationAccessHoursItem.IntervalsOfDay | 8 | AN | Cond/Req | 1,1 |  |  |
|  |  | ModifyAttributesRequest. ModifyRequest. ALocatioAccessPerson |  |  | Opt | 0,1 |  | This attribute is optional; if it is present in the request, its child nodes follows the REQ/OPT rule in Usage colume. |
| Name | ALocationAccessPerson | ModifyAttributesRequest.ModifyRequest | 64 max | AN | Req | 1,1 |  |  |
| Phone | ALocationAccessPerson | ModifyAttributesRequest.ModifyRequest | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | ModifyAttributesRequest.ModifyRequest.ALocationAccessPerson | 64 max | AN | Opt | 0,1 |  |  |
| City | Loc | ModifyAttributesRequest.ModifyRequest.ALocationAccessPerson | 64 max | AN | Opt | 0,1 |  |  |
| State | Loc | ModifyAttributesRequest.ModifyRequest.ALocationAccessPerson | 64 max | AN | Opt | 0,1 |  |  |
| Zip | Loc | ModifyAttributesRequest.ModifyRequest.ALocationAccessPerson | 64 max | N | Opt | 0,1 |  |  |
| Email | ALocationAccessPerson | ModifyAttributesRequest.ModifyRequest | 64 max | AN | Opt | 0,1 |  |  |
| Fax | ALocationAccessPerson | ModifyAttributesRequest.ModifyRequest | 64 max | AN | Opt | 0,1 |  |  |
| Respon | ALocationAccessPerson | ModifyAttributesRequest.ModifyRequest | 64 max | AN | Opt | 0,1 |  |  |
| Pager | ALocationAccessPerson | ModifyAttributesRequest.ModifyRequest | 64 max | AN | Opt | 0,1 |  |  |
|  |  | ModifyAttributesRequest. ModifyRequest. AuthorizationList |  |  | Opt | 0,1 |  | This attribute is optional; if it is present in the request, its child nodes follows the REQ/OPT rule in Usage colume. |
| State | AuthorizationItem | ModifyAttributesRequest.ModifyRequest.AuthorizationList | 1 | N | Cond/Req | 1,1 | 2 3 | 2 – Provided 3 – Denied AuthorizationItem can appear multiple times Once an activity (Type) of authorization has been set to provided (State=2), it (Type) cannot be subsequently denied. |
| AfterHoursRepair | Type | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Standby | Type | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| AfterHoursStandby | Type | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Test | Type | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| ManagerInitiatedTest | Type | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Dispatch | Type | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| NoAccess | Type | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| DelayedMaintenance | Type | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Release | Type | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| DeregulatedWork | Type | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| AuthTime | AuthorizationItem | ModifyAttributesRequest.ModifyRequest.AuthorizationList | 14 – 20 | AN | Opt | 0,1 |  | AuthorizationItem is repeatable AuthTime format – GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Name | AuthPerson | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem | 64 max | AN | Cond/Req | 1,1 |  |  |
| Phone | AuthPerson | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem.AuthPerson | 64 max | AN | Opt | 0,1 |  |  |
| City | Loc | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem.AuthPerson | 64 max | AN | Opt | 0,1 |  |  |
| State | Loc | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem.AuthPerson | 64 max | AN | Opt | 0,1 |  |  |
| Zip | Loc | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem.AuthPerson | 64 max | N | Opt | 0,1 |  |  |
| Email | AuthPerson | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem | 64 max | AN | Opt | 0,1 |  |  |
| Fax | AuthPerson | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem | 64 max | AN | Opt | 0,1 |  |  |
| Respon | AuthPerson | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem | 64 max | AN | Opt | 0,1 |  |  |
| Pager | AuthPerson | ModifyAttributesRequest.ModifyRequest.AuthorizationList.AuthorizationItem | 64 max | AN | Opt | 0,1 |  |  |
|  |  | ModifyAttributesRequest. ModifyRequest. EscalationList |  |  | Opt | 0,1 |  | This attribute is optional; if it is present in the request, its child nodes follows the REQ/OPT rule in Usage colume. |
| State | EscalationItem | ModifyAttributesRequest.ModifyRequest.EscalationList | 1 | N | Cond/Req | 1,1 | 1 | 1 – Requested |
| EscTime | EscalationItem | ModifyAttributesRequest.ModifyRequest.EscalationList | 14 – 20 | AN | Cond/Req | 1,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Name | RequestPerson | ModifyAttributesRequest.ModifyRequest.EscalationList.EscalationItem | 64 max | AN | Cond/Req | 1,1 |  |  |
| Phone | RequestPerson | ModifyAttributesRequest.ModifyRequest.EscalationList.EscalationItem | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | ModifyAttributesRequest.ModifyRequest.EscalationList.EscalationItem.RequestPerson | 64 max | AN | Opt | 0,1 |  |  |
| City | Loc | ModifyAttributesRequest.ModifyRequest.EscalationList.EscalationItem. RequestPerson | 64 max | AN | Opt | 0,1 |  |  |
| State | Loc | ModifyAttributesRequest.ModifyRequest.EscalationList.EscalationItem.RequestPerson | 64 max | AN | Opt | 0,1 |  |  |
| Zip | Loc | ModifyAttributesRequest.ModifyRequest.EscalationList.EscalationItem.RequestPerson | 64 max | N | Opt | 0,1 |  |  |
| Email | RequestPerson | ModifyAttributesRequest.ModifyRequest.EscalationList.EscalationItem | 64 max | AN | Opt | 0,1 |  |  |
| Fax | RequestPerson | ModifyAttributesRequest.ModifyRequest.EscalationList.EscalationItem | 64 max | AN | Opt | 0,1 |  |  |
| Respon | RequestPerson | ModifyAttributesRequest.ModifyRequest.EscalationList.EscalationItem | 64 max | AN | Opt | 0,1 |  |  |
| Pager | RequestPerson | ModifyAttributesRequest.ModifyRequest.EscalationList.EscalationItem | 64 max | AN | Opt | 0,1 |  |  |
| Level | EscalationItem | ModifyAttributesRequest.ModifyRequest.EscalationList | 1 | N | Opt | 0,1 | 0 1 2 3 4 | 0 - No Escalation 1 - first-level 2 - second-level 3 - third-level 4 - fourth-level |
|  |  | ModifyAttributesRequest. ModifyRequest. ManagedObjectAccessHoursItem |  |  | Opt | 0,1 |  | This attribute is optional; if it is present in the request, its child nodes follows the REQ/OPT rule in Usage colume. |
| Sunday | DaysOfWeek | ModifyAttributesRequest.ModifyRequest.ManagedObjectAccessHours.ManagedObjectAccessHoursItem | 5 max | AN | Cond/Req | 1,1 | true false | ManagedObjectAccessHoursItem can appear multiple times |
| Monday | DaysOfWeek | ModifyAttributesRequest.ModifyRequest.ManagedObjectAccessHours.ManagedObjectAccessHoursItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Tuesday | DaysOfWeek | ModifyAttributesRequest.ModifyRequest.ManagedObjectAccessHours.ManagedObjectAccessHoursItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Wednesday | DaysOfWeek | ModifyAttributesRequest.ModifyRequest.ManagedObjectAccessHours.ManagedObjectAccessHoursItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Thursday | DaysOfWeek | ModifyAttributesRequest.ModifyRequest.ManagedObjectAccessHours.ManagedObjectAccessHoursItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Friday | DaysOfWeek | ModifyAttributesRequest.ModifyRequest.ManagedObjectAccessHours.ManagedObjectAccessHoursItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Saturday | DaysOfWeek | ModifyAttributesRequest.ModifyRequest.ManagedObjectAccessHours.ManagedObjectAccessHoursItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| IntervalStart | IntervalsOfDayItem | ModifyAttributesRequest.ModifyRequest.ManagedObjectAccessHours.ManagedObjectAccessHoursItem.IntervalsOfDay | 8 | AN | Cond/Req | 1,1 |  |  |
| IntervalEnd | IntervalsOfDayItem | ModifyAttributesRequest.ModifyRequest.ManagedObjectAccessHours.ManagedObjectAccessHoursItem.IntervalsOfDay | 8 | AN | Cond/Req | 1,1 |  |  |
|  |  | ModifyAttributesRequest. ModifyRequest. ManagedObjectInstanceAliasList |  |  | Opt | 0,1 |  | This attribute is optional; if it is present in the request, its child nodes follows the REQ/OPT rule in Usage colume. |
| ManagedObjectInstanceAliasItem | ManagedObjectInstanceAliasList | ModifyAttributesRequest.ModifyRequest | 64 max | AN | Cond/Req | 1 |  |  |
|  |  | ModifyAttributesRequest. ModifyRequest. ManagerContactPerson |  |  | Opt | 0,1 |  | This attribute is optional; if it is present in the request, its child nodes follows the REQ/OPT rule in Usage colume. |
| Name | ManagerContactPerson | ModifyAttributesRequest.ModifyRequest | 64 max | AN | Cond/Req | 1,1 |  |  |
| Phone | ManagerContactPerson | ModifyAttributesRequest.ModifyRequest | 18 | AN | Cond/Req | 1,1 |  |  |
| CivicAddress | Loc | ModifyAttributesRequest.ModifyRequest.ManagerContactPerson | 64 max | AN | Opt | 0,1 |  |  |
| City | Loc | ModifyAttributesRequest.ModifyRequest.ManagerContactPerson | 64 max | AN | Opt | 0,1 |  |  |
| State | Loc | ModifyAttributesRequest.ModifyRequest.ManagerContactPerson | 64 max | AN | Opt | 0,1 |  |  |
| Zip | Loc | ModifyAttributesRequest.ModifyRequest.ManagerContactPerson | 64 max | N | Opt | 0,1 |  |  |
| Email | ManagerContactPerson | ModifyAttributesRequest.ModifyRequest | 64 max | AN | Opt | 0,1 |  |  |
| Fax | ManagerContactPerson | ModifyAttributesRequest.ModifyRequest | 64 max | AN | Opt | 0,1 |  |  |
| Respon | ManagerContactPerson | ModifyAttributesRequest.ModifyRequest | 64 max | AN | Opt | 0,1 |  |  |
| Pager | ManagerContactPerson | ModifyAttributesRequest.ModifyRequest | 64 max | AN | Opt | 0,1 |  |  |
| Number | PerceivedTroubleSeverity | ModifyAttributesRequest.ModifyRequest | 1 | N | Opt | 0,1 |  |  |
| PreferredPriority | ModifyRequest | ModifyAttributesRequest | 1 | N | Opt | 0,1 | 0 1 2 3 | 0 – undefined 1 – minor 2 – major 3 – serious |
|  |  | ModifyAttributesRequest. ModifyRequest. TroubleReportStatusWindow |  |  | Opt | 0,1 |  | This attribute is optional; if it is present in the request, its child nodes follows the REQ/OPT rule in Usage colume. |
| Day | TroubleReportStatusWindow | ModifyAttributesRequest.ModifyRequest | 2 max | N | Cond/Req | 1,1 |  |  |
| Hour | TroubleReportStatusWindow | ModifyAttributesRequest.ModifyRequest | 2 max | N | Cond/Req | 1,1 |  |  |
| Minute | TroubleReportStatusWindow | ModifyAttributesRequest.ModifyRequest | 2 max | N | Cond/Req | 1,1 |  |  |
| Second | TroubleReportStatusWindow | ModifyAttributesRequest.ModifyRequest | 2 max | N | Opt | 0,1 |  |  |
| Msec | TroubleReportStatusWindow | ModifyAttributesRequest.ModifyRequest | 3 max | N | Opt | 0,1 |  |  |

Table 9.  Trouble Report Modification Response

| tML Trouble Report Modification Response |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | ModifyAttributesResponse | 36 max | AN | Req | 1,1 |  |  |
| Type | RDNSequenceItem | ModifyAttributesResponse.TargetObjectName.DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | ModifyAttributesResponse.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,1 | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) |  |
| Type | RDNSequenceItem | ModifyAttributesResponse.TargetObjectName.DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | ModifyAttributesResponse.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | ModifyAttributesResponse.TargetObjectName.DistinguishedName | 15 | AN | Req | 1,1 | troubleReportID |  |
| Assertion | RDNSequenceItem | ModifyAttributesResponse.TargetObjectName.DistinguishedName | 32 max | AN | Req | 1,1 | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |
|  |  | ModifyAttributesResponse.Normal |  |  |  |  |  | All Tags under the Parent Aggregate of “Normal” submitted on the Request must be returned on the Response with either a ‘true’ or ‘false’ value. tML trouble report modification supports partial success case. So a response XML could have both “Normal” and “Exception” aggregates present. |
| AdditionalTroubleInfoList | Normal | ModifyAttributesResponse | 5 max | AN | Opt | 0,1 | true – Successfully Modify false – Unsuccessful Modify |  |
| ALocationAccessAddress | Normal | ModifyAttributesResponse | 5 max | AN | Opt | 0,1 | true – Successfully Modify false – Unsuccessful Modify |  |
| ALocationAccessHours | Normal | ModifyAttributesResponse | 5 max | AN | Opt | 0,1 | true – Successfully Modify false – Unsuccessful Modify |  |
| ALocationAccessPerson | Normal | ModifyAttributesResponse | 5 max | AN | Opt | 0,1 | true – Successfully Modify false – Unsuccessful Modify |  |
| AuthorizationList | Normal | ModifyAttributesResponse | 5 max | AN | Opt | 0,1 | true – Successfully Modify false – Unsuccessful Modify |  |
| EscalationList | Normal | ModifyAttributesResponse | 5 max | AN | Opt | 0,1 | true – Successfully Modify false – Unsuccessful Modify |  |
| ManagedObjectAccessHours | Normal | ModifyAttributesResponse | 5 max | AN | Opt | 0,1 | true – Successfully Modify false – Unsuccessful Modify |  |
| ManagedObjectInstanceAliasList | Normal | ModifyAttributesResponse | 5 max | AN | Opt | 0,1 | true – Successfully Modify false – Unsuccessful Modify |  |
| ManagerContactPerson | Normal | ModifyAttributesResponse | 5 max | AN | Opt | 0,1 | true – Successfully Modify false – Unsuccessful Modify |  |
| PerceivedTroubleSeverity | Normal | ModifyAttributesResponse | 5 max | AN | Opt | 0,1 | true – Successfully Modify false – Unsuccessful Modify |  |
| PreferredPriority | Normal | ModifyAttributesResponse | 5 max | AN | Opt | 0,1 | true – Successfully Modify false – Unsuccessful Modify |  |
| TroubleReportStatusWindow | Normal | ModifyAttributesResponse | 5 max | AN | Opt | 0,1 | true – Successfully Modify false – Unsuccessful Modify |  |
|  |  | ModifyAttributesResponse.Exception |  |  |  |  |  | tML trouble report modification supports partial success case. So a response XML could have both “Normal” and “Exception” aggregates present. The following aggregates: AccessDenied ResourceLimitation InvalidDataReceived ProcessingFailure NotFound MissingData TroubleReportChangeDenied are all optional under ModifyAttributesResponse.Exception. If any one of above aggregates is present, then at least one ExceptionList should be present for that aggregate, and multiple ExceptionList entries can be present. However, TroubleReportChangeDenied does not have ExceptionList aggregate. The usage column merely indicates the child tag usage situation if a given aggregate is present. |
| Tag | ExceptionList | ModifyAttributesResponse. Exception.AccessDenied | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | ModifyAttributesResponse. Exception.AccessDenied | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | ModifyAttributesResponse. Exception.ResourceLimitation | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | ModifyAttributesResponse. Exception.ResourceLimitation | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | ModifyAttributesResponse. Exception.InvalidDataReceived | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | ModifyAttributesResponse. Exception.InvalidDataReceived | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | ModifyAttributesResponse. Exception.ProcessingFailure | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | ModifyAttributesResponse. Exception.ProcessingFailure | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | ModifyAttributesResponse. Exception.NotFound | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | ModifyAttributesResponse. Exception.NotFound | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | ModifyAttributesResponse. Exception.MissingData | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | ModifyAttributesResponse. Exception.MissingData | * | AN | Req | 1,1 |  | Error message |
| ChangeDeniedReason | TroubleReportChangeDenied | ModifyAttributesResponse.Exception | 1 | N | Req | 1,1 | 1 2 3 | 1 – Waiting Verification of Closure 2 – Trouble Report already Closed 3 – Activity Authorization Pending |

## Trouble Report Cancellation

This service is used for a customer to issue a cancel request on an existing Trouble Report in an active status (active means the trouble report state is not equal to 3 or 4). When the customer receives a normal response, it merely indicates that the customer’s request has been received by Verizon Web Service Gateway, and will be forwarded to an appropriate Verizon trouble administration system division for processing based on Verizon business  practice rules. Therefore, the trouble report may not be cancelled immediately by a Verizon trouble administration system division; or the trouble report may have already been closed by a Verizon trouble administration system division, etc.. For example, in a situation where a technician has already been dispatched to handle the customer’s original request before a Verizon trouble administration system division receives the cancel request from Verizon Web Service Gateway, the customer may be responsible for related charge(s) regarding repair activities.

Table 10.  Trouble Report Cancellation Request

| tML Trouble Report Cancellation Request |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | CancelTroubleReportRequest | 36 max | AN | Req | 1,1 |  |  |
| UserId | Customer | CancelTroubleReportRequest | 10 | AN | Req | 1,1 |  | Refer to §7.3 for detailed informational. |
| ServiceProfile | Customer | CancelTroubleReportRequest | 8 max | AN | Req | 1,1 | RESELLER CLEC Carrier | “RESELLER” or “CLEC” for Verizon Local Customers “Carrier” for Verizon Access Customers |
| Type | RDNSequenceItem | CancelTroubleReportRequest.TargetObjectName.DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | CancelTroubleReportRequest.TargetObjectName.DistinguishedName | 3 | AN | Req | 1,1 | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) |  |
| Type | RDNSequenceItem | CancelTroubleReportRequest.TargetObjectName.DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | CancelTroubleReportRequest.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | CancelTroubleReportRequest.TargetObjectName.DistinguishedName | 15 | AN | Req | 1,1 | troubleReportID |  |
| Assertion | RDNSequenceItem | CancelTroubleReportRequest.TargetObjectName.DistinguishedName | 32 max | AN | Req | 1,1 | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |
| CancelRequestedByManager | CancelRequestedByManager | CancelTroubleReportRequest | 5 max | AN | Req | 1,1 | true | If “false” is entered, return an error. |
|  | CancelRemark |  |  |  | Opt |  |  |  |
| AdditionalTroubleInfoItem | CancelRemark | CancelTroubleReportRequest | 256 max | AN | Cond/Req | 1,n |  | AdditionalTroubleInfoItem can appear multiple times |
|  | TroubleClearancePerson |  |  |  | Req |  |  |  |
| Name | TroubleClearancePerson | CancelTroubleReportRequest | 64 max | AN | Req | 1,1 |  |  |
| Phone | TroubleClearancePerson | CancelTroubleReportRequest | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | CancelTroubleReportRequest.TroubleClearancePerson | 64 max | AN | Opt | 0,1 |  |  |
| City | Loc | CancelTroubleReportRequest.TroubleClearancePerson | 64 max | AN | Opt | 0,1 |  |  |
| State | Loc | CancelTroubleReportRequest.TroubleClearancePerson | 64 max | AN | Opt | 0,1 |  |  |
| Zip | Loc | CancelTroubleReportRequest.TroubleClearancePerson | 64 max | N | Opt | 0,1 |  |  |
| Email | TroubleClearancePerson | CancelTroubleReportRequest | 64 max | AN | Opt | 0,1 |  |  |
| Fax | TroubleClearancePerson | CancelTroubleReportRequest | 64 max | AN | Opt | 0,1 |  |  |
| Respon | TroubleClearancePerson | CancelTroubleReportRequest | 64 max | AN | Opt | 0,1 |  |  |
| Pager | TroubleClearancePerson | CancelTroubleReportRequest | 64 max | AN | Opt | 0,1 |  |  |

Table 11.  Trouble Report Cancellation Response - Normal

| tML Trouble Report Cancellation Response |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | CancelTroubleReportResponse | 36 max | AN | Req | 1,1 |  |  |
| Type | RDNSequenceItem | CancelTroubleReportResponse.TargetObjectName.DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | CancelTroubleReportResponse.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,1 | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) |  |
| Type | RDNSequenceItem | CancelTroubleReportResponse.TargetObjectName.DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | CancelTroubleReportResponse.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | CancelTroubleReportResponse.TargetObjectName.DistinguishedName | 15 | AN | Req | 1,1 | troubleReportID |  |
| Assertion | RDNSequenceItem | CancelTroubleReportResponse.TargetObjectName.DistinguishedName | 32 max | AN | Req | 1,1 | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |

Table 12.  Trouble Report Cancellation Response - Exception

| tML Trouble Report Cancellation Response |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | CancelTroubleReportResponse | 36 max | AN | Req | 1,1 |  |  |
| Type | RDNSequenceItem | CancelTroubleReportResponse.TargetObjectName.DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | CancelTroubleReportResponse.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,1 | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) |  |
| Type | RDNSequenceItem | CancelTroubleReportResponse.TargetObjectName.DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | CancelTroubleReportResponse.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | CancelTroubleReportResponse.TargetObjectName.DistinguishedName | 15 | AN | Req | 1,1 | troubleReportID |  |
| Assertion | RDNSequenceItem | CancelTroubleReportResponse.TargetObjectName.DistinguishedName | 32 max | AN | Req | 1,1 | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |
|  |  | CancelTroubleReportResponse. Exception |  |  |  |  |  | The following aggregates: AccessDenied ResourceLimitation InvalidDataReceived ProcessingFailure NotFound MissingData TroubleReportChangeDenied are all optional under CancelTroubleReportResponse. Exception. If any one of above aggregates is present, then at least one ExceptionList should be present for that aggregate, and multiple ExceptionList entries can be present. |
| Tag | ExceptionList | CancelTroubleReportResponse. Exception.AccessDenied | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | CancelTroubleReportResponse. Exception.AccessDenied | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | CancelTroubleReportResponse. Exception.ResourceLimitation | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | CancelTroubleReportResponse. Exception.ResourceLimitation | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | CancelTroubleReportResponse. Exception.InvalidDataReceived | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | CancelTroubleReportResponse. Exception.InvalidDataReceived | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | CancelTroubleReportResponse. Exception.ProcessingFailure | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | CancelTroubleReportResponse. Exception.ProcessingFailure | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | CancelTroubleReportResponse. Exception.NotFound | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | CancelTroubleReportResponse. Exception.NotFound | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | CancelTroubleReportResponse. Exception.MissingData | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | CancelTroubleReportResponse. Exception.MissingData | * | AN | Req | 1,1 |  | Error message |
| ChangeDeniedReason | TroubleReportChangeDenied | CancelTroubleReportResponse.Exception | 1 | N | Req | 1,1 | 1 2 3 | 1 – Waiting Verification of Closure 2 – Trouble Report already Closed 3 – Activity Authorization Pending |

## Trouble Report Close Out Verification

Table 13.  Trouble Report Close Out Verification Request

| tML Trouble Report Close Out Verification Request |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | VerifyRepairCompletionRequest | 36 max | AN | Req | 1,1 |  |  |
| UserId | Customer | VerifyRepairCompletionRequest | 10 | AN | Req | 1,1 |  | Refer to §7.3 for detailed informational. |
| ServiceProfile | Customer | VerifyRepairCompletionRequest | 8 max | AN | Req | 1,1 | RESELLER CLEC Carrier | “RESELLER” or “CLEC” for Verizon Local Customers “Carrier” for Verizon Access Customers |
| Type | RDNSequenceItem | VerifyRepairCompletionRequest.TargetObjectName.DistinguishedName | 9 | AN | Req | 1,N | networkID |  |
| Assertion | RDNSequenceItem | VerifyRepairCompletionRequest.TargetObjectName.DistinguishedName | 3 | AN | Req | 1,N | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) |  |
| Type | RDNSequenceItem | VerifyRepairCompletionRequest.TargetObjectName.DistinguishedName | 11 | AN | Req | 1,N | accountName |  |
| Assertion | RDNSequenceItem | VerifyRepairCompletionRequest.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,N | SC Account Name Value |  |
| Type | RDNSequenceItem | VerifyRepairCompletionRequest.TargetObjectName.DistinguishedName | 15 | AN | Req | 1,N | troubleReportID |  |
| Assertion | RDNSequenceItem | VerifyRepairCompletionRequest.TargetObjectName.DistinguishedName | 32 max | AN | Req | 1,N | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |
| CloseOutVerification | CloseOutVerification | VerifyRepairCompletionRequest | 1 | N | Req | 1,1 | 0 1 2 3 4 | 0 – No Action 1 – Verified 2 – Denied 3 – Denied Activity Duration Disputed 4 – Denied Close Out Narrative Disputed |
| AdditionalTroubleInfoItem | VerificationRemarks | VerifyRepairCompletionRequest | 256 max | AN | Req | 1,N |  | Multiple AdditionalTroubleInfoItem can be present. VerificationRemarks aggregate is optional. If VerificationRemarks aggregate is present, at least one AdditionalTroubleInfoItem should be present. |
|  | TroubleClearancePerson |  |  |  | Req |  |  |  |
| Name | TroubleClearancePerson | VerifyRepairCompletionRequest | 64 max | AN | Req | 1,1 |  | The maximum length supported by Verizon for Name value is 30 characters |
| Phone | TroubleClearancePerson | VerifyRepairCompletionRequest | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | VerifyRepairCompletionRequest.TroubleClearancePerson | 64 max | AN | Opt | 0,1 |  |  |
| City | Loc | VerifyRepairCompletionRequest.TroubleClearancePerson | 64 max | AN | Opt | 0,1 |  |  |
| State | Loc | VerifyRepairCompletionRequest.TroubleClearancePerson | 64 max | AN | Opt | 0,1 |  |  |
| Zip | Loc | VerifyRepairCompletionRequest.TroubleClearancePerson | 64 max | N | Opt | 0,1 |  |  |
| Email | TroubleClearancePerson | VerifyRepairCompletionRequest | 64 max | AN | Opt | 0,1 |  |  |
| Fax | TroubleClearancePerson | VerifyRepairCompletionRequest | 64 max | AN | Opt | 0,1 |  |  |
| Respon | TroubleClearancePerson | VerifyRepairCompletionRequest | 64 max | AN | Opt | 0,1 |  |  |
| Pager | TroubleClearancePerson | VerifyRepairCompletionRequest | 64 max | AN | Opt | 0,1 |  |  |

Table 14.  Trouble Report Close Out Verification Response – Normal

| tML Trouble Report Close Out Verification Response |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | VerifyRepairCompletionResponse | 36 max | AN | Req | 1,1 |  |  |
| Type | RDNSequenceItem | VerifyRepairCompletionResponse.TargetObjectName.DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | VerifyRepairCompletionResponse.TargetObjectName.DistinguishedName | 3 | AN | Req | 1,1 | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) |  |
| Type | RDNSequenceItem | VerifyRepairCompletionResponse.TargetObjectName.DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | VerifyRepairCompletionResponse.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | VerifyRepairCompletionResponse.TargetObjectName.DistinguishedName | 15 | AN | Req | 1,1 | troubleReportID |  |
| Assertion | RDNSequenceItem | VerifyRepairCompletionResponse.TargetObjectName.DistinguishedName | 32 max | AN | Req | 1,1 | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |

Table 15.  Trouble Report Close Out Verification Response – Exception

| tML Trouble Report Close Out Verification Response (Exception) |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | VerifyRepairCompletionResponse | 36 max | AN | Req | 1,1 |  |  |
| Type | RDNSequenceItem | VerifyRepairCompletionResponse.TargetObjectName.DistinguishedName | 9 | AN | Req | 1,N | networkID |  |
| Assertion | RDNSequenceItem | VerifyRepairCompletionResponse.TargetObjectName.DistinguishedName | 3 | AN | Req | 1,N | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) |  |
| Type | RDNSequenceItem | VerifyRepairCompletionResponse.TargetObjectName.DistinguishedName | 11 | AN | Req | 1,N | accountName |  |
| Assertion | RDNSequenceItem | VerifyRepairCompletionResponse.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,N | SC Account Name Value |  |
| Type | RDNSequenceItem | VerifyRepairCompletionResponse.TargetObjectName.DistinguishedName | 15 | AN | Req | 1,N | troubleReportID |  |
| Assertion | RDNSequenceItem | VerifyRepairCompletionResponse.TargetObjectName.DistinguishedName | 32 max | AN | Req | 1,N | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |
|  |  | VerifyRepairCompletionResponse.Exception |  |  |  |  |  | The following aggregates: AccessDenied ResourceLimitation InvalidDataReceived ProcessingFailure NotFound MissingData CannotVerifyOrDeniedAtThisTime are all optional under VerifyRepairCompletionResponse.Exception If any one of above aggregates is present, then at least one ExceptionList should be present for that aggregate, and multiple ExceptionList entries can be present. |
| Tag | ExceptionList | VerifyRepairCompletionResponse. Exception.AccessDenied | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | VerifyRepairCompletionResponse. Exception.AccessDenied | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | VerifyRepairCompletionResponse. Exception.ResourceLimitation | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | VerifyRepairCompletionResponse. Exception.ResourceLimitation | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | VerifyRepairCompletionResponse. Exception.InvalidDataReceived | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | VerifyRepairCompletionResponse. Exception.InvalidDataReceived | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | VerifyRepairCompletionResponse. Exception.ProcessingFailure | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | VerifyRepairCompletionResponse. Exception.ProcessingFailure | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | VerifyRepairCompletionResponse.Exception.NotFound | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | VerifyRepairCompletionResponse.Exception.NotFound | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | VerifyRepairCompletionResponse.Exception.MissingData | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | VerifyRepairCompletionResponse.Exception.MissingData | * | AN | Req | 1,1 |  | Error message |
| CannotVerifyOrDeniedAtThisTime | Exception | VerifyRepairCompletionResponse | * | AN | Req | 1,1 |  | Field Note – The presence of this tag means that “Communication in Progress. Message is out of Sequence.” |

## Retrieve Trouble Report Attributes

Other than retrieving Trouble Reports created in TAXI system,  this transaction can also be used to perform Trouble Ticket late bonding, please refer to Annex E	Trouble Ticket Late Bonding

Table 16.  Retrieve Trouble Report Attributes Request

| tML Retrieve Trouble Report Attributes Request |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | RetrieveAttributesByTroubleReportIdRequest | 36 max | AN | Req | 1,1 |  |  |
| UserId | Customer | RetrieveAttributesByTroubleReportIdRequest | 10 | AN | Req | 1,1 |  | Refer to §7.3 for detailed informational. |
| ServiceProfile | Customer | RetrieveAttributesByTroubleReportIdRequest | 8 max | AN | Req | 1,1 | RESELLER CLEC Carrier | “RESELLER” or “CLEC” for Verizon Local Customers “Carrier” for Verizon Access Customers |
| Type | RDNSequenceItem | RetrieveAttributesByTroubleReportIdRequest.TargetObjectName.DistinguishedName | 9 | AN | Req | 1,N | networkID |  |
| Assertion | RDNSequenceItem | RetrieveAttributesByTroubleReportIdRequest.TargetObjectName.DistinguishedName | 3 | AN | Req | 1,N | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) |  |
| Type | RDNSequenceItem | RetrieveAttributesByTroubleReportIdRequest.TargetObjectName.DistinguishedName | 11 | AN | Req | 1,N | accountName |  |
| Assertion | RDNSequenceItem | RetrieveAttributesByTroubleReportIdRequest.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,N | SC Account Name Value |  |
| Type | RDNSequenceItem | RetrieveAttributesByTroubleReportIdRequest.TargetObjectName.DistinguishedName | 15 | AN | Req | 1,N | troubleReportID |  |
| Assertion | RDNSequenceItem | RetrieveAttributesByTroubleReportIdRequest.TargetObjectName.DistinguishedName | 32 max | AN | Req | 1,N | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |
| AttributeIDItem | RetrieveAttributes | RetrieveAttributesByTroubleReportIdRequest | * | A | Opt | 0,1 | ActivityDuration AdditionalTroubleInfoList AdditionalTroubleStatusInfo AgentContactPerson ALocationAccessHours ALocationAccessAddress ALocationAccessPerson AuthorizationList CalledNumber CancelRequestedByManager CloseOutNarr CloseOutVerification CommitmentTime CommitmentTimeRequest CustomerTroubleTickNum CustomerWorkCenter EscalationList InitiatingMode ManagedObjectAccessHours ManagedObjectInstance ManagedObjectInstanceAliasList ManagerContactPerson OutageDuration PerceivedTroubleSeverity PreferredPriority ReceivedTime RepeatReport RestoredTime (continued on next page) | At least one AttributeIDItem under RetrieveAttributes must be present. Multiple AttributeIDItem tags can be requested. Cannot have duplicate valid entries with same AttributeIDItem contents. This note applicable to the rest of this table down below. |
| AttributeIDItem |  |  |  |  |  |  | (continued) TroubleClearancePerson TroubleDetectionTime TroubleFound TroubleReportState TroubleReportStatus TroubleReportStatusTime TroubleReportStatusWindow TroubleType TspPriority |  |

Table 17.  Retrieve Trouble Report Attributes Response

| tML Retrieve Trouble Report Attributes Response |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | RetrieveAttributesByTroubleReportIdResponse | 36 Max. | AN | Req | 1,1 |  | Create request correlation id |
| Type | RDNSequenceItem | RetrieveAttributesByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | RetrieveAttributesByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 3 | AN | Req | 1,1 | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) |  |
| Type | RDNSequenceItem | RetrieveAttributesByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | RetrieveAttributesByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | RetrieveAttributesByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 15 | AN | Req | 1,1 | troubleReportID |  |
| Assertion | RDNSequenceItem | RetrieveAttributesByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 32 Max | AN | Req | 1,1 | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |
| Day | Duration | RetrieveAttributesByTroubleReportIdResponse.Normal.ActivityDuration.ActivityDurationItem | 2 max | N | Req | 1,1 | 0-31 |  |
| Hour | Duration | RetrieveAttributesByTroubleReportIdResponse.Normal.ActivityDuration.ActivityDurationItem | 2 max | N | Req | 1,1 | 0-23 |  |
| Minute | Duration | RetrieveAttributesByTroubleReportIdResponse.Normal.ActivityDuration.ActivityDurationItem | 2 max | N | Req | 1,1 | 0-59 |  |
| Second | Duration | RetrieveAttributesByTroubleReportIdResponse.Normal.ActivityDuration.ActivityDurationItem | 2 max | N | Req | 1,1 | 0-59 |  |
| Msec | Duration | RetrieveAttributesByTroubleReportIdResponse.Normal.ActivityDuration.ActivityDurationItem | 3 max | N | Req | 1,1 | 0-999 |  |
| Billable | ActivityDurationItem | RetrieveAttributesByTroubleReportIdResponse.Normal.ActivityDuration | 5 max | AN | Req | 1,1 | true false |  |
| AfterHoursRepair | Type | RetrieveAttributesByTroubleReportIdResponse.Normal.ActivityDuration.ActivityDurationItem | 5 max | AN | Req | 1,1 | true false |  |
| Standby | Type | RetrieveAttributesByTroubleReportIdResponse.Normal.ActivityDuration.ActivityDurationItem | 5 max | AN | Req | 1,1 | true false |  |
| AfterHoursStandby | Type | RetrieveAttributesByTroubleReportIdResponse.Normal.ActivityDuration.ActivityDurationItem | 5 max | AN | Req | 1,1 | true false |  |
| Test | Type | RetrieveAttributesByTroubleReportIdResponse.Normal.ActivityDuration.ActivityDurationItem | 5 max | AN | Req | 1,1 | true false |  |
| ManagerInitiatedTest | Type | RetrieveAttributesByTroubleReportIdResponse.Normal.ActivityDuration.ActivityDurationItem | 5 max | AN | Req | 1,1 | true false |  |
| Dispatch | Type | RetrieveAttributesByTroubleReportIdResponse.Normal.ActivityDuration.ActivityDurationItem | 5 max | AN | Req | 1,1 | true false |  |
| NoAccess | Type | RetrieveAttributesByTroubleReportIdResponse.Normal.ActivityDuration.ActivityDurationItem | 5 max | AN | Req | 1,1 | true false |  |
| DelayedMaintenance | Type | RetrieveAttributesByTroubleReportIdResponse.Normal.ActivityDuration.ActivityDurationItem | 5 max | AN | Req | 1,1 | true false |  |
| Release | Type | RetrieveAttributesByTroubleReportIdResponse.Normal.ActivityDuration.ActivityDurationItem | 5 max | AN | Req | 1,1 | true false |  |
| DeregulatedWork | Type | RetrieveAttributesByTroubleReportIdResponse.Normal.ActivityDuration.ActivityDurationItem | 5 max | AN | Req | 1,1 | true false |  |
|  |  | RetrieveAttributesByTroubleReportIdResponse.Normal |  |  |  |  |  | The appearance of retrieved attribute(s) list under RetrieveAttributesByTroubleReportIdResponse.Normal depending on the attribute entry list in request XML. The structure(s) of the retrieved attribute(s) will depend on original attribute value layouts in request/response XMLs, and event notification XML(s). If a retrieved attribute has no value associated with it (the attribute value has never been set by either manager or agent), the attribute will not appear under RetrieveAttributesByTroubleReportIdResponse.Normal aggregate section, and instead it will appear as one of entry under RetrieveAttributesByTroubleReportIdResponse.Exception.MissingData.ExceptionList. This is a special case which should not be treated as an “error”. The above notes applicable to the rest of this table down below. |
| AdditionalTroubleInfoItem | AdditionalTroubleInfoList | RetrieveAttributesByTroubleReportIdResponse.Normal | 256 Max | AN | Req | 1,N |  | Retrieved multiple AdditionalTroubleInfoItem may not maintain the original order as they were originally provided based transactional timestamp Content in AdditionalTroubleInfoList will be concatenated under one AdditionalTroubleInfoItem for a particular request (whether it is create and modification) – even though the original request may have multiple AdditionalTroubleInfoItems under AdditionalTroubleInfoList |
| AdditionalTroubleStatusInfoItem | AdditionalTroubleStatusInfo | RetrieveAttributesByTroubleReportIdResponse.Normal | 256 max | AN | Opt | 0,N |  | Retrieved multiple AdditionalTroubleStatusInfoItem may not maintain the original order as they were originally provided based transactional timestamp |
| Name | AgentContactPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Req | 1,1 |  |  |
| Phone | AgentContactPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal.AgentContactPerson | 64 Max | AN | Req | 1,1 |  |  |
| City | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal.AgentContactPerson | 64 Max | AN | Req | 1,1 |  |  |
| State | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal.AgentContactPerson | 64 Max | AN | Req | 1,1 |  |  |
| Zip | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal.AgentContactPerson | 64 Max | N | Req | 1,1 |  |  |
| Email | AgentContactPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | AgentContactPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | AgentContactPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | AgentContactPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| PremisesName | ALocationAccessAddress | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Req | 1.1 |  |  |
| CivicAddress | PremisesAddress | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessAddress | 64 Max | AN | Req | 1,1 |  |  |
| City | PremisesAddress | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessAddress | 64 Max | AN | Req | 1,1 |  |  |
| State | PremisesAddress | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessAddress | 64 Max | AN | Req | 1,1 |  |  |
| Zip | PremisesAddress | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessAddress | 64 Max | N | Req | 1,1 |  |  |
| Sunday | DaysOfWeek | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Req | 1,1 | true false | Retrieved multiple LocationAccessHoursItem may not maintain the original order as they were originally provided based transactional timestamp |
| Monday | DaysOfWeek | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Tuesday | DaysOfWeek | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Wednesday | DaysOfWeek | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Thursday | DaysOfWeek | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Friday | DaysOfWeek | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Saturday | DaysOfWeek | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| IntervalStart | IntervalsOfDayItem | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem . IntervalsOfDay | 8 | AN | Req | 1,n |  | Premises' Local Time Military Format: HH:MM:SS |
| IntervalEnd | IntervalsOfDayItem | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem . IntervalsOfDay | 8 | AN | Req | 1,n |  | Premises' Local Time Military Format: HH:MM:SS |
| Name | ALocationAccessPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Req | 1,1 |  |  |
| Phone | ALocationAccessPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 18 | AN | Req | 1,1 |  |  |
| CivicAddress | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessPerson | 64 Max | AN | Opt | 0,1 |  |  |
| City | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessPerson | 64 Max | AN | Opt | 0,1 |  |  |
| State | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessPerson | 64 Max | AN | Opt | 0,1 |  |  |
| Zip | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. ALocationAccessPerson | 64 Max | N | Opt | 0,1 |  |  |
| Email | ALocationAccessPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | ALocationAccessPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | ALocationAccessPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | ALocationAccessPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| State | AuthorizationItem | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList | 1 | N | Req | 1,1 |  |  |
| AfterHoursRepair | Type | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false | Retrieved multiple AuthorizationItem may not maintain the original order as they were originally provided based transactional timestamp |
| Standby | Type | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| AfterHoursStandby | Type | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| Test | Type | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| ManagerInitiatedTest | Type | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| Dispatch | Type | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| NoAccess | Type | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| DelayedMaintenance | Type | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| Release | Type | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| DeregulatedWork | Type | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| AuthTime | AuthorizationItem | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList | 14 - 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Name | AuthPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem | 64 Max | AN | Req | 1,1 |  |  |
| Phone | AuthPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem.AuthPerson | 64 Max | AN | Opt | 0,1 |  |  |
| City | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem.AuthPerson | 64 Max | AN | Opt | 0,1 |  |  |
| State | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem.AuthPerson | 64 Max | AN | Opt | 0,1 |  |  |
| Zip | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem.AuthPerson | 64 Max | AN | Opt | 0,1 |  |  |
| Email | AuthPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | AuthPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | AuthPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | AuthPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. AuthorizationList. AuthorizationItem | 64 Max | AN | Opt | 0,1 |  |  |
| CalledNumber | Normal | RetrieveAttributesByTroubleReportIdResponse | 64 Max | N | Opt | 0,1 |  |  |
| CancelRequestedByManager | Normal | RetrieveAttributesByTroubleReportIdResponse | 5 Max | A | Opt | 0,1 | true false |  |
| CloseOutNarr | Normal | RetrieveAttributesByTroubleReportIdResponse | 256 Max | AN | Opt | 0,1 |  |  |
| CloseOutVerification | Normal | RetrieveAttributesByTroubleReportIdResponse | 1 | N | Opt | 0,1 |  |  |
| OnsiteTime | CommitmentTimeRequest | RetrieveAttributesByTroubleReportIdResponse.Normal | 14 - 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| CustomerTroubleTickNum | Normal | RetrieveAttributesByTroubleReportIdResponse | 64 Max | AN | Opt | 0,1 |  |  |
| CustomerWorkCenter | Normal | RetrieveAttributesByTroubleReportIdResponse | 64 Max | AN | Opt | 0,1 |  |  |
| State | EscalationItem | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList | 1 | N | Req | 1,1 | 1 |  |
| EscTime | EscalationItem | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList | 14 - 20 | AN | Req | 1,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Name | RequestPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem | 64 Max | AN | Req | 1,1 |  | Retrieved multiple EscalationItem may not maintain the original order as they were originally provided based transactional timestamp |
| Phone | RequestPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem. RequestPerson | 64 Max | AN | Opt | 0,1 |  |  |
| City | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem. RequestPerson | 64 Max | AN | Opt | 0,1 |  |  |
| State | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem. RequestPerson | 64 Max | AN | Opt | 0,1 |  |  |
| Zip | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem. RequestPerson | 64 Max | N | Opt | 0,1 |  |  |
| Email | RequestPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | RequestPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | RequestPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | RequestPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Level | EscalationItem | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList | 1 | N | Opt | 0,1 |  |  |
| Name | EscPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Phone | EscPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem. EscPerson | 64 Max | AN | Opt | 0,1 |  |  |
| City | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem. EscPerson | 64 Max | AN | Opt | 0,1 |  |  |
| State | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem. EscPerson | 64 Max | AN | Opt | 0,1 |  |  |
| Zip | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem. EscPerson | 64 Max | N | Opt | 0,1 |  |  |
| Email | EscPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | EscPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | EscPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | EscPerson | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 |  |  |
| InitiatingMode | Normal | RetrieveAttributesByTroubleReportIdResponse | 1 | N | Opt | 0,1 |  |  |
| Sunday | DaysOfWeek | RetrieveAttributesByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Req | 1,1 | true false | Retrieved multiple ManagedObjectAccessHoursItem may not maintain the original order as they were originally provided based transactional timestamp |
| Monday | DaysOfWeek | RetrieveAttributesByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Tuesday | DaysOfWeek | RetrieveAttributesByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Wednesday | DaysOfWeek | RetrieveAttributesByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Thursday | DaysOfWeek | RetrieveAttributesByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Friday | DaysOfWeek | RetrieveAttributesByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Saturday | DaysOfWeek | RetrieveAttributesByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| IntervalStart | IntervalsOfDayItem | RetrieveAttributesByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem. IntervalsOfDay | 8 | AN | Req | 1,1 |  | Local time in HH:MM:SS format |
| IntervalEnd | IntervalsOfDayItem | RetrieveAttributesByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem. IntervalsOfDay | 8 | AN | Req | 1,1 |  | Local time in HH:MM:SS format |
| ManagedObjectInstanceAliasItem | ManagedObjectInstanceAliasList | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 |  | Retrieved multiple ManagedObjectInstanceAliasItem may not maintain the original order as they were originally provided based transactional timestamp |
| Name | ManagerContactPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Req | 1,1 |  |  |
| Phone | ManagerContactPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 18 | AN | Req | 1,1 |  |  |
| CivicAddress | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. ManagerContactPerson | 64 Max | AN | Opt | 0,1 |  |  |
| City | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. ManagerContactPerson | 64 Max | AN | Opt | 0,1 |  |  |
| State | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. ManagerContactPerson | 64 Max | AN | Opt | 0,1 |  |  |
| Zip | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal. ManagerContactPerson | 64 Max | N | Opt | 0,1 |  |  |
| Email | ManagerContactPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | ManagerContactPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | ManagerContactPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | ManagerContactPerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| Day | TimeInterval | RetrieveAttributesByTroubleReportIdResponse.Normal.OutageDuration | 2 max | N | Req | 1,1 | 0-31 |  |
| Hour | TimeInterval | RetrieveAttributesByTroubleReportIdResponse.Normal.OutageDuration | 2 max | N | Req | 1,1 | 0-23 |  |
| Minute | TimeInterval | RetrieveAttributesByTroubleReportIdResponse.Normal.OutageDuration | 2 max | N | Req | 1,1 | 0-59 |  |
| Second | TimeInterval | RetrieveAttributesByTroubleReportIdResponse.Normal.OutageDuration | 2 max | N | Req | 1,1 | 0-59 |  |
| Msec | TimeInterval | RetrieveAttributesByTroubleReportIdResponse.Normal.OutageDuration | 3 max | N | Req | 1,1 | 0-999 |  |
| Number | PerceivedTroubleSeverity | RetrieveAttributesByTroubleReportIdResponse.Normal | 1 | N | Opt | 0,1 |  |  |
| PreferredPriority | Normal | RetrieveAttributesByTroubleReportIdResponse | 1 | N | Opt | 0,1 |  |  |
| ReceivedTime | Normal | RetrieveAttributesByTroubleReportIdResponse | 14 – 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| RepeatReport | Normal | RetrieveAttributesByTroubleReportIdResponse | 1 | N | Opt | 0,1 |  |  |
| RestoredTime | Normal | RetrieveAttributesByTroubleReportIdResponse | 14 – 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Name | TroubleClearancePerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 max | N | Req | 1,1 |  |  |
| Phone | TroubleClearancePerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal.TroubleClearancePerson | 64 max | AN | Opt | 0,1 |  |  |
| City | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal.TroubleClearancePerson | 64 max | AN | Opt | 0,1 |  |  |
| State | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal.TroubleClearancePerson | 64 max | AN | Opt | 0,1 |  |  |
| Zip | Loc | RetrieveAttributesByTroubleReportIdResponse.Normal.TroubleClearancePerson | 64 max | N | Opt | 0,1 |  |  |
| Email | TroubleClearancePerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 max | AN | Opt | 0,1 |  |  |
| Fax | TroubleClearancePerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 max | AN | Opt | 0,1 |  |  |
| Respon | TroubleClearancePerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 max | AN | Opt | 0,1 |  |  |
| Pager | TroubleClearancePerson | RetrieveAttributesByTroubleReportIdResponse.Normal | 64 max | AN | Opt | 0,1 |  |  |
| TroubleDetectionTime | Normal | RetrieveAttributesByTroubleReportIdResponse | 14 - 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Number | TroubleFound | RetrieveAttributesByTroubleReportIdResponse.Normal | 2 Max | N | Opt | 0,1 |  |  |
| TroubleReportState | Normal | RetrieveAttributesByTroubleReportIdResponse | 1 | N | Opt | 0,1 |  |  |
| Number | TroubleReportStatus | RetrieveAttributesByTroubleReportIdResponse.Normal | 3 max | N | Opt | 0,1 |  |  |
| TroubleReportStatusTime | Normal | RetrieveAttributesByTroubleReportIdResponse | 14 – 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Day | TroubleReportStatusWindow | RetrieveAttributesByTroubleReportIdResponse.Normal | 2 Max | N | Req | 1,1 |  |  |
| Hour | TroubleReportStatusWindow | RetrieveAttributesByTroubleReportIdResponse.Normal | 2 Max | N | Req | 1,1 |  |  |
| Minute | TroubleReportStatusWindow | RetrieveAttributesByTroubleReportIdResponse.Normal | 2 Max | N | Req | 1,1 |  |  |
| Second | TroubleReportStatusWindow | RetrieveAttributesByTroubleReportIdResponse.Normal | 2 Max | N | Opt | 0,1 |  |  |
| Msec | TroubleReportStatusWindow | RetrieveAttributesByTroubleReportIdResponse.Normal | 3 Max | N | Opt | 0,1 |  |  |
| Number | TroubleType | RetrieveAttributesByTroubleReportIdResponse.Normal | 4 Max | N | Opt | 0,1 |  |  |
| TspPriority | Normal | RetrieveAttributesByTroubleReportIdResponse | 2 | AN | Opt | 0,1 |  | TSP = Telecom Service Priority |

Table 18.  Retrieve Trouble Report Attributes Response - Exception

| tML Retrieve Trouble Report Attributes Response |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | RetrieveAttributesByTroubleReportIdResponse | 36 max | AN | Req | 1,1 |  |  |
| Type | RDNSequenceItem | RetrieveAttributesByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | RetrieveAttributesByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,1 | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) |  |
| Type | RDNSequenceItem | RetrieveAttributesByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | RetrieveAttributesByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | RetrieveAttributesByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 15 | AN | Req | 1,1 | troubleReportID |  |
| Assertion | RDNSequenceItem | RetrieveAttributesByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 64 max | AN | Req | 1,1 | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |
|  |  | RetrieveAttributesByTroubleReportIdResponse.Exception |  |  |  |  |  | The following aggregates: AccessDenied ResourceLimitation InvalidDataReceived ProcessingFailure NotFound MissingData are all optional under RetrieveAttributesByTroubleReportIdResponse.Exception If any one of above aggregates is present, then at least one ExceptionList should be present for that aggregate, and multiple ExceptionList entries can be present. If a retrieved attribute has no value associated with it (the attribute value has never been set by either manager or agent), the attribute will not appear under RetrieveAttributesByTroubleReportIdResponse.Normal aggregate section, and instead it will appear as one of entry under RetrieveAttributesByTroubleReportIdResponse.Exception.MissingData.ExceptionList. This is a special case which should not be treated as an “error”. |
| Tag | ExceptionList | RetrieveAttributesByTroubleReportIdResponse. Exception.AccessDenied | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | RetrieveAttributesByTroubleReportIdResponse. Exception.AccessDenied | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | RetrieveAttributesByTroubleReportIdResponse. Exception.ResourceLimitation | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | RetrieveAttributesByTroubleReportIdResponse. Exception.ResourceLimitation | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | RetrieveAttributesByTroubleReportIdResponse. Exception.InvalidDataReceived | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | RetrieveAttributesByTroubleReportIdResponse. Exception.InvalidDataReceived | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | RetrieveAttributesByTroubleReportIdResponse. Exception.ProcessingFailure | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | RetrieveAttributesByTroubleReportIdResponse. Exception.ProcessingFailure | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | RetrieveAttributesByTroubleReportIdResponse. Exception.NotFound | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | RetrieveAttributesByTroubleReportIdResponse. Exception.NotFound | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | RetrieveAttributesByTroubleReportIdResponse. Exception.MissingData | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | RetrieveAttributesByTroubleReportIdResponse. Exception.MissingData | * | AN | Req | 1,1 |  | Error message |

## Trouble Report AVC Event Notification

Table 19.  Trouble Report AVC Event Notification

| tML AVC Event Notification |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| NotificationId | NotificationId | AttributeValueChangeNotification | 36 max | AN | Req | 1,1 |  |  |
| EventTime | EventTime | AttributeValueChangeNotification | 14 – 20 | AN | Req | 1,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Type | RDNSequenceItem | AttributeValueChangeNotification.TargetObjectName.DistinguishedName | 9 | AN | Req | 1,N | networkID |  |
| Assertion | RDNSequenceItem | AttributeValueChangeNotification.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,N | SP Network ID Value |  |
| Type | RDNSequenceItem | AttributeValueChangeNotification.TargetObjectName.DistinguishedName | 11 | AN | Req | 1,N | accountName |  |
| Assertion | RDNSequenceItem | AttributeValueChangeNotification.TargetObjectName.DistinguishedName | 3 | AN | Req | 1,N | SC Account Name Value |  |
| Type | RDNSequenceItem | AttributeValueChangeNotification.TargetObjectName.DistinguishedName | 15 | AN | Req | 1,N | troubleReportID |  |
| Assertion | RDNSequenceItem | AttributeValueChangeNotification.TargetObjectName.DistinguishedName | 32 max | AN | Req | 1,N | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |
|  |  | AttributeValueChangeNotification.EventData |  |  |  |  |  | One Tag under the Parent Aggregate “Event Data” is required per Valid Entry At least one Tag must be requested Multiple Tags can be requested. |
|  | ActivityDurationList |  |  |  | Opt |  |  |  |
| Day | Duration | AttributeValueChangeNotification.EventData.ActivityDurationList.ActivityDurationItem | 2 max | N | Cond/Req | 1,1 | 0-31 | ActivityDuration aggregate is optional |
| Hour | Duration | AttributeValueChangeNotification.EventData.ActivityDurationList.ActivityDurationItem | 2 max | N | Cond/Req | 1,1 | 0-23 |  |
| Minute | Duration | AttributeValueChangeNotification.EventData.ActivityDuration.ActivityDurationItem | 2 max | N | Cond/Req | 1,1 | 0-59 |  |
| Second | Duration | AttributeValueChangeNotification.EventData.ActivityDurationList.ActivityDurationItem | 2 max | N | Cond/Req | 1,1 | 0-59 |  |
| Msec | Duration | AttributeValueChangeNotification.EventData.ActivityDurationList.ActivityDurationItem | 3 max | N | Cond/Req | 1,1 | 0-999 |  |
| Billable | ActivityDurationItem | AttributeValueChangeNotification.EventData.ActivityDurationList.ActivityDurationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| AfterHoursRepair | Type | AttributeValueChangeNotification.EventData.ActivityDurationList.ActivityDurationItem | * | A | Cond/Req | 1,1 | true false | Type aggregate is optional |
| Standby | Type | AttributeValueChangeNotification.EventData.ActivityDurationList.ActivityDurationItem | * | A | Cond/Req | 1,1 | true false |  |
| AfterHoursStandby | Type | AttributeValueChangeNotification.EventData.ActivityDurationList.ActivityDurationItem | * | A | Cond/Req | 1,1 | true false |  |
| Test | Type | AttributeValueChangeNotification.EventData.ActivityDurationList.ActivityDurationItem | * | A | Cond/Req | 1,1 | true false |  |
| ManagerInitiatedTest | Type | AttributeValueChangeNotification.EventData.ActivityDurationList.ActivityDurationItem | * | A | Cond/Req | 1,1 | true false |  |
| Dispatch | Type | AttributeValueChangeNotification.EventData.ActivityDurationList.ActivityDurationItem | * | A | Cond/Req | 1,1 | true false |  |
| NoAccess | Type | AttributeValueChangeNotification.EventData.ActivityDurationList.ActivityDurationItem | * | A | Cond/Req | 1,1 | true false |  |
| DelayedMaintenance | Type | AttributeValueChangeNotification.EventData.ActivityDurationList.ActivityDurationItem | * | A | Cond/Req | 1,1 | true false |  |
| Release | Type | AttributeValueChangeNotification.EventData.ActivityDurationList.ActivityDurationItem | * | A | Cond/Req | 1,1 | true false |  |
| DeregulatedWork | Type | AttributeValueChangeNotification.EventData.ActivityDurationList.ActivityDurationItem | * | A | Cond/Req | 1,1 | true false |  |
|  | AdditionalTroubleStatusInfo |  |  |  | Opt |  |  |  |
| AdditionalTroubleStatusInfoItem | AdditionalTroubleStatusInfo | AttributeValueChangeNotification.EventData | 256 max | AN | Cond/Req | 1,N |  | AdditionalTroubleStatusInfo aggregate is optional In an AVC message associated with a successful Trouble Report Create, AdditionalTroubleStatusInfo tag may carry Facility Equipment Provisioned (FEP) information at the very beginning of this field with either "FEP::=Copper" or "FEP::=Fiber" in addition to other information pertaining AdditionalTroubleStatusInfo if present at the time (The AVC message associated with a successful Trouble Report Create is identified with the presence of TroubleReportState=1, TroubleReportStatus=8, and TroubleReportStatusTime). |
| State | AuthorizationItem | AttributeValueChangeNotification.EventData.AuthorizationList | 1 | N | Cond/Req | 1,1 | 1 2 3 | AuthorizationList aggregate is optional 1 – requested 2 – provided 3 – denied Previously provided (State = 2) and/or denied (State = 3) Activity Type as well as authorization time/person information may be present in separate AuthorizationItem(s) as they were initially entered through Trouble Report Modification request or Trouble Report Creation request |
| AfterHoursRepair | Type | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Standby | Type | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| AfterHoursStandby | Type | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Test | Type | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| ManagerInitiatedTest | Type | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Dispatch | Type | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| NoAccess | Type | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| DelayedMaintenance | Type | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| Release | Type | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| DeregulatedWork | Type | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem | 5 max | AN | Cond/Req | 1,1 | true false |  |
| AuthTime | AuthorizationItem | AttributeValueChangeNotification.EventData.AuthorizationList | 14-20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ AuthTime associated with previously provided (State = 2) and/or denied (State = 3) may be present in separate AuthorizationItem(s) as they were initially entered through Trouble Report Modification request or Trouble Report Creation request |
| Name | AuthPerson | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem | 64 max | AN | Cond/Req | 1,1 |  | AuthPerson associated with previously provided (State = 2) and/or denied (State = 3) may be present in separate AuthorizationItem(s) as they were initially entered through Trouble Report Modification request or Trouble Report Creation request. |
| Phone | AuthPerson | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem.AuthPerson | 64 max | N | Opt | 0,1 |  |  |
| City | Loc | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem.AuthPerson | 64 max | AN | Opt | 0,1 |  |  |
| State | Loc | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem.AuthPerson | 64 max | AN | Opt | 0,1 |  |  |
| Zip | Loc | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem.AuthPerson | 64 max | N | Opt | 0,1 |  |  |
| Email | AuthPerson | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem | 64 max | AN | Opt | 0,1 |  |  |
| Fax | AuthPerson | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem | 64 max | AN | Opt | 0,1 |  |  |
| Respon | AuthPerson | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem | 64 max | AN | Opt | 0,1 |  |  |
| Pager | AuthPerson | AttributeValueChangeNotification.EventData.AuthorizationList.AuthorizationItem | 64 max | AN | Opt | 0,1 |  |  |
| CloseOutNarr | EventData | AttributeValueChangeNotification | 256 max | AN | Opt | 0,1 |  |  |
|  | CommitmentTime |  |  |  | Opt |  |  |  |
| OnsiteTime | CommitmentTime | AttributeValueChangeNotification.EventData | 14 - 20 | AN | Cond/Req | 1,1 |  | CommitmentTime aggregate is optional. GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ Updated CommitmentTimes may be provided for local customers only. It may not be provided for access customers. |
|  | EscalationList |  |  |  | Opt |  |  |  |
| State | EscalationItem | AttributeValueChangeNotification.EventData.EscalationList | 1 | N | Cond/Req | 1,1 | 2 3 | EscalationList aggregate is optional 2 – provided 3 – denied |
| EscTime | EscalationItem | AttributeValueChangeNotification.EventData.EscalationList | 14-20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Level | EscalationItem | AttributeValueChangeNotification.EventData.EscalationList | 1 | N | Opt | 0,1 | 1 2 3 4 | 1 - first-level 2 - second-level 3 - third-level 4 - fourth-level |
|  | EscPerson |  |  |  | Opt |  |  |  |
| Name | EscPerson | AttributeValueChangeNotification.EventData.EscalationList.EscalationItem | 64 max | AN | Cond/Req | 1,1 |  |  |
| Phone | EscPerson | AttributeValueChangeNotification.EventData.EscalationList.EscalationItem | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | AttributeValueChangeNotification.EventData.EscalationList.EscalationItem.EscPerson | 64 max | N | Opt | 0,1 |  |  |
| City | Loc | AttributeValueChangeNotification.EventData.EscalationList.EscalationItem.EscPerson | 64 max | AN | Opt | 0,1 |  |  |
| State | Loc | AttributeValueChangeNotification.EventData.EscalationList.EscalationItem.EscPerson | 64 max | AN | Opt | 0,1 |  |  |
| Zip | Loc | AttributeValueChangeNotification.EventData.EscalationList.EscalationItem.EscPerson | 64 max | N | Opt | 0,1 |  |  |
| Email | EscPerson | AttributeValueChangeNotification.EventData.EscalationList.EscalationItem | 64 max | AN | Opt | 0,1 |  |  |
| Fax | EscPerson | AttributeValueChangeNotification.EventData.EscalationList.EscalationItem | 64 max | AN | Opt | 0,1 |  |  |
| Respon | EscPerson | AttributeValueChangeNotification.EventData.EscalationList.EscalationItem | 64 max | AN | Opt | 0,1 |  |  |
| Pager | EscPerson | AttributeValueChangeNotification.EventData.EscalationList.EscalationItem | 64 max | AN | Opt | 0,1 |  |  |
|  | OutageDuration |  |  |  | Opt |  |  |  |
| Day | TimeInterval | AttributeValueChangeNotification.EventData.OutageDuration | 2 max | N | Cond/Req | 1,1 | 0-31 | OutageDuration aggregate is optional |
| Hour | TimeInterval | AttributeValueChangeNotification.EventData.OutageDuration | 2 max | N | Cond/Req | 1,1 | 0-23 |  |
| Minute | TimeInterval | AttributeValueChangeNotification.EventData.OutageDuration | 2 max | N | Cond/Req | 1,1 | 0-59 |  |
| Second | TimeInterval | AttributeValueChangeNotification.EventData.OutageDuration | 2 max | N | Cond/Req | 1,1 | 0-59 |  |
| Msec | TimeInterval | AttributeValueChangeNotification.EventData.OutageDuration | 3 max | N | Cond/Req | 1,1 | 0-999 |  |
| RestoredTime | EventData | AttributeValueChangeNotification | 14 – 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Number | TroubleFound | AttributeValueChangeNotification.EventData | 2 max | N | Opt | 0,1 | [Valid values can be found in the T1 227 document] |  |
| TroubleReportState | Event Data | AttributeValueChangeNotification | 1 | N | Opt | 0,1 |  |  |
| Number | TroubleReportStatus | AttributeValueChangeNotification.EventData | 3 max | N | Opt | 0,1 |  |  |
| TroubleReportStatusTime | EventData | AttributeValueChangeNotification | 14 – 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |

## Trouble Report Close Out Notification

Table 20.  Trouble Report Close Out Notification

| tML Trouble Report Close Out Notification |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| NotificationId | NotificationId | AttributeValueChangeNotification | 36 max | AN | Req | 1,1 |  |  |
| EventTime | EventTime | AttributeValueChangeNotification | 14 – 20 | AN | Req | 1,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Type | RDNSequenceItem | AttributeValueChangeNotification.TargetObjectName.DistinguishedName | 9 | AN | Req | 1,N | networkID |  |
| Assertion | RDNSequenceItem | AttributeValueChangeNotification.TargetObjectName.DistinguishedName | 3 | AN | Req | 1,N | SP Network ID Value |  |
| Type | RDNSequenceItem | AttributeValueChangeNotification.TargetObjectName.DistinguishedName | 11 | AN | Req | 1,N | accountName |  |
| Assertion | RDNSequenceItem | AttributeValueChangeNotification.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,N | SC Account Name Value |  |
| Type | RDNSequenceItem | AttributeValueChangeNotification.TargetObjectName.DistinguishedName | 15 | AN | Req | 1,N | troubleReportID |  |
| Assertion | RDNSequenceItem | AttributeValueChangeNotification.TargetObjectName.DistinguishedName | 32 max | AN | Req | 1,N | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |
|  |  | AttributeValueChangeNotification.EventData |  |  |  |  |  | One Tag under the Parent Aggregate “Event Data” is required per Valid Entry At least one Tag must be requested Multiple Tags can be requested. |
| CloseOutNarr | EventData | AttributeValueChangeNotification | 256 max | AN | Req | 1,1 |  |  |
|  | OutageDuration |  |  |  | Opt |  |  |  |
| Day | TimeInterval | AttributeValueChangeNotification.EventData.OutageDuration | 2 max | N | Cond/Req | 1,1 | 0-31 |  |
| Hour | TimeInterval | AttributeValueChangeNotification.EventData.OutageDuration | 2 max | N | Cond/Req | 1,1 | 0-23 |  |
| Minute | TimeInterval | AttributeValueChangeNotification.EventData.OutageDuration | 2 max | N | Cond/Req | 1,1 | 0-59 |  |
| Second | TimeInterval | AttributeValueChangeNotification.EventData.OutageDuration | 2 max | N | Cond/Req | 1,1 | 0-59 |  |
| Msec | TimeInterval | AttributeValueChangeNotification.EventData.OutageDuration | 3 max | N | Cond/Req | 1,1 | 0-999 |  |
| RestoredTime | EventData | AttributeValueChangeNotification | 14 – 20 | AN | Req | 1,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Number | TroubleFound | AttributeValueChangeNotification.EventData | 2 max | N | Req | 1,1 | [Valid values can be found in the T1 227 document] |  |
| TroubleReportState | Event Data | AttributeValueChangeNotification | 1 | N | Req | 1,1 | 3 |  |
| Number | TroubleReportStatus | AttributeValueChangeNotification.EventData | 3 max | N | Req | 1,1 | 24, 25, 26 |  |
| TroubleReportStatusTime | EventData | AttributeValueChangeNotification | 14 – 20 | AN | Req | 1,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |

## Multiple Trouble Report Create

Table 21.  Multiple Trouble Report Create Request

| tML Multiple Trouble Report Create Request |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | MultiTroubleReportCreationRequest | 36 Max. | AN | Req | 1,1 |  | Create request correlation id |
| UserId | Customer | MultiTroubleReportCreationRequest | 10 | AN | Req | 1,1 |  | Refer to §7.3 for detailed informational. |
| ServiceProfile | Customer | MultiTroubleReportCreationRequest | 8 Max | AN | Req | 1,1 | RESELLER CLEC Carrier | “RESELLER” or “CLEC” for Verizon Local Customers “Carrier” for Verizon Access Customers |
| NameBindingId | NameBindingId | MultiTroubleReportCreationRequest | 20 | N | Opt | 0,1 | 1.2.840.10015.0.6.24 1.2.840.10015.0.6.25 1.2.840.10015.0.6.26 1.2.840.10015.0.6.27 | NameBindingId is an optional field. |
| Type | RDNSequenceItem | MultiTroubleReportCreationRequest.ManagedObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | MultiTroubleReportCreationRequest.ManagedObjectInstance. DistinguishedName | 5 | AN | Req | 1,1 | Assertion::= State value followed by SP Network ID Value. SP Network ID Value is either VZL, or VZC VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) | For example, a local customer would send an Assertion tag with the value NYVZL if the reported circuit id’s customer end is located in New York state. |
| Type | RDNSequenceItem | MultiTroubleReportCreationRequest.ManagedObjectInstance. DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | MultiTroubleReportCreationRequest.ManagedObjectInstance. DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | MultiTroubleReportCreationRequest.ManagedObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | serviceID |  |
| Assertion | RDNSequenceItem | MultiTroubleReportCreationRequest.ManagedObjectInstance. DistinguishedName | 64 Max | AN | Req | 1,1 | Service ID Value | Use an appropriate circuit id to populate this field – for definition of circuit ids, refer to Annex B Circuit Format Definition for Designed and Non-Designed Circuits |
| Number | TroubleType | MultiTroubleReportCreationRequest | 4 Max | N | Req | 1,1 |  |  |
| AdditionalTroubleInfoItem | AdditionalTroubleInfoList | MultiTroubleReportCreationRequest | 256 Max | AN | Req | 1,n |  | If a service test has been performed prior to a customer invoking a Trouble Report Create request for a given circuit and the customer would like Verizon to perform a desired dispatch option, the customer may place a text string with syntax of “TR <XX> <YY>” at the very beginning of the first instance of AdditionalTroubleInfoItem, where the exact contents of <XX> and <YY> are provided in Annex A TR <XX> <YY> Construction Rules |
| TroubleReportFormatId | AdditionalCreateInfo | MultiTroubleReportCreationRequest | 1 | N | Opt | 0,1 |  | Aggregate AdditionalCreateInfo is conditional – required when dealing with designed circuits with types of “S” (including “3”), “T”, “C” and “M”, not required for “P” type circuit (for detailed information regarding the circuit type for a given circuit, refer to Annex B Circuit Format Definition for Designed and Non-Designed Circuits). TroubleReportFormatId is an optional field. |
|  | AdditionalCircuitItem | MultiTroubleReportCreationRequest.AdditionalCircuitList |  |  | Req | 1,N |  |  |
| CircuitID | AdditionalCircuitItem | MultiTroubleReportCreationRequest.AdditionalCircuitList | 64 Max | AN | Req | 1,1 | Service ID Value | Use an appropriate circuit id to populate this field – for definition of circuit ids, refer to Annex B Circuit Format Definition for Designed and Non-Designed Circuits |
| MeetPoint | AdditionalCircuitItem | MultiTroubleReportCreationRequest.AdditionalCircuitList | 20 | AN | Opt | 0,1 |  |  |
| AssociatedTN | AdditionalCircuitItem | MultiTroubleReportCreationRequest.AdditionalCircuitList | 15 | AN | Opt | 0,1 |  |  |
| PremisesName | ALocationAccessAddress | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Req | 1.1 |  | Business Name ALocationAccessAddress is an optional field |
| CivicAddress | PremisesAddress | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessAddress | 64 Max | AN | Req | 1,1 |  |  |
| City | PremisesAddress | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessAddress | 64 Max | AN | Req | 1,1 |  |  |
| State | PremisesAddress | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessAddress | 64 Max | AN | Req | 1,1 |  |  |
| Zip | PremisesAddress | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessAddress | 64 Max | N | Req | 1,1 |  |  |
| Sunday | DaysOfWeek | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Req | 1,1 | true false | ALocationAccessHours is optional LocationAccessHoursItem can appear multiple times |
| Monday | DaysOfWeek | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Tuesday | DaysOfWeek | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Wednesday | DaysOfWeek | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Thursday | DaysOfWeek | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Friday | DaysOfWeek | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Saturday | DaysOfWeek | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| IntervalStart | IntervalsOfDayItem | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem . IntervalsOfDay | 8 | AN | Req | 1,n |  | Premises' Local Time Military Format: HH:MM:SS |
| IntervalEnd | IntervalsOfDayItem | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessHours. LocationAccessHoursItem . IntervalsOfDay | 8 | AN | Req | 1,n |  | Premises' Local Time Military Format: HH:MM:SS |
| Name | ALocationAccessPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Req | 1,1 |  | AlocationAccessPerson is optional |
| Phone | ALocationAccessPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 18 | AN | Req | 1,1 |  |  |
| CivicAddress | Loc | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessPerson | 64 Max | AN | Opt | 0,1 |  |  |
| City | Loc | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessPerson | 64 Max | AN | Opt | 0,1 |  |  |
| State | Loc | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessPerson | 64 Max | AN | Opt | 0,1 |  |  |
| Zip | Loc | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ALocationAccessPerson | 64 Max | N | Opt | 0,1 |  |  |
| Email | ALocationAccessPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | ALocationAccessPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | ALocationAccessPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | ALocationAccessPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 |  |  |
| State | AuthorizationItem | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList | 1 | N | Req | 1,1 | 2 3 | AuthorizationList is optional AuthorizationItem can appear multiple times 2 – provided 3 – denied Once an activity (Type) of authorization has been set to provided (State=2), it (Type) cannot be subsequently denied. |
| AfterHoursRepair | Type | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| Standby | Type | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| AfterHoursStandby | Type | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| Test | Type | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| ManagerInitiatedTest | Type | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| Dispatch | Type | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| NoAccess | Type | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| DelayedMaintenance | Type | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| Release | Type | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| DeregulatedWork | Type | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 5 Max | AN | Req | 1,1 | true false |  |
| AuthTime | AuthorizationItem | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList | 14 - 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Name | AuthPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 64 Max | AN | Req | 1,1 |  | AuthPerson aggregate is optional |
| Phone | AuthPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem.AuthPerson | 64 Max | AN | Opt | 0,1 |  |  |
| City | Loc | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem.AuthPerson | 64 Max | AN | Opt | 0,1 |  |  |
| State | Loc | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem.AuthPerson | 64 Max | AN | Opt | 0,1 |  |  |
| Zip | Loc | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem.AuthPerson | 64 Max | AN | Opt | 0,1 |  |  |
| Email | AuthPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | AuthPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | AuthPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | AuthPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo. AuthorizationList. AuthorizationItem | 64 Max | AN | Opt | 0,1 |  |  |
| CalledNumber | AdditionalCreateInfo | MultiTroubleReportCreationRequest | 64 Max | N | Opt | 0,1 |  |  |
| OnsiteTime | CommitmentTimeRequest | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 14 - 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ CommitmentTimeRequest will not be supported for Access Customers with designed circuits (type “3”, “S”, “T”, “C”, and “M”). |
| CustomerTroubleTickNum | AdditionalCreateInfo | MultiTroubleReportCreationRequest | 64 Max | AN | Opt | 0,1 |  |  |
| CustomerWorkCenter | AdditionalCreateInfo | MultiTroubleReportCreationRequest | 64 Max | AN | Opt | 0,1 |  |  |
| State | EscalationItem | MultiTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList | 1 | N | Req | 1,1 | 1 | EscalationList is optional 1 – requested |
| EscTime | EscalationItem | MultiTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList | 14 - 20 | AN | Req | 1,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Name | RequestPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem | 64 Max | AN | Req | 1,1 |  |  |
| Phone | RequestPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | MultiTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem. RequestPerson | 64 Max | AN | Opt | 0,1 |  |  |
| City | Loc | MultiTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem. RequestPerson | 64 Max | AN | Opt | 0,1 |  |  |
| State | Loc | MultiTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem. RequestPerson | 64 Max | AN | Opt | 0,1 |  |  |
| Zip | Loc | MultiTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem. RequestPerson | 64 Max | N | Opt | 0,1 |  |  |
| Email | RequestPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | RequestPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | RequestPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | RequestPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList.EscalationItem | 64 Max | AN | Opt | 0,1 |  |  |
| Level | EscalationItem | MultiTroubleReportCreationRequest.AdditionalCreateInfo. EscalationList | 1 | N | Opt | 0,1 | 0 1 | 0 - No Escalation 1 - first-level |
| Sunday | DaysOfWeek | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Req | 1,1 | true false | ManagedObjectAccessHours is optional for non-designed circuits. It is required for designed circuits. ManagedObjectAccessHoursItem can appear multiple times |
| Monday | DaysOfWeek | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Tuesday | DaysOfWeek | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Wednesday | DaysOfWeek | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Thursday | DaysOfWeek | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Friday | DaysOfWeek | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| Saturday | DaysOfWeek | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Req | 1,1 | true false |  |
| IntervalStart | IntervalsOfDayItem | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem. IntervalsOfDay | 8 | AN | Req | 1,1 |  | Local time in HH:MM:SS format |
| IntervalEnd | IntervalsOfDayItem | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ManagedObjectAccessHours. ManagedObjectAccessHoursItem.IntervalsOfDay | 8 | AN | Req | 1,1 |  | Local time in HH:MM:SS format |
| ManagedObjectInstanceAliasItem | ManagedObjectInstanceAliasList | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 |  |  |
| Name | ManagerContactPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Req | 1,1 |  | ManagerContactPerson is conditional – it is required for “S” (including “3”), “T”, “C” and “M” type circuits; not applicable for “P” type circuit. |
| Phone | ManagerContactPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 18 | AN | Req | 1,1 |  |  |
| CivicAddress | Loc | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ManagerContactPerson | 64 Max | AN | Opt | 0,1 |  |  |
| City | Loc | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ManagerContactPerson | 64 Max | AN | Opt | 0,1 |  |  |
| State | Loc | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ManagerContactPerson | 64 Max | AN | Opt | 0,1 |  |  |
| Zip | Loc | MultiTroubleReportCreationRequest.AdditionalCreateInfo. ManagerContactPerson | 64 Max | N | Opt | 0,1 |  |  |
| Email | ManagerContactPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | ManagerContactPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | ManagerContactPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | ManagerContactPerson | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 64 Max | AN | Opt | 0,1 |  |  |
| Number | PerceivedTroubleSeverity | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 1 | N | Opt | 0,1 | 0 1 2 3 | 0 – out of service 1 – back in service 2 – service impairment 3 – non service affecting trouble |
| PreferredPriority | AdditionalCreateInfo | MultiTroubleReportCreationRequest | 1 | N | Opt | 0,1 | 0 1 2 3 | 0 – undefined 1 – minor 2 – major 3 – serious |
| RepeatReport | AdditionalCreateInfo | MultiTroubleReportCreationRequest | 1 | N | Opt | 0,1 | 0 1 2 3 4 5 | 0 – unspecified 1 – recent installation 2 – repeat 3 – both installation & repeat 4 – chronic 5 – both installation & chronic |
| TroubleDetectionTime | AdditionalCreateInfo | MultiTroubleReportCreationRequest | 14 - 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Day | TroubleReportStatusWindow | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 2 Max | N | Req | 1,1 | From "0" to "31" | TroubleReportStatusWindow is optional |
| Hour | TroubleReportStatusWindow | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 2 Max | N | Req | 1,1 | From "0" to "23" |  |
| Minute | TroubleReportStatusWindow | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 2 Max | N | Req | 1,1 | From "0" to "59" |  |
| Second | TroubleReportStatusWindow | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 2 Max | N | Opt | 0,1 | From "0" to "59" |  |
| Msec | TroubleReportStatusWindow | MultiTroubleReportCreationRequest.AdditionalCreateInfo | 3 Max | N | Opt | 0,1 | From "0" to "999" |  |
| TspPriority | AdditionalCreateInfo | MultiTroubleReportCreationRequest | 2 | AN | Opt | 0,1 |  | TSP = Telecom Service Priority |

Table 22.  Multiple Trouble Report Create Response  (Normal)

| tML Multiple Trouble Report Create Response (Normal) |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | MultiTroubleReportCreationResponse | 36 Max | AN | Req | 1,1 |  | Create request correlation id |
| Type | RDNSequenceItem | MultiTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | MultiTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 5 | AN | Req | 1,1 | SP Network ID Value (First 2 chars will be state code and then remaining will be the last three characters mentioned below) VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) | First two characters will be the state code that was supplied in the create request. |
| Type | RDNSequenceItem | MultiTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | MultiTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | MultiTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 9 | AN | Req | 1,1 | serviceID |  |
| Assertion | RDNSequenceItem | MultiTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 64 Max | AN | Req | 1,1 | Service ID Value |  |
| InitiatingMode | Normal | MultiTroubleReportCreationResponseCreateResponse | 1 | N | Req | 1,1 | "0" |  |
| ReceivedTime | Normal | MultiTroubleReportCreationResponseCreateResponse | 14 - 20 | AN | Req | 1,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| TroubleReportId | Normal | MultiTroubleReportCreationResponse.CreateResponse | 32 Max | AN | Req | 1,1 |  | The maximum length supported by Verizon for TroubleReportId value is 18 characters |
| TroubleReportState | Normal | MultiTroubleReportCreationResponseCreateResponse | 1 | N | Req | 1,1 |  |  |
| Number | TroubleReportStatus | MultiTroubleReportCreationResponseCreateResponse.Normal | 3 Max | N | Req | 1,1 |  |  |
| TroubleReportStatusTime | Normal | MultiTroubleReportCreationResponseCreateResponse | 14 - 20 | AN | Req | 1,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| Name | AgentContactPerson | MultiTroubleReportCreationResponseCreateResponse.Normal | 64 Max | AN | Req | 1,1 |  | AgentContactPerson is conditional. For designed circuits owned by Access Carrier customers (type “3”, “S”, “T”, “C”, and “M”), the name of the work center that owns the trouble report as well we the center telephone number will be provided. |
| Phone | AgentContactPerson | MultiTroubleReportCreationResponseCreateResponse.Normal | 18 | AN | Opt | 0,1 |  |  |
| CivicAddress | Loc | MultiTroubleReportCreationResponseCreateResponse.Normal. AgentContactPerson | 64 Max | AN | Req | 1,1 |  | Loc is optional |
| City | Loc | MultiTroubleReportCreationResponseCreateResponse.Normal. AgentContactPerson | 64 Max | AN | Req | 1,1 |  |  |
| State | Loc | MultiTroubleReportCreationResponseCreateResponse.Normal. AgentContactPerson | 64 Max | AN | Req | 1,1 |  |  |
| Zip | Loc | MultiTroubleReportCreationResponseCreateResponse.Normal. AgentContactPerson | 64 Max | N | Req | 1,1 |  |  |
| Email | AgentContactPerson | MultiTroubleReportCreationResponseCreateResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | AgentContactPerson | MultiTroubleReportCreationResponseCreateResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | AgentContactPerson | MultiTroubleReportCreationResponseCreateResponse.Normal | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | AgentContactPerson | MultiTroubleReportCreationResponseCreateResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| OnsiteTime | CommitmentTime | MultiTroubleReportCreationResponseCreateResponse.Normal | 14 - 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ CommitmentTimes will not be provided on designed circuits owned by Access Carrier customers (type “3”, “S”, “T”, “C”, and “M”). As the trouble report process progresses, the Verizon center will provide estimated time to repair through AVC messages. |
|  | AdditionalTroubleTicketItem | MultiTroubleReportCreationResponseCreateResponse.Normal.AdditionalTroubleTicketList |  |  |  | 1,N |  |  |
| CircuitID | AdditionalTroubleTicketItem | MultiTroubleReportCreationResponseCreateResponse.Normal.AdditionalTroubleTicketList | 64 Max | AN | Req | 1,1 | Service ID Value | Use an appropriate circuit id to populate this field – for definition of circuit ids, refer to Annex B Circuit Format Definition for Designed and Non-Designed Circuits |
| TroubleReportID | AdditionalTroubleTicketItem | MultiTroubleReportCreationResponseCreateResponse.Normal. AdditionalTroubleTicketList | 32 Max | AN | Opt | 0,1 |  | The maximum length supported by Verizon for TroubleReportId value is 18 characters |
| OnsiteTime | CommitmentTime | MultiTroubleReportCreationResponseCreateResponse.Normal. AdditionalTroubleTicketList. AdditionalTroubleTicketItem | 14 - 20 | AN | Opt | 0,1 |  | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ CommitmentTimes will not be provided on designed circuits owned by Access Carrier customers (type “3”, “S”, “T”, “C”, and “M”). As the trouble report process progresses, the Verizon center will provide estimated time to repair through AVC messages. |
| ErrorCode | AdditionalTroubleTicketItem | MultiTroubleReportCreationResponseCreateResponse.Normal.AdditionalTroubleTicketList | 4 | AN | Opt | 0,1 |  | Error code |
| ErrorDescription | AdditionalTroubleTicketItem | MultiTroubleReportCreationResponseCreateResponse.Normal.AdditionalTicketInfoList | * | AN | Opt | 0,1 |  | Error message |

Table 23.  Multiple Trouble Report Create Response – Exception

| tML Multiple Trouble Report Create Response (Exception) |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | MultiTroubleReportCreationResponse | 36 Max | AN | Req | 1,1 |  | Create request correlation id |
| Type | RDNSequenceItem | MultiTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | MultiTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 4 | AN | Req | 1,1 | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) |  |
| Type | RDNSequenceItem | MultiTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | MultiTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | MultiTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 9 | AN | Req | 1,1 | serviceID |  |
| Assertion | RDNSequenceItem | MultiTroubleReportCreationResponse.TargetObjectName. DistinguishedName | 64 Max | AN | Req | 1,1 | Service ID Value |  |
| Type | RDNSequenceItem | MultiTroubleReportCreationResponseCreateResponse. Exception. TroubleReportAlreadyExists.ManagedObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | networkID | For further processing regarding TroubleReportAlreadyExists exception, please refer to Annex E Trouble Ticket Late Bonding |
| Assertion | RDNSequenceItem | MultiTroubleReportCreationResponseCreateResponse. Exception. TroubleReportAlreadyExists.ManagedObjectInstance. DistinguishedName | 4 | AN | Req | 1,1 | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) |  |
| Type | RDNSequenceItem | MultiTroubleReportCreationResponseCreateResponse. Exception. TroubleReportAlreadyExists.ManagedObjectInstance. DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | MultiTroubleReportCreationResponse.CreateResponse. Exception. TroubleReportAlreadyExists.ManagedObjectInstance. DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | MultiTroubleReportCreationResponse.CreateResponse. Exception. TroubleReportAlreadyExists.ManagedObjectInstance. DistinguishedName | 15 | AN | Req | 1,1 | troubleReportID |  |
| Assertion | RDNSequenceItem | MultiTroubleReportCreationResponse.CreateResponse. Exception. TroubleReportAlreadyExists.ManagedObjectInstance. DistinguishedName | 32 Max | AN | Req | 1,1 | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |
|  |  | MultiTroubleReportCreationResponse.CreateResponse. Exception |  |  |  |  |  | Every tag at aggregate level under “Exception” tag is optional. However, for an error response case, at least one aggregate will be present. The usage column merely indicates the child tag usage situation for a given aggregate. |
| AttributeIDItem | TRMustBePresentAttributeMissing | MultiTroubleReportCreationResponse.CreateResponse. Exception | * | AN | Req | 1,n |  | Req trouble report attribute name(s) |
| FallBackReporting | FallBackReporting | MultiTroubleReportCreationResponse.CreateResponse. Exception | * | AN | Req | 1,1 |  |  |
| Tag | ExceptionList | MultiTroubleReportCreationResponse.CreateResponse. Exception.AccessDenied | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | MultiTroubleReportCreationResponse.CreateResponse. Exception.AccessDenied | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | MultiTroubleReportCreationResponse.CreateResponse. Exception.ResourceLimitation | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | MultiTroubleReportCreationResponse.CreateResponse. Exception.ResourceLimitation | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | MultiTroubleReportCreationResponse.CreateResponse. Exception.InvalidDataReceived | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | MultiTroubleReportCreationResponse.CreateResponse. Exception.InvalidDataReceived | * | AN | Req | 1,1 |  | Error message |
| Tag | ExceptionList | MultiTroubleReportCreationResponseCreateResponse. Exception.ProcessingFailure | 4 | AN | Req | 1,1 |  | Error code |
| Value | ExceptionList | MultiTroubleReportCreationResponseCreateResponse. Exception.ProcessingFailure | * | AN | Req | 1,1 |  | Error message |

## Quick Test

This transaction facilitates testing on a non-POT circuit.   Successful response(s) to Quick Test Request are categorized into ResultType as “A” (Acknowledgement), “S” (Intermediate Status”),  “C” (final Completed).

This transaction is defined as an asynchronous transaction.

Table 24.  Quick Test Request

| tML Line Quick Test Request |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId |  | 36 max | AN | Req | 1,1 |  |  |
| UserId | Customer |  | 10 | AN | Req | 1,1 |  | Refer to §7.3 for detailed informational. |
| ServiceProfile | Customer |  | 16 max | AN | Req | 1,1 | Carrier |  |
| Type | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 5 | AN | Req | 1,1 | NYVZC NJVZC CAVZC … | Assertion::= State value followed by SP Network ID Value. SP Network ID Value is VZC |
| Type | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 4 | AN | Req | 1,1 | Account Name Value | This is used to validate digital certificate |
| Type | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | serviceID |  |
| Assertion | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 64 Max | AN | Req | 1,1 | Service ID Value | Circuit ID value, use “/” as delimiter |
| Acknowledgement |  |  |  |  | Opt | 0,1 | Y, N |  |
| StatusMessage |  |  |  |  | Opt | 0,1 | Y, N |  |
| FinalDetail |  |  |  |  | Opt | 0,1 | Y, N | . |
| JobType |  |  |  |  | Opt | 0,1 | JobType, valid values: M, A Comment: "A" = Automatic test; "M" = Manually initiated test; | If not present, Default to M |
| DispatchAuth |  |  |  |  | Opt | 0,1 | Y or N | If not present, Default to Y |

Table 25 Quick Test Response

| tML Quick Test Response |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId |  | 36 max | AN | Req | 1,1 |  |  |
| Type | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 5 | AN | Req | 1,1 | NYVZC NJVZC CAVZC … | Assertion::= State value followed by SP Network ID Value. SP Network ID Value is VZC. |
| Type | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 4 | AN | Req | 1,1 | Account Name Value | This is used to validate digital certificate |
| Type | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | serviceID |  |
| Assertion | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 64 Max | AN | Req | 1,1 | Service ID Value |  |
| ReturnCode |  | Normal |  |  | Req |  | 0000 = Completely successful. 0XXX = Partially successful. 1-9XXX = Error encountered |  |
| ResultType |  | Normal |  |  | Req |  | C=Complete E = Error X= Cancelled I = In complete/Partial results S = Status Message A=Ack message |  |
| InfoMessage |  | Normal |  |  | Opt | 0,1 |  |  |
| CircuitDescription | Status | Normal |  |  | Opt |  |  |  |
| SummaryStatus | Status | Normal |  |  | Opt |  |  |  |
| SummaryText | Status | Normal |  |  | Opt |  |  |  |
| Disposition | Status | Normal |  |  | Opt | 0,1 |  |  |
| DescriptorsNumber | Status.Descriptors | Normal |  |  | Cond | 1,1 | Number of Descriptiors | Required if Descriptors field is present |
| Descriptor | Status.Descriptors | Normal |  |  | Cond | 1,N |  | Required if Descriptors are present |
| Index | Status.Descriptors.Descriptor | Normal | 4 | N | Cond | 1,1 |  | Required if Descriptors are present |
| TestIdentifier | Status.Descriptors.Descriptor | Normal |  |  | Opt | 0,1 |  |  |
| TargetIdentifier | Status.Descriptors.Descriptor | Normal |  |  | Opt | 0,1 |  |  |
| MacroStatus | Status.Descriptors.Descriptor | Normal |  |  | Opt | 0,1 |  |  |
| MacroDescription | Status.Descriptors.Descriptor | Normal |  |  | Opt | 0,1 |  |  |
| Analysis | Status | Normal |  |  | Opt | 0,1 |  |  |
| AnalysisNumber | Analysis | Normal |  |  | Cond | 1,1 |  | Required if Analysis field is present |
| AnalysisItem | Analysis | Normal |  |  | Cond | 1,1 |  | Required if Analysis field is present |
| DiagnosisCode | Analysis.AnalysisItem | Normal |  |  |  |  | IN, OUT, ISO: indicate a FAULT is observed in the Verizon Core Network. TOK: indicates tests ran clean to the customer equipment (CSU). CPE: indicates tests ran clean to the Network Interface Device (NID), but CSU could not be looped, or errors were found to the CSU. RVW: indicates testing could not be completed successfully (access failure, design problem etc) CFA: indicates that the errors are observed from the direction of the carrier. |  |
| ShortSummary | Analysis.AnalysisItem | Normal |  |  |  |  |  |  |
| LongSummary | Analysis.AnalysisItem | Normal |  |  | Optional |  |  |  |
| TransportLevel | Analysis.AnalysisItem | Normal |  |  | Optional |  |  |  |
| CircuitID | Analysis.AnalysisItem | Normal |  |  | Optional |  |  |  |
| Details | Normal | Normal |  |  |  |  |  |  |
| Tag | ExceptionList | Exception.ProcessingFailure | 4 char | N | Opt | 0,1 |  | Error Code from TAXI |
| Value | ExceptionList | Exception.ProcessingFailure | 256 max | AN | Opt | 0,1 |  | Error Description from TAXI |

## Performance Monitoring

This transaction facilitate performance monitoring by setting the duration and interval of the monitoring activity.   Successful responses to Monitoring are categorized into ResultType as “A” (Acknowledgement),  “S” (Intermediate Status”),  “C” (final Completed).   This transaction is defined as an asynchronous transaction.

Table 26.  Performance Monitoring Request

| tML Performance Monitoring Request |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId |  | 36 max | AN | Req | 1,1 |  |  |
| UserId | Customer |  | 10 | AN | Req | 1,1 |  | Refer to §7.3 for detailed informational. |
| ServiceProfile | Customer |  | 16 max | AN | Req | 1,1 | Carrier |  |
| Type | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 5 | AN | Req | 1,1 | NYVZC NJVZC CAVZC … | Assertion::= State value followed by SP Network ID Value. SP Network ID Value is VZC |
| Type | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 4 | AN | Req | 1,1 | Account Name Value | This is used to validate digital certificate |
| Type | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | serviceID |  |
| Assertion | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 64 Max | AN | Req | 1,1 | Service ID Value | Circuit ID value, use “/” as delimiter |
| Acknowledgement |  |  |  |  | Opt | 0,1 | Y, N |  |
| StatusMessage |  |  |  |  | Opt | 0,1 | Y, N |  |
| FinalDetail |  |  |  |  | Opt | 0,1 | Y, N |  |
| Frequency |  |  |  |  | Req | 1,1 | DAILY or 15MIN |  |
| Interval |  |  |  |  | Req | 1,1 | DAILY: 1 to 7 15MIN: 1 to 32 |  |

Table 27 Performance Monitoring Response

| tML Performance Monitoring Response |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId |  | 36 max | AN | Req | 1,1 |  |  |
| Type | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 5 | AN | Req | 1,1 | NYVZC NJVZC CAVZC … | Assertion::= State value followed by SP Network ID Value. SP Network ID Value is VZC |
| Type | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 4 | AN | Req | 1,1 | Account Name Value | This is used to validate digital certificate |
| Type | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | serviceID |  |
| Assertion | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 64 Max | AN | Req | 1,1 | Service ID Value |  |
| ReturnCode |  | Normal |  |  |  |  |  |  |
| ResultType |  | Normal |  |  |  |  |  |  |
| InfoMessage |  | Normal |  |  | Opt | 0,1 |  |  |
| ErrorMessage |  | Normal |  |  | Opt | 0,1 |  |  |
| TroubleReportReferenceNumber |  | Normal |  |  | Opt |  |  |  |
| GroupTroubleReportReferenceNumber |  | Normal |  |  | Opt | 0,1 |  |  |
| CircuitDescription | Status | Normal |  |  |  |  |  |  |
| SummaryStatus | Status | Normal |  |  |  |  |  |  |
| SummaryText | Status | Normal |  |  |  |  |  |  |
| Disposition | Status | Normal |  |  | Opt | 0,1 |  |  |
| DescriptorsNumber | Status | Normal |  |  | Cond | 1,1 | Number of Descriptiors | Required if Descriptors field is present |
| Descriptor | Status.Descriptors | Normal |  |  | Cond | 1,N |  | Required if Descriptors are present |
| Index | Status.Descriptors.Descriptor | Normal | 4 | N | Cond | 1,1 |  | Required if Descriptors are present |
| TestIdentifier | Status.Descriptors.Descriptor | Normal |  |  | Opt | 0,1 |  |  |
| TargetIdentifier | Status.Descriptors.Descriptor | Normal |  |  | Opt | 0,1 |  |  |
| MacroStatus | Status.Descriptors.Descriptor | Normal |  |  | Opt | 0,1 |  |  |
| MacroDescription | Status.Descriptors.Descriptor | Normal |  |  | Opt | 0,1 |  |  |
| Analysis | Status | Normal |  |  | Opt | 0,1 |  |  |
| AnalysisNumber | Analysis | Normal |  |  | Cond | 1,1 |  | Required if Analysis field is present |
| AnalysisItem | Analysis | Normal |  |  | Cond | 1,1 |  | Required if Analysis field is present |
| DiagnosisCode | Analysis.AnalysisItem | Normal |  |  |  |  | ISO No Loopback; operation unsuccessful TOK Loopback successfully place facing direction A/Z RVW Operation could not be attempted; no viable test access; OSS communication failure |  |
| ShortSummary | Analysis.AnalysisItem | Normal |  |  |  |  |  |  |
| LongSummary | Analysis.AnalysisItem | Normal |  |  | Optional |  |  |  |
| TransportLevel | Analysis.AnalysisItem | Normal |  |  | Optional |  |  |  |
| CircuitID | Analysis.AnalysisItem | Normal |  |  | Optional |  |  |  |
| Details | Normal | Normal |  |  |  |  |  |  |
| Tag | ExceptionList | Exception.ProcessingFailure | 4 char | N | Opt | 0,1 |  | Error Code from TAXI |
| Value | ExceptionList | Exception.ProcessingFailure | 256 max | AN | Opt | 0,1 |  | Error Description from TAXI |

## Set Loopback

Request to initiate a circuit into a loop.  Successful response  contains TroubleReferenceNumber to be used in Release Loopback Request.   This transaction is defined as an asynchronous transaction.

Table 28.  Set Loopback Request

| tML SetLoopback Request |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId |  | 36 max | AN | Req | 1,1 |  |  |
| UserId | Customer |  | 10 | AN | Req | 1,1 |  | Refer to §7.3 for detailed informational. |
| ServiceProfile | Customer |  | 16 max | AN | Req | 1,1 | Carrier |  |
| Type | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 5 | AN | Req | 1,1 | NYVZC NJVZC CAVZC … | Assertion::= State value followed by SP Network ID Value. SP Network ID Value is VZC |
| Type | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 4 | AN | Req | 1,1 | Account Name Value | This is used to validate digital certificate |
| Type | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | serviceID |  |
| Assertion | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 64 Max | AN | Req | 1,1 | Service ID Value | Circuit ID value, use “/” as delimiter |
| Acknowledgement |  |  |  |  | Opt | 0,1 | Y or N |  |
| StatusMessage |  |  |  |  | Opt | 0,1 | Y or N |  |
| FinalDetail |  |  |  |  | Opt | 0,1 | Y or N |  |
| Location |  |  |  |  | Req | 1,1 | LPLOC NEAREST LPLOC FARTHEST |  |
| Direction |  |  |  |  | Req | 1,1 | A or Z |  |
| Duration |  |  |  |  |  | 1,1 | 1 to 120 | Test Duration. Test duration is specified in number of minutes the LOOPBACK will be up. TESTDUR is required for LOOPBACKUP command. "1-999" minutes. If client has not issued LOOPBACKDOWN command prior to TESTDUR, Delphi will release the LOOPBACK 30 minutes after the TESTDUR |

Table 29 SetLoopback Response

| tML SetLoopback Response |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId |  | 36 max | AN | Req | 1,1 |  |  |
| Type | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 5 | AN | Req | 1,1 | NYVZC NJVZC CAVZC … | Assertion::= State value followed by SP Network ID Value. SP Network ID Value is VZC. |
| Type | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 4 | AN | Req | 1,1 | Account Name Value | This is used to validate digital certificate |
| Type | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | serviceID |  |
| Assertion | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 64 Max | AN | Req | 1,1 | Service ID Value |  |
| TroubleReportReferenceNumber |  | Normal |  |  | Opt |  |  |  |
| ReturnCode |  | Normal |  |  |  |  |  |  |
| ResultType |  | Normal |  |  |  |  | C = Complete A = Ack |  |
| InfoMessage |  | Normal |  |  |  |  |  |  |
| ErrorMessage |  | Normal |  |  |  | 0,1 |  |  |
| CircuitDescription | Status | Normal |  |  |  |  |  |  |
| SummaryStatus | Status | Normal |  |  |  |  |  |  |
| SummaryText | Status | Normal |  |  |  |  |  |  |
| Disposition | Status | Normal |  |  | Opt | 0,1 |  |  |
| DescriptorsNumber | Status.Descriptors | Normal |  |  | Cond | 1,1 | Number of Descriptiors | Required if Descriptors field is present |
| Descriptor | Status.Descriptors | Normal |  |  | Cond | 1,N |  | Required if Descriptors are present |
| Index | Status.Descriptors.Descriptor | Normal | 4 | N | Cond | 1,1 |  | Required if Descriptors are present |
| TestIdentifier | Status.Descriptors.Descriptor | Normal |  |  | Opt | 0,1 |  |  |
| TargetIdentifier | Status.Descriptors.Descriptor | Normal |  |  | Opt | 0,1 |  |  |
| MacroStatus | Status.Descriptors.Descriptor | Normal |  |  | Opt | 0,1 |  |  |
| MacroDescription | Status.Descriptors.Descriptor | Normal |  |  | Opt | 0,1 |  |  |
| Analysis | Status | Normal |  |  | Opt | 0,1 |  |  |
| AnalysisNumber | Analysis | Normal |  |  | Cond | 1,1 |  | Required if Analysis field is present |
| AnalysisItem | Analysis | Normal |  |  | Cond | 1,1 |  | Required if Analysis field is present |
| DiagnosisCode | Analysis.AnalysisItem | Normal |  |  |  |  | TOK: indicates tests ran clean to the customer equipment (CSU). |  |
| ShortSummary | Analysis.AnalysisItem | Normal |  |  |  |  |  |  |
| LongSummary | Analysis.AnalysisItem | Normal |  |  | Optional |  |  |  |
| TransportLevel | Analysis.AnalysisItem | Normal |  |  | Optional |  |  |  |
| CircuitID | Analysis.AnalysisItem | Normal |  |  | Optional |  |  |  |
| Details | Normal | Normal |  |  |  |  |  |  |
| Tag | ExceptionList | Exception.ProcessingFailure | 4 char | N | Opt | 0,1 |  | Error Code from TAXI |
| Value | ExceptionList | Exception.ProcessingFailure | 256 max | AN | Opt | 0,1 |  | Error Description from TAXI |

## Release Loopback

This transaction releases the circuit from a loop.  Using the troubleReferenceNumber from Set Loopback response.   A Release Loopback Response could be sent by Verizon as an unsolicitated message when loop test expires on its own.    This transaction is defined as an asynchronous transaction.

Table 30.  ReleaseLoopback Request

| tML Release Loopback Request |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId |  | 36 max | AN | Req | 1,1 |  |  |
| UserId | Customer |  | 10 | AN | Req | 1,1 |  | Refer to §7.3 for detailed informational. |
| ServiceProfile | Customer |  | 16 max | AN | Req | 1,1 | Carrier |  |
| Type | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 5 | AN | Req | 1,1 | NYVZC NJVZC CAVZC … | Assertion::= State value followed by SP Network ID Value. SP Network ID Value is VZC |
| Type | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 4 | AN | Req | 1,1 | Account Name Value | This is used to validate digital certificate |
| Type | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | serviceID |  |
| Assertion | RDNSequenceItem | ManagedObjectInstance. DistinguishedName | 64 Max | AN | Req | 1,1 | Service ID Value | Circuit ID value, use “/” as delimiter |
| TroubleReportReferenceNumber |  |  |  |  | Req | 1,1 |  |  |

Table 31 Release Loopback Response

| tML Release Loopback Response |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId |  | 36 max | AN | Req | 1,1 |  |  |
| Type | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 5 | AN | Req | 1,1 | NYVZC NJVZC CAVZC … | Assertion::= State value followed by SP Network ID Value. SP Network ID Value is VZC. |
| Type | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 4 | AN | Req | 1,1 | Account Name Value | This is used to validate digital certificate |
| Type | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 9 | AN | Req | 1,1 | serviceID |  |
| Assertion | RDNSequenceItem | TargetObjectInstance. DistinguishedName | 64 Max | AN | Req | 1,1 | Service ID Value |  |
| ReturnCode |  | Normal |  |  |  | 1,1 | 0000 = Completely successful. 0XXX = Partially successful. 1-9XXX = Error encountered |  |
| ResultType |  | Normal |  |  |  | 1,1 | C = Complete |  |
| InfoMessage |  | Normal |  |  |  |  |  |  |
| ErrorMessage |  | Normal |  |  |  | 0,1 |  |  |
| CircuitDescription | Status | Normal |  |  |  |  |  |  |
| SummaryStatus | Status | Normal |  |  |  |  |  |  |
| SummaryText | Status | Normal |  |  |  |  |  |  |
| Disposition | Status | Normal |  |  | Opt | 0,1 |  |  |
| DescriptorsNumber | Status.Descriptors | Normal |  |  | Cond | 1,1 | Number of Descriptiors | Required if Descriptors field is present |
| Descriptor | Status.Descriptors | Normal |  |  | Cond | 1,N |  | Required if Descriptors are present |
| Index | Status.Descriptors.Descriptor | Normal | 4 | N | Cond | 1,1 |  | Required if Descriptors are present |
| TestIdentifier | Status.Descriptors.Descriptor | Normal |  |  | Opt | 0,1 |  |  |
| TargetIdentifier | Status.Descriptors.Descriptor | Normal |  |  | Opt | 0,1 |  |  |
| MacroStatus | Status.Descriptors.Descriptor | Normal |  |  | Opt | 0,1 |  |  |
| MacroDescription | Status.Descriptors.Descriptor | Normal |  |  | Opt | 0,1 |  |  |
| Analysis | Status | Normal |  |  | Opt | 0,1 |  |  |
| AnalysisNumber | Analysis | Normal |  |  | Cond | 1,1 |  | Required if Analysis field is present |
| AnalysisItem | Analysis | Normal |  |  | Cond | 1,1 |  | Required if Analysis field is present |
| DiagnosisCode | Analysis.AnalysisItem | Normal |  |  |  |  | TOK |  |
| ShortSummary | Analysis.AnalysisItem | Normal |  |  |  |  |  |  |
| LongSummary | Analysis.AnalysisItem | Normal |  |  | Optional |  |  |  |
| TransportLevel | Analysis.AnalysisItem | Normal |  |  | Optional |  |  |  |
| CircuitID | Analysis.AnalysisItem | Normal |  |  | Optional |  |  |  |
| Details | Normal | Normal |  |  |  |  |  |  |
| Tag | ExceptionList | Exception.ProcessingFailure | 4 char | N | Opt | 0,1 |  | Error Code from TAXI |
| Value | ExceptionList | Exception.ProcessingFailure | 256 max | AN | Opt | 0,1 |  | Error Description from TAXI |

## Retrieve Local Contact by Trouble Report Id

Currently this transaction is available in TAXI-Access only.

Table 32.  Retrieve Local Contact Request

| tML Retrieve Trouble Report Attributes Request |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | RetrieveLocalContactByTroubleReportIdRequest | 36 max | AN | Req | 1,1 |  |  |
| UserId | Customer | RetrieveLocalContactByTroubleReportIdRequest | 10 | AN | Req | 1,1 |  | Refer to §7.3 for detailed informational. |
| ServiceProfile | Customer | RetrieveLocalContactByTroubleReportIdRequest | 8 max | AN | Req | 1,1 | Carrier |  |
| Type | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdRequest.TargetObjectName.DistinguishedName | 9 | AN | Req | 1,N | networkID |  |
| Assertion | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdRequest.TargetObjectName.DistinguishedName | 3 | AN | Req | 1,N | State code + SP Network ID Value e.g. NYVZL for a local customer (CLEC, RESELLER) e.g. NYVZC for a carrier (access) customer (Carrier) |  |
| Type | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdRequest.TargetObjectName.DistinguishedName | 11 | AN | Req | 1,N | accountName |  |
| Assertion | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdRequest.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,N | SC Account Name Value |  |
| Type | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdRequest.TargetObjectName.DistinguishedName | 15 | AN | Req | 1,N | troubleReportID |  |
| Assertion | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdRequest.TargetObjectName.DistinguishedName | 32 max | AN | Req | 1,N | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |

Table 33.  Retrieve Local Contact Response

| tML Retrieve Trouble Report Attributes Response |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | RetrieveLocalContactByTroubleReportIdResponse | 36 Max. | AN | Req | 1,1 |  | Create request correlation id |
| Type | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 3 | AN | Req | 1,1 | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) |  |
| Type | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 15 | AN | Req | 1,1 | troubleReportID |  |
| Assertion | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 32 Max | AN | Req | 1,1 | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |
|  |  | RetrieveLocalContactByTroubleReportIdResponse.Normal |  |  |  |  |  |  |
| ALocationAccessAddress |  | RetrieveLocalContactByTroubleReportIdResponse.Normal |  |  | Opt | 0,1 |  |  |
| PremisesName | ALocationAccessAddress | RetrieveLocalContactByTroubleReportIdResponse.Normal | 64 Max | AN | Cond | 1.1 |  |  |
| PremisesPhone | ALocationAccessAddress | RetrieveLocalContactByTroubleReportIdResponse.Normal | 64 Max | AN | Cond | 1.1 |  |  |
| CivicAddress | PremisesAddress | RetrieveLocalContactByTroubleReportIdResponse.Normal. ALocationAccessAddress | 64 Max | AN | Cond | 1,1 |  |  |
|  | ALocationAccessHours | RetrieveLocalContactByTroubleReportIdResponse.Normal. |  |  | Opt | 0,1 |  |  |
| LocationAccessHoursItem | ALocationAccessHours | RetrieveLocalContactByTroubleReportIdResponse.Normal. |  |  | Cond | 0,1 |  |  |
| Sunday | DaysOfWeek | RetrieveLocalContactByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Cond | 1,1 | true false | Retrieved multiple LocationAccessHoursItem may not maintain the original order as they were originally provided based transactional timestamp |
| Monday | DaysOfWeek | RetrieveLocalContactByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Cond | 1,1 | true false |  |
| Tuesday | DaysOfWeek | RetrieveLocalContactByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Cond | 1,1 | true false |  |
| Wednesday | DaysOfWeek | RetrieveLocalContactByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Cond | 1,1 | true false |  |
| Thursday | DaysOfWeek | RetrieveLocalContactByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Cond | 1,1 | true false |  |
| Friday | DaysOfWeek | RetrieveLocalContactByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Cond | 1,1 | true false |  |
| Saturday | DaysOfWeek | RetrieveLocalContactByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem | 5 Max | AN | Cond | 1,1 | true false |  |
| IntervalStart | IntervalsOfDayItem | RetrieveLocalContactByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem . IntervalsOfDay | 8 | AN | Cond | 1,n |  | Premises' Local Time Military Format: HH:MM:SS |
| IntervalEnd | IntervalsOfDayItem | RetrieveLocalContactByTroubleReportIdResponse.Normal. ALocationAccessHours. LocationAccessHoursItem . IntervalsOfDay | 8 | AN | Cond | 1,n |  | Premises' Local Time Military Format: HH:MM:SS |
| ALocationAccessPerson |  | RetrieveLocalContactByTroubleReportIdResponse.Normal |  |  | Opt | 0,1 |  |  |
| Name | ALocationAccessPerson | RetrieveLocalContactByTroubleReportIdResponse.Normal | 64 Max | AN | Cond | 1,1 |  |  |
| Phone | ALocationAccessPerson | RetrieveLocalContactByTroubleReportIdResponse.Normal | 18 | AN | Cond | 1,1 |  |  |
| Email | ALocationAccessPerson | RetrieveLocalContactByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| Fax | ALocationAccessPerson | RetrieveLocalContactByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| Respon | ALocationAccessPerson | RetrieveLocalContactByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 | Yes No |  |
| Pager | ALocationAccessPerson | RetrieveLocalContactByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| CircuitId |  | RetrieveLocalContactByTroubleReportIdResponse.Normal | 64 Max | AN | Opt | 0,1 |  |  |
| EscalationList |  | RetrieveAttributesByTroubleReportIdResponse.Normal. |  |  | Opt | 0,1 |  |  |
| EscalationItem | EscalationList | RetrieveAttributesByTroubleReportIdResponse.Normal. |  |  | Opt | 0,1 |  |  |
| Level | EscalationItem | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList | 1 | N | Opt | 0,1 | 1,2,3,4 |  |
| Remarks | EscalationItem | RetrieveAttributesByTroubleReportIdResponse.Normal. EscalationList | 256 | N | Opt | 0,1 |  |  |
| ManagedObjectAccessHours |  | RetrieveLocalContactByTroubleReportIdResponse.Normal |  |  | Opt | 0,1 |  |  |
| ManagedObjectAccessHoursItem | ManagedObjectAccessHours | RetrieveLocalContactByTroubleReportIdResponse.Normal |  |  | Opt | 0,1 |  |  |
| Sunday | DaysOfWeek | RetrieveLocalContactByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Cond | 1,1 | true false | Retrieved multiple ManagedObjectAccessHoursItem may not maintain the original order as they were originally provided based transactional timestamp |
| Monday | DaysOfWeek | RetrieveLocalContactByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Cond | 1,1 | true false |  |
| Tuesday | DaysOfWeek | RetrieveLocalContactByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Cond | 1,1 | true false |  |
| Wednesday | DaysOfWeek | RetrieveLocalContactByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Cond | 1,1 | true false |  |
| Thursday | DaysOfWeek | RetrieveLocalContactByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Cond | 1,1 | true false |  |
| Friday | DaysOfWeek | RetrieveLocalContactByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Cond | 1,1 | true false |  |
| Saturday | DaysOfWeek | RetrieveLocalContactByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem | 5 Max | AN | Cond | 1,1 | true false |  |
| IntervalStart | IntervalsOfDayItem | RetrieveLocalContactByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem. IntervalsOfDay | 8 | AN | Cond | 1,1 |  | Local time in HH:MM:SS format |
| IntervalEnd | IntervalsOfDayItem | RetrieveLocalContactByTroubleReportIdResponse.Normal. ManagedObjectAccessHours. ManagedObjectAccessHoursItem. IntervalsOfDay | 8 | AN | Cond | 1,1 |  | Local time in HH:MM:SS format |

Table 34.  Retrieve Local Contact Response - Exception

| tML Retrieve Trouble Report Attributes Response |
| --- |
| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | Valid Entries | Notes and Conditions |
| RequestId | RequestId | RetrieveLocalContactByTroubleReportIdResponse | 36 max | AN | Req | 1,1 |  |  |
| Type | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 9 | AN | Req | 1,1 | networkID |  |
| Assertion | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,1 | SP Network ID Value VZL for a local customer (CLEC, RESELLER) VZC for a carrier (access) customer (Carrier) |  |
| Type | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 11 | AN | Req | 1,1 | accountName |  |
| Assertion | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 4 | AN | Req | 1,1 | SC Account Name Value |  |
| Type | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 15 | AN | Req | 1,1 | troubleReportID |  |
| Assertion | RDNSequenceItem | RetrieveLocalContactByTroubleReportIdResponse.TargetObjectName.DistinguishedName | 64 max | AN | Req | 1,1 | Trouble Report ID Value | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |

## Retrieve Technician Notes By Trouble Report Id

This transaction is available to TAXI Access customers.

Table 35.  tML Retrieve Technician Notes  Request

| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | TAXI Tag | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| RequestId | RequestId | RetrieveTechnicianNotesRequest | 36 max | AN | Req | 1,1 |  |  |
| UserId | Customer | RetrieveTechnicianNotesRequest | 10 | AN | Req | 1,1 | <Header> <UserID> |  |
| ServiceProfile | Customer | RetrieveTechnicianNotesRequest | 8 max | AN | Req | 1,1 |  | “RESELLER” or “CLEC” for Verizon Local Customers “Carrier” for Verizon Access Customers |
| Type | RDNSequenceItem | RetrieveTechnicianNotesRequest. TargetObjectName. DistinguishedName | 9 | AN | Req | 1,1 |  |  |
| Assertion | RDNSequenceItem | RetrieveTechnicianNotesRequest.TargetObjectName. DistinguishedName | 5 | AN | Req | 1,1 |  | Assertion::= State value followed by SP Network ID Value. SP Network ID Value is VZC. |
| Type | RDNSequenceItem | RetrieveTechnicianNotesRequest. TargetObjectName. DistinguishedName | 11 | AN | Req | 1,1 |  |  |
| Assertion | RDNSequenceItem | RetrieveTechnicianNotesRequest. TargetObjectName. DistinguishedName | 4 | AN | Req | 1,1 |  | This is used to validate digital certificate |
| Type | RDNSequenceItem | RetrieveTechnicianNotesRequest. TargetObjectName. DistinguishedName | 9 | AN | Opt | 1,1 |  |  |
| Assertion | RDNSequenceItem | RetrieveTechnicianNotesRequest. TargetObjectName. DistinguishedName | 64 Max | AN | Opt | 1,1 | <RetrieveTechnicianNotes><TroubleReportID>WNYAC012345</ TroubleReportID> </RetrieveTechnicianNotes > | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |

Table 36.  tML Retrieve Technician Notes Response

| Tag | Aggregate | Parent Aggregate | Length | Type | Usage | Occur | TAXI Tags | Notes and Conditions |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| RequestId | RequestId | RetrieveTechnicianNotesResponse | 36 max | AN | Req | 1,1 | From EchoBack |  |
|  |  | RetrieveTechnicianNotesRequest. TargetObjectName. |  |  |  |  | From EchoBack |  |
| Type | RDNSequenceItem | RetrieveTechnicianNotesRequest. TargetObjectName. DistinguishedName | 9 | AN | Req | 1,1 | From EchoBack |  |
| Assertion | RDNSequenceItem | RetrieveTechnicianNotesRequest.TargetObjectName. DistinguishedName | 5 | AN | Req | 1,1 | From EchoBack | Assertion::= State value followed by SP Network ID Value. SP Network ID Value is VZC. |
| Type | RDNSequenceItem | RetrieveTechnicianNotesRequest. TargetObjectName. DistinguishedName | 11 | AN | Req | 1,1 | From EchoBack |  |
| Assertion | RDNSequenceItem | RetrieveTechnicianNotesRequest. TargetObjectName. DistinguishedName | 4 | AN | Req | 1,1 | From EchoBack | This is used to validate digital certificate |
| Type | RDNSequenceItem | RetrieveTechnicianNotesRequest. TargetObjectName. DistinguishedName | 9 | AN | Opt | 1,1 | From EchoBack |  |
| Assertion | RDNSequenceItem | RetrieveTechnicianNotesRequest. TargetObjectName. DistinguishedName | 64 Max | AN | Opt | 1,1 | From EchoBack | The maximum length supported by Verizon for Trouble Report ID value is 18 characters |
|  |  | RetrieveTechnicianNotesResponse. Normal |  |  |  | 0,1 |  |  |
| ActivityLog |  | RetrieveTechnicianNotesResponse. Normal |  |  | Req | 1 |  |  |
| ActivityLogItem | ActivityLog | RetrieveTechnicianNotesResponse.Normal |  |  | Req | 1,n | <ActivityLog> |  |
| ActivityLogDate | ActivityLog.ActivityLogItem | RetrieveTechnicianNotesResponse.Normal | 20 char | AN | Req | 1 | <ActivityLogDate> | GMT in W3C XML schema dateTime type format: YYYY-MM-DDTHH:MM:SSZ |
| ActivityDescription | ActivityLog.ActivityLogItem | RetrieveTechnicianNotesResponse.Normal | 3000 max | AN | Req | 1 | <ActivityDescription> |  |
|  |  | RetrieveTechnicianNotesResponse. Exception.ProcessingFailure |  |  |  | 0,1 |  |  |
| Tag | ExceptionList | RetrieveTechnicianNotesResponse. Exception.ProcessingFailure | 4 char | N | Opt | 0,1 | ErrorCode | Error Code from TAXI |
| Value | ExceptionList | RetrieveTechnicianNotesResponse. Exception.ProcessingFailure | 256 max | AN | Opt | 0,1 | ErrorDescription | Error Description from TAXI |

# Sample tML

## Sample tML for POTS Service Test

This transaction is offered only in Local Webservice.

### Request

<?xml version="1.0" encoding="UTF-8"?>

<POTSUncontrolledTestRequest

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest

tML-ServiceTest.xsd">

<RequestId>PotsTest123</RequestId>

<Customer>

<tML-TABase:UserId>WSEATTL01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>CLEC</tML-TABase:ServiceProfile>

</Customer>

<TestRequestType>1</TestRequestType>

<ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>VAVZL</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ATTL</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>7039746778</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

</POTSUncontrolledTestRequest>

### Response – Normal (Full – TestRequestType is 1)

<?xml version="1.0" encoding="UTF-8"?>

<POTSUncontrolledTestResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest

tML-ServiceTest.xsd">

<RequestId>PotsTest123</RequestId>

<ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>VAVZL</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ATTL</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>7039746778</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<PotsTestResponse>

<Normal>

<tML-ServiceTestBase:Summary>This is a summary...</tML-ServiceTestBase:Summary>

<tML-ServiceTestBase:Results>

<tML-ServiceTestBase:Full>

<tML-ServiceTestBase:DcSignature>

<tML-ServiceTestBase:TipToRingResistance>10</tML-ServiceTestBase:TipToRingResistance>

<tML-ServiceTestBase:TipToGroundResistance>1000</tML-ServiceTestBase:TipToGroundResistance>

<tML-ServiceTestBase:TipToGroundVolts>50</tML-ServiceTestBase:TipToGroundVolts>

<tML-ServiceTestBase:RingToGroundResistance>200</tML-ServiceTestBase:RingToGroundResistance>

<tML-ServiceTestBase:RingToGroundVolts>10</tML-ServiceTestBase:RingToGroundVolts>

</tML-ServiceTestBase:DcSignature>

<tML-ServiceTestBase:AcSignature>

<tML-ServiceTestBase:Ringers>2</tML-ServiceTestBase:Ringers>

<tML-ServiceTestBase:TipToRingResistance>1000</tML-ServiceTestBase:TipToRingResistance>

<tML-ServiceTestBase:TipToGroundResistance>1000</tML-ServiceTestBase:TipToGroundResistance>

<tML-ServiceTestBase:RingToGroundResistance>200</tML-ServiceTestBase:RingToGroundResistance>

</tML-ServiceTestBase:AcSignature>

<tML-ServiceTestBase:CentralOffice>

<tML-ServiceTestBase:LineCircuitStatus>OK</tML-ServiceTestBase:LineCircuitStatus>

<tML-ServiceTestBase:DialToneStatus>Not OK</tML-ServiceTestBase:DialToneStatus>

</tML-ServiceTestBase:CentralOffice>

<tML-ServiceTestBase:Balance>

<tML-ServiceTestBase:Capacitive>99</tML-ServiceTestBase:Capacitive>

<tML-ServiceTestBase:Longitudinal>20</tML-ServiceTestBase:Longitudinal>

</tML-ServiceTestBase:Balance>

<tML-ServiceTestBase:Loop>

<tML-ServiceTestBase:TotalLoop>15</tML-ServiceTestBase:TotalLoop>

</tML-ServiceTestBase:Loop>

</tML-ServiceTestBase:Full>

</tML-ServiceTestBase:Results>

</Normal>

</PotsTestResponse>

</POTSUncontrolledTestResponse>

### Response – Normal (Quick Test RequestType is 2)

<?xml version="1.0" encoding="UTF-8"?>

<POTSUncontrolledTestResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest

tML-ServiceTest.xsd">

<RequestId>PotsTest123</RequestId>

<ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>Service Provider Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>Service Consumer Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>7039746778</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<PotsTestResponse>

<Normal>

<tML-ServiceTestBase:Summary>This is a summary...</tML-ServiceTestBase:Summary>

<tML-ServiceTestBase:Results>

<tML-ServiceTestBase:Quick>

<tML-ServiceTestBase:DcSignature>

<tML-ServiceTestBase:TipToRingResistance>10</tML-ServiceTestBase:TipToRingResistance>

<tML-ServiceTestBase:TipToGroundResistance>1000</tML-ServiceTestBase:TipToGroundResistance>

<tML-ServiceTestBase:TipToGroundVolts>50</tML-ServiceTestBase:TipToGroundVolts>

<tML-ServiceTestBase:RingToGroundResistance>200</tML-ServiceTestBase:RingToGroundResistance>

<tML-ServiceTestBase:RingToGroundVolts>10</tML-ServiceTestBase:RingToGroundVolts>

</tML-ServiceTestBase:DcSignature>

<tML-ServiceTestBase:AcSignature>

<tML-ServiceTestBase:Ringers>2</tML-ServiceTestBase:Ringers>

<tML-ServiceTestBase:TipToRingResistance>1000</tML-ServiceTestBase:TipToRingResistance>

<tML-ServiceTestBase:TipToGroundResistance>1000</tML-ServiceTestBase:TipToGroundResistance>

<tML-ServiceTestBase:RingToGroundResistance>200</tML-ServiceTestBase:RingToGroundResistance>

</tML-ServiceTestBase:AcSignature>

<tML-ServiceTestBase:Balance>

<tML-ServiceTestBase:Capacitive>99</tML-ServiceTestBase:Capacitive>

<tML-ServiceTestBase:Longitudinal>20</tML-ServiceTestBase:Longitudinal>

</tML-ServiceTestBase:Balance>

<tML-ServiceTestBase:Loop>

<tML-ServiceTestBase:TotalLoop>15</tML-ServiceTestBase:TotalLoop>

</tML-ServiceTestBase:Loop>

</tML-ServiceTestBase:Quick>

</tML-ServiceTestBase:Results>

</Normal>

</PotsTestResponse>

</POTSUncontrolledTestResponse>

### Response – Normal (Central Office TestRequestType is 3)

<?xml version="1.0" encoding="UTF-8"?>

<POTSUncontrolledTestResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest

tML-ServiceTest.xsd">

<RequestId>PotsTest123</RequestId>

<ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>Service Provider Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>Service Consumer Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>7039746778</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<PotsTestResponse>

<Normal>

<tML-ServiceTestBase:Summary>This is a summary...</tML-ServiceTestBase:Summary>

<tML-ServiceTestBase:Results>

<tML-ServiceTestBase:CentralOffice>

<tML-ServiceTestBase:DcSignature>

<tML-ServiceTestBase:TipToRingResistance>10</tML-ServiceTestBase:TipToRingResistance>

<tML-ServiceTestBase:TipToGroundResistance>1000</tML-ServiceTestBase:TipToGroundResistance>

<tML-ServiceTestBase:TipToGroundVolts>50</tML-ServiceTestBase:TipToGroundVolts>

<tML-ServiceTestBase:RingToGroundResistance>200</tML-ServiceTestBase:RingToGroundResistance>

<tML-ServiceTestBase:RingToGroundVolts>10</tML-ServiceTestBase:RingToGroundVolts>

</tML-ServiceTestBase:DcSignature>

<tML-ServiceTestBase:AcSignature>

<tML-ServiceTestBase:Ringers>2</tML-ServiceTestBase:Ringers>

<tML-ServiceTestBase:TipToRingResistance>1000</tML-ServiceTestBase:TipToRingResistance>

<tML-ServiceTestBase:TipToGroundResistance>1000</tML-ServiceTestBase:TipToGroundResistance>

<tML-ServiceTestBase:RingToGroundResistance>200</tML-ServiceTestBase:RingToGroundResistance>

</tML-ServiceTestBase:AcSignature>

<tML-ServiceTestBase:CentralOffice>

<tML-ServiceTestBase:LineCircuitStatus>OK</tML-ServiceTestBase:LineCircuitStatus>

<tML-ServiceTestBase:DialToneStatus>Not OK</tML-ServiceTestBase:DialToneStatus>

</tML-ServiceTestBase:CentralOffice>

<tML-ServiceTestBase:Balance>

<tML-ServiceTestBase:Capacitive>99</tML-ServiceTestBase:Capacitive>

<tML-ServiceTestBase:Longitudinal>20</tML-ServiceTestBase:Longitudinal>

</tML-ServiceTestBase:Balance>

<tML-ServiceTestBase:Loop>

<tML-ServiceTestBase:TotalLoop>15</tML-ServiceTestBase:TotalLoop>

</tML-ServiceTestBase:Loop>

</tML-ServiceTestBase:CentralOffice>

</tML-ServiceTestBase:Results>

</Normal>

</PotsTestResponse>

</POTSUncontrolledTestResponse>

### Response – Normal (Loop TestRequestType is 4)

<?xml version="1.0" encoding="UTF-8"?>

<POTSUncontrolledTestResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest

tML-ServiceTest.xsd">

<RequestId>PotsTest123</RequestId>

<ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>Service Provider Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>Service Consumer Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>7039746778</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<PotsTestResponse>

<Normal>

<tML-ServiceTestBase:Summary>This is a summary...</tML-ServiceTestBase:Summary>

<tML-ServiceTestBase:Results>

<tML-ServiceTestBase:Loop>

<tML-ServiceTestBase:DcSignature>

<tML-ServiceTestBase:TipToRingResistance>10</tML-ServiceTestBase:TipToRingResistance>

<tML-ServiceTestBase:TipToGroundResistance>1000</tML-ServiceTestBase:TipToGroundResistance>

<tML-ServiceTestBase:TipToGroundVolts>50</tML-ServiceTestBase:TipToGroundVolts>

<tML-ServiceTestBase:RingToGroundResistance>200</tML-ServiceTestBase:RingToGroundResistance>

<tML-ServiceTestBase:RingToGroundVolts>10</tML-ServiceTestBase:RingToGroundVolts>

</tML-ServiceTestBase:DcSignature>

<tML-ServiceTestBase:AcSignature>

<tML-ServiceTestBase:Ringers>2</tML-ServiceTestBase:Ringers>

<tML-ServiceTestBase:TipToRingResistance>1000</tML-ServiceTestBase:TipToRingResistance>

<tML-ServiceTestBase:TipToGroundResistance>1000</tML-ServiceTestBase:TipToGroundResistance>

<tML-ServiceTestBase:RingToGroundResistance>200</tML-ServiceTestBase:RingToGroundResistance>

</tML-ServiceTestBase:AcSignature>

<tML-ServiceTestBase:CentralOffice>

<tML-ServiceTestBase:LineCircuitStatus>OK</tML-ServiceTestBase:LineCircuitStatus>

<tML-ServiceTestBase:DialToneStatus>Not OK</tML-ServiceTestBase:DialToneStatus>

</tML-ServiceTestBase:CentralOffice>

<tML-ServiceTestBase:Balance>

<tML-ServiceTestBase:Capacitive>99</tML-ServiceTestBase:Capacitive>

<tML-ServiceTestBase:Longitudinal>20</tML-ServiceTestBase:Longitudinal>

</tML-ServiceTestBase:Balance>

<tML-ServiceTestBase:Loop>

<tML-ServiceTestBase:TotalLoop>15</tML-ServiceTestBase:TotalLoop>

</tML-ServiceTestBase:Loop>

</tML-ServiceTestBase:Loop>

</tML-ServiceTestBase:Results>

</Normal>

</PotsTestResponse>

</POTSUncontrolledTestResponse>

### Response – Error (Case 1)

<?xml version="1.0" encoding="UTF-8"?>

<POTSUncontrolledTestResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest

tML-ServiceTest.xsd">

<RequestId>PotsTest123</RequestId>

<ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>Service Provider Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>Service Consumer Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>7039746778</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<PotsTestResponse>

<tML-ServiceTestBase:Exception>

<tML-ServiceTestBase:TroubleRepairInProgress>

This POTS line is under repair...

</tML-ServiceTestBase:TroubleRepairInProgress>

</tML-ServiceTestBase:Exception>

</PotsTestResponse>

</POTSUncontrolledTestResponse>

### Response – Error (Case 2)

<?xml version="1.0" encoding="UTF-8"?>

<POTSUncontrolledTestResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest

tML-ServiceTest.xsd">

<RequestId>PotsTest123</RequestId>

<ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>Service Provider Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>Service Consumer Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>7039746778</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<PotsTestResponse>

< tML-TABase:Exception>

<tML-TABase:AccessDenied>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>0001</tML-TABase:Tag>

<tML-TABase:Value>The user is not authorized to ...</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:AccessDenied>

</ tML-TABase:Exception>

</PotsTestResponse>

</POTSUncontrolledTestResponse>

## Sample tML for Trouble Report Create

### Local Customers

#### Trouble Report Create Request

<?xml version="1.0" encoding="UTF-8"?>

<RequestTroubleReportCreationRequest

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<Customer>

<tML-TABase:UserId>WSEABCD01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>CLEC</tML-TABase:ServiceProfile>

</Customer>

<NameBindingId>

<tML-TABase:NameBindingId>1.2.840.10015.0.6.24</tML-TABase:NameBindingId>

</NameBindingId>

<ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>7039746778</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<TroubleType>

<tML-TABase:Number>100</tML-TABase:Number>

</TroubleType>

<AdditionalTroubleInfoList>

<tML-TABase:AdditionalTroubleInfoItem>1234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456</tML-TABase:AdditionalTroubleInfoItem>

</AdditionalTroubleInfoList>

<AdditionalCreateInfo>

<tML-TABase:TroubleReportFormatId>1</tML-TABase:TroubleReportFormatId>

<tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:AdditionalTroubleInfoItem>some remark text</tML-TABase:AdditionalTroubleInfoItem>

</tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:ALocationAccessAddress>

<tML-TABase:PremisesName>My Oeacn Beach Home</tML-TABase:PremisesName>

<tML-TABase:PremisesAddress>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:PremisesAddress>

</tML-TABase:ALocationAccessAddress>

<tML-TABase:ALocationAccessHours>

<tML-TABase:LocationAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:LocationAccessHoursItem>

</tML-TABase:ALocationAccessHours>

<tML-TABase:ALocationAccessPerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:ALocationAccessPerson>

<tML-TABase:AuthorizationList>

<tML-TABase:AuthorizationItem>

<tML-TABase:State>2</tML-TABase:State>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>false</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>false</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

<tML-TABase:AuthTime>2002-09-12T13:25:00Z</tML-TABase:AuthTime>

<tML-TABase:AuthPerson>

<tML-TABase:Name>My Auth Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AuthPerson>

</tML-TABase:AuthorizationItem>

</tML-TABase:AuthorizationList>

<tML-TABase:CalledNumber>7039746778</tML-TABase:CalledNumber>

<tML-TABase:CommitmentTimeRequest>

<tML-TABase:OnsiteTime>2002-09-12T13:25:00Z</tML-TABase:OnsiteTime>

</tML-TABase:CommitmentTimeRequest>

<tML-TABase:CustomerTroubleTickNum>CLECTicket123</tML-TABase:CustomerTroubleTickNum>

<tML-TABase:CustomerWorkCenter>abc</tML-TABase:CustomerWorkCenter>

<tML-TABase:EscalationList>

<tML-TABase:EscalationItem>

<tML-TABase:State>1</tML-TABase:State>

<tML-TABase:EscTime>2002-09-12T13:25:00Z</tML-TABase:EscTime>

<tML-TABase:RequestPerson>

<tML-TABase:Name>My Request Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:RequestPerson>

<tML-TABase:Level>2</tML-TABase:Level>

</tML-TABase:EscalationItem>

</tML-TABase:EscalationList>

<tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:ManagedObjectAccessHoursItem>

</tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagedObjectInstanceAliasItem>Service Alias Name</tML-TABase:ManagedObjectInstanceAliasItem>

</tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagerContactPerson>

<tML-TABase:Name>Manager Contact Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:ManagerContactPerson>

<tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:Number>0</tML-TABase:Number>

</tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:PreferredPriority>3</tML-TABase:PreferredPriority>

<tML-TABase:RepeatReport>2</tML-TABase:RepeatReport>

<tML-TABase:TroubleDetectionTime>2002-09-12T13:25:00Z</tML-TABase:TroubleDetectionTime>

<tML-TABase:TroubleReportStatusWindow>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:TroubleReportStatusWindow>

<tML-TABase:TspPriority>E2</tML-TABase:TspPriority>

</AdditionalCreateInfo>

</RequestTroubleReportCreationRequest>

#### Trouble Report Create Response – Normal

<?xml version="1.0" encoding="UTF-8"?>

<RequestTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Normal>

<tML-TABase:InitiatingMode>0</tML-TABase:InitiatingMode>

<tML-TABase:ReceivedTime>2002-09-12T13:20:00Z</tML-TABase:ReceivedTime>

<tML-TABase:TroubleReportId>abc123WL</tML-TABase:TroubleReportId>

<tML-TABase:TroubleReportState>1</tML-TABase:TroubleReportState>

<tML-TABase:TroubleReportStatus>

<tML-TABase:Number>8</tML-TABase:Number>

</tML-TABase:TroubleReportStatus>

<tML-TABase:TroubleReportStatusTime>2002-09-12T13:25:00Z</tML-TABase:TroubleReportStatusTime>

<tML-TABase:AgentContactPerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AgentContactPerson>

<tML-TABase:CommitmentTime>

<tML-TABase:OnsiteTime>2002-09-14T13:25:00Z</tML-TABase:OnsiteTime>

</tML-TABase:CommitmentTime>

</tML-TABase:Normal>

</CreateResponse>

</RequestTroubleReportCreationResponse>

#### Trouble Report Create Response – Exception (Trouble Report Already Exists)

For further processing regarding TroubleReportAlreadyExists exception, please refer to Annex E	Trouble Ticket Late Bonding

<?xml version="1.0" encoding="UTF-8"?>

<RequestTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Exception>

<tML-TABase:TroubleReportAlreadyExists>

<tML-TABase:ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</tML-TABase:ManagedObjectInstance>

</tML-TABase:TroubleReportAlreadyExists>

</tML-TABase:Exception>

</CreateResponse>

</RequestTroubleReportCreationResponse>

#### Trouble Report Create Response – Exception (Req Attributes Missing)

<?xml version="1.0" encoding="UTF-8"?>

<RequestTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Exception>

<tML-TABase:TRMustBePresentAttributeMissing>

<tML-TABase:AttributeIDItem>TroubleType</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AdditionalTroubleInfoList</tML-TABase:AttributeIDItem>

</tML-TABase:TRMustBePresentAttributeMissing>

</tML-TABase:Exception>

</CreateResponse>

</RequestTroubleReportCreationResponse>

#### Trouble Report Create Response – Exception (Fall Back Reporting)

<?xml version="1.0" encoding="UTF-8"?>

<RequestTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Exception>

<tML-TABase:FallBackReporting>

Please report the trouble to Verizon enterprise office by calling 1-800-888-9999

Monday through Friday from 1 am to 11:59 pm (National and Verizon holidays excluded)

</tML-TABase:FallBackReporting>

</tML-TABase:Exception>

</CreateResponse>

</RequestTroubleReportCreationResponse>

#### Trouble Report Create Response – Exception (Invalid Data Received)

<?xml version="1.0" encoding="UTF-8"?>

<RequestTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Exception>

<tML-TABase:InvalidDataReceived>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>0002</tML-TABase:Tag>

<tML-TABase:Value>TroubleType</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:InvalidDataReceived>

</tML-TABase:Exception>

</CreateResponse>

</RequestTroubleReportCreationResponse>

#### Trouble Report Create Response – Exception (Processing Failure)

<?xml version="1.0" encoding="UTF-8"?>

<RequestTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Exception>

<tML-TABase:ProcessingFailure>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>0003</tML-TABase:Tag>

<tML-TABase:Value>Java Runtime Exception:Array Index Out of Bound</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:ProcessingFailure>

</tML-TABase:Exception>

</CreateResponse>

</RequestTroubleReportCreationResponse>

### Access Carrier and/or Retail Customers

#### Trouble Report Create Request

<?xml version="1.0" encoding="UTF-8"?>

<RequestTroubleReportCreationRequest

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>Carrier</tML-TABase:ServiceProfile>

</Customer>

<NameBindingId>

<tML-TABase:NameBindingId>1.2.840.10015.0.6.24</tML-TABase:NameBindingId>

</NameBindingId>

<ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>528/PH-5EDG1/BLTNCAAD1MD/77/YUCPCAXF79M</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<TroubleType>

<tML-TABase:Number>1518</tML-TABase:Number>

</TroubleType>

<AdditionalTroubleInfoList>

<tML-TABase:AdditionalTroubleInfoItem>1234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456</tML-TABase:AdditionalTroubleInfoItem>

</AdditionalTroubleInfoList>

<AdditionalCreateInfo>

<tML-TABase:TroubleReportFormatId>1</tML-TABase:TroubleReportFormatId>

<tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:AdditionalTroubleInfoItem>some remark text</tML-TABase:AdditionalTroubleInfoItem>

</tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:ALocationAccessAddress>

<tML-TABase:PremisesName>My Oeacn Beach Home</tML-TABase:PremisesName>

<tML-TABase:PremisesAddress>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:PremisesAddress>

</tML-TABase:ALocationAccessAddress>

<tML-TABase:ALocationAccessHours>

<tML-TABase:LocationAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:LocationAccessHoursItem>

</tML-TABase:ALocationAccessHours>

<tML-TABase:ALocationAccessPerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:ALocationAccessPerson>

<tML-TABase:AuthorizationList>

<tML-TABase:AuthorizationItem>

<tML-TABase:State>2</tML-TABase:State>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>false</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>false</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

<tML-TABase:AuthTime>2002-09-12T13:25:00Z</tML-TABase:AuthTime>

<tML-TABase:AuthPerson>

<tML-TABase:Name>My Auth Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AuthPerson>

</tML-TABase:AuthorizationItem>

</tML-TABase:AuthorizationList>

<tML-TABase:CalledNumber>7039746778</tML-TABase:CalledNumber>

<tML-TABase:CustomerTroubleTickNum>CLECTicket123</tML-TABase:CustomerTroubleTickNum>

<tML-TABase:CustomerWorkCenter>abc</tML-TABase:CustomerWorkCenter>

<tML-TABase:EscalationList>

<tML-TABase:EscalationItem>

<tML-TABase:State>1</tML-TABase:State>

<tML-TABase:EscTime>2002-09-12T13:25:00Z</tML-TABase:EscTime>

<tML-TABase:RequestPerson>

<tML-TABase:Name>My Request Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:RequestPerson>

<tML-TABase:Level>2</tML-TABase:Level>

</tML-TABase:EscalationItem>

</tML-TABase:EscalationList>

<tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:ManagedObjectAccessHoursItem>

</tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagedObjectInstanceAliasItem>a 2-6 code</tML-TABase:ManagedObjectInstanceAliasItem>

</tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagerContactPerson>

<tML-TABase:Name>Manager Contact Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:ManagerContactPerson>

<tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:Number>0</tML-TABase:Number>

</tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:PreferredPriority>3</tML-TABase:PreferredPriority>

<tML-TABase:RepeatReport>2</tML-TABase:RepeatReport>

<tML-TABase:TroubleDetectionTime>2002-09-12T13:25:00Z</tML-TABase:TroubleDetectionTime>

<tML-TABase:TroubleReportStatusWindow>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:TroubleReportStatusWindow>

<tML-TABase:TspPriority>E2</tML-TABase:TspPriority>

</AdditionalCreateInfo>

</RequestTroubleReportCreationRequest>

#### Trouble Report Create Response – Normal

<?xml version="1.0" encoding="UTF-8"?>

<RequestTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Normal>

<tML-TABase:InitiatingMode>0</tML-TABase:InitiatingMode>

<tML-TABase:ReceivedTime>2002-09-12T13:20:00Z</tML-TABase:ReceivedTime>

<tML-TABase:TroubleReportId>abc123WL</tML-TABase:TroubleReportId>

<tML-TABase:TroubleReportState>1</tML-TABase:TroubleReportState>

<tML-TABase:TroubleReportStatus>

<tML-TABase:Number>8</tML-TABase:Number>

</tML-TABase:TroubleReportStatus>

<tML-TABase:TroubleReportStatusTime>2002-09-12T13:25:00Z</tML-TABase:TroubleReportStatusTime>

<tML-TABase:AgentContactPerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AgentContactPerson>

</tML-TABase:Normal>

</CreateResponse>

</RequestTroubleReportCreationResponse>

#### Trouble Report Create Response – Exception (Trouble Report Already Exists)

For further processing regarding TroubleReportAlreadyExists exception, please refer to Annex E	Trouble Ticket Late Bonding

<?xml version="1.0" encoding="UTF-8"?>

<RequestTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Exception>

<tML-TABase:TroubleReportAlreadyExists>

<tML-TABase:ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</tML-TABase:ManagedObjectInstance>

</tML-TABase:TroubleReportAlreadyExists>

</tML-TABase:Exception>

</CreateResponse>

</RequestTroubleReportCreationResponse>

#### Trouble Report Create Response – Exception (Req Attributes Missing)

<?xml version="1.0" encoding="UTF-8"?>

<RequestTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Exception>

<tML-TABase:TRMustBePresentAttributeMissing>

<tML-TABase:AttributeIDItem>TroubleType</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AdditionalTroubleInfoList</tML-TABase:AttributeIDItem>

</tML-TABase:TRMustBePresentAttributeMissing>

</tML-TABase:Exception>

</CreateResponse>

</RequestTroubleReportCreationResponse>

#### Trouble Report Create Response – Exception (Fall Back Reporting)

<?xml version="1.0" encoding="UTF-8"?>

<RequestTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Exception>

<tML-TABase:FallBackReporting>

Please report the trouble to Verizon enterprise office by calling 1-800-888-9999

Monday through Friday from 1 am to 11:59 pm (National and Verizon holidays excluded)

</tML-TABase:FallBackReporting>

</tML-TABase:Exception>

</CreateResponse>

</RequestTroubleReportCreationResponse>

#### Trouble Report Create Response – Exception (Invalid Data Received)

<?xml version="1.0" encoding="UTF-8"?>

<RequestTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Exception>

<tML-TABase:InvalidDataReceived>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>0002</tML-TABase:Tag>

<tML-TABase:Value>TroubleType</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:InvalidDataReceived>

</tML-TABase:Exception>

</CreateResponse>

</RequestTroubleReportCreationResponse>

#### Trouble Report Create Response – Exception (Processing Failure)

<?xml version="1.0" encoding="UTF-8"?>

<RequestTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Exception>

<tML-TABase:ProcessingFailure>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>0003</tML-TABase:Tag>

<tML-TABase:Value> Java Runtime Exception: Array Index Out of Bound</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:ProcessingFailure>

</tML-TABase:Exception>

</CreateResponse>

</RequestTroubleReportCreationResponse>

## Sample tML for Trouble Report Modification

### Trouble Report Modification Request

Every child node under ModifyRequest is optional.  Customer can choose to modify only one TA attribute or group multiple attributes’ modification together.    If there is no value change on a particular attribute, that attribute is not needed in ModifyRequest.

<?xml version="1.0" encoding="UTF-8"?>

<ModifyAttributesRequest

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>Carrier</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<ModifyRequest>

<tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:AdditionalTroubleInfoItem>This is a new trouble narrative that needs to will replace the original trouble narrative</tML-TABase:AdditionalTroubleInfoItem>

</tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:ALocationAccessAddress>

<tML-TABase:PremisesName>My ocean Beach Home</tML-TABase:PremisesName>

<tML-TABase:PremisesAddress>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:PremisesAddress>

</tML-TABase:ALocationAccessAddress>

<tML-TABase:ALocationAccessHours>

<tML-TABase:LocationAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:LocationAccessHoursItem>

<tML-TABase:LocationAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>false</tML-TABase:Monday>

<tML-TABase:Tuesday>true</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>13:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:LocationAccessHoursItem>

</tML-TABase:ALocationAccessHours>

<tML-TABase:ALocationAccessPerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:ALocationAccessPerson>

<tML-TABase:AuthorizationList>

<tML-TABase:AuthorizationItem>

<tML-TABase:State>2</tML-TABase:State>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>false</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>false</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

<tML-TABase:AuthTime>2002-09-12T13:25:00Z</tML-TABase:AuthTime>

<tML-TABase:AuthPerson>

<tML-TABase:Name>My Auth Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AuthPerson>

</tML-TABase:AuthorizationItem>

<tML-TABase:AuthorizationItem>

<tML-TABase:State>3</tML-TABase:State>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>true</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>false</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>false</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>false</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

<tML-TABase:AuthTime>2002-09-12T13:25:00Z</tML-TABase:AuthTime>

<tML-TABase:AuthPerson>

<tML-TABase:Name>My Auth Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AuthPerson>

</tML-TABase:AuthorizationItem>

</tML-TABase:AuthorizationList>

<tML-TABase:EscalationList>

<tML-TABase:EscalationItem>

<tML-TABase:State>1</tML-TABase:State>

<tML-TABase:EscTime>2002-09-12T13:25:00Z</tML-TABase:EscTime>

<tML-TABase:RequestPerson>

<tML-TABase:Name>My Request Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:RequestPerson>

<tML-TABase:Level>2</tML-TABase:Level>

</tML-TABase:EscalationItem>

</tML-TABase:EscalationList>

<tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:ManagedObjectAccessHoursItem>

</tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagedObjectInstanceAliasItem>Service Alias Name</tML-TABase:ManagedObjectInstanceAliasItem>

</tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagerContactPerson>

<tML-TABase:Name>Manager Contact Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:ManagerContactPerson>

<tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:Number>0</tML-TABase:Number>

</tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:PreferredPriority>3</tML-TABase:PreferredPriority>

<tML-TABase:TroubleReportStatusWindow>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:TroubleReportStatusWindow>

</ModifyRequest>

</ModifyAttributesRequest>

### Trouble Report Modification Response – Normal

<?xml version="1.0" encoding="UTF-8"?>

<ModifyAttributesResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<Normal>

<tML-TABase:AdditionalTroubleInfoList>true</tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:ALocationAccessAddress>true</tML-TABase:ALocationAccessAddress>

<tML-TABase:ALocationAccessHours>true</tML-TABase:ALocationAccessHours>

<tML-TABase:ALocationAccessPerson>true</tML-TABase:ALocationAccessPerson>

<tML-TABase:AuthorizationList>true</tML-TABase:AuthorizationList>

<tML-TABase:EscalationList>true</tML-TABase:EscalationList>

<tML-TABase:ManagedObjectAccessHours>true</tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectInstanceAliasList>true</tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagerContactPerson>true</tML-TABase:ManagerContactPerson>

<tML-TABase:PerceivedTroubleSeverity>true</tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:PreferredPriority>true</tML-TABase:PreferredPriority>

<tML-TABase:TroubleReportStatusWindow>true</tML-TABase:TroubleReportStatusWindow>

</Normal>

</ModifyAttributesResponse>

### Trouble Report Modification Response – Partial Success

<?xml version="1.0" encoding="UTF-8"?>

<ModifyAttributesResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<Normal>

<tML-TABase:AdditionalTroubleInfoList>true</tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:ALocationAccessAddress>false</tML-TABase:ALocationAccessAddress>

<tML-TABase:ALocationAccessHours>false</tML-TABase:ALocationAccessHours>

<tML-TABase:ALocationAccessPerson>false</tML-TABase:ALocationAccessPerson>

<tML-TABase:EscalationList>false</tML-TABase:EscalationList>

<tML-TABase:ManagedObjectAccessHours>false</tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectInstanceAliasList>false</tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagerContactPerson>false</tML-TABase:ManagerContactPerson>

<tML-TABase:PerceivedTroubleSeverity>false</tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:PreferredPriority>false</tML-TABase:PreferredPriority>

<tML-TABase:TroubleReportStatusWindow>false</tML-TABase:TroubleReportStatusWindow>

</Normal>

<Exception>

<tML-TABase:ProcessingFailure>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>0003</tML-TABase:Tag>

<tML-TABase:Value> ADD FAILED - S1 SECURITY VIOLATION </tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:ProcessingFailure>

</Exception>

</ModifyAttributesResponse>

### Trouble Report Modification Response – Exception

<?xml version="1.0" encoding="UTF-8"?>

<ModifyAttributesResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<Exception>

<tML-TABase:TroubleReportChangeDenied>

<tML-TABase:ChangeDeniedReason>1</tML-TABase:ChangeDeniedReason>

<tML-TABase:ManagedObjectInstance>

<tML-TABase:DistinguishedName/>

</tML-TABase:ManagedObjectInstance>

<tML-TABase:TroubleReportId/>

</tML-TABase:TroubleReportChangeDenied>

</Exception>

</ModifyAttributesResponse>

Note:  The ManagedObjectIntstance and TroubleReportId nodes were erroneously included in the definition of TroubleReportChangeDenied exception in T1.278.   We were asked to send blank in our implementation to satisfy several CLEC’s use of strict XML validators.

<?xml version="1.0" encoding="UTF-8"?>

<ModifyAttributesResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<Exception>

<tML-TABase:ProcessingFailure>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>0003</tML-TABase:Tag>

<tML-TABase:Value>System Not Responding: Time Out Error</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:ProcessingFailure>

</Exception>

</ModifyAttributesResponse>

## Sample tML for Trouble Report Cancellation

### Trouble Report Cancellation Request

<?xml version="1.0" encoding="UTF-8"?>

<CancelTroubleReportRequest

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>RESELLER</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CancelRequestedByManager>true</CancelRequestedByManager>

<CancelRemark>

<tML-TABase:AdditionalTroubleInfoItem>This trouble report is no longer valid</tML-TABase:AdditionalTroubleInfoItem>

</CancelRemark>

<TroubleClearancePerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</TroubleClearancePerson>

</CancelTroubleReportRequest>

### Trouble Report Cancellation Response – Normal

<?xml version="1.0" encoding="UTF-8"?>

<CancelTroubleReportResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

</CancelTroubleReportResponse>

### Trouble Report Cancellation Response – Exception

<?xml version="1.0" encoding="UTF-8"?>

<CancelTroubleReportResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<Exception>

<tML-TABase:TroubleReportChangeDenied>

<tML-TABase:ChangeDeniedReason>1</tML-TABase:ChangeDeniedReason>

</tML-TABase:TroubleReportChangeDenied>

</Exception>

</CancelTroubleReportResponse>

## Sample tML for Trouble Report Close Out Verification

### Trouble Report Close Out Verification Request

<?xml version="1.0" encoding="UTF-8"?>

<VerifyRepairCompletionRequest

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>RESELLER</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CloseOutVerification>1</CloseOutVerification>

<VerificationRemarks>

<tML-TABase:AdditionalTroubleInfoItem>The repair seems to be OK</tML-TABase:AdditionalTroubleInfoItem>

</VerificationRemarks>

<TroubleClearancePerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</TroubleClearancePerson>

</VerifyRepairCompletionRequest>

### Trouble Report Close Out Verification Response

<?xml version="1.0" encoding="UTF-8"?>

<VerifyRepairCompletionResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

</VerifyRepairCompletionResponse>

### Trouble Report Close Out Verification Response – Exception

<?xml version="1.0" encoding="UTF-8"?>

<VerifyRepairCompletionResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<Exception>

<tML-TABase:CannotVerifyOrDeniedAtThisTime>

Ticket is in a state of cleared ;no additional changes can be performed

</tML-TABase:CannotVerifyOrDeniedAtThisTime>

</Exception>

</VerifyRepairCompletionResponse>

## Sample tML for Trouble Report AVC Event Notification

### Local Customers

<?xml version="1.0" encoding="UTF-8"?>

<AttributeValueChangeNotification

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<NotificationId>123</NotificationId>

<EventTime>2002-09-12T13:25:00Z</EventTime>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<EventData>

<tML-TABase:ActivityDurationList>

<tML-TABase:ActivityDurationItem>

<tML-TABase:Duration>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:Duration>

<tML-TABase:Billable>true</tML-TABase:Billable>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>true</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>true</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

</tML-TABase:ActivityDurationItem>

</tML-TABase:ActivityDurationList>

<tML-TABase:AdditionalTroubleStatusInfo>

<tML-TABase:AdditionalTroubleStatusInfoItem>testing...</tML-TABase:AdditionalTroubleStatusInfoItem>

<tML-TABase:AdditionalTroubleStatusInfoItem>dispatched</tML-TABase:AdditionalTroubleStatusInfoItem>

</tML-TABase:AdditionalTroubleStatusInfo>

<tML-TABase:AuthorizationList>

<tML-TABase:AuthorizationItem>

<tML-TABase:State>1</tML-TABase:State>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>false</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>false</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>false</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>false</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>true</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

</tML-TABase:AuthorizationItem>

<tML-TABase:AuthorizationItem>

<tML-TABase:State>2</tML-TABase:State>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>false</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>false</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

<tML-TABase:AuthTime>2002-09-12T13:25:00Z</tML-TABase:AuthTime>

<tML-TABase:AuthPerson>

<tML-TABase:Name>My Auth Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AuthPerson>

</tML-TABase:AuthorizationItem>

</tML-TABase:AuthorizationList>

<tML-TABase:CloseOutNarr>It is time to put an end on this…</tML-TABase:CloseOutNarr>

<tML-TABase:EscalationList>

<tML-TABase:EscalationItem>

<tML-TABase:State>2</tML-TABase:State>

<tML-TABase:EscTime>2002-09-12T13:25:00Z</tML-TABase:EscTime>

<tML-TABase:Level>2</tML-TABase:Level>

<tML-TABase:EscPerson>

<tML-TABase:Name>My Escalation Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:EscPerson>

</tML-TABase:EscalationItem>

</tML-TABase:EscalationList>

<tML-TABase:OutageDuration>

<tML-TABase:TimeInterval>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:TimeInterval>

</tML-TABase:OutageDuration>

<tML-TABase:RestoredTime>2002-09-14T13:25:00Z</tML-TABase:RestoredTime>

<tML-TABase:TroubleFound>

<tML-TABase:Number>2</tML-TABase:Number>

</tML-TABase:TroubleFound>

<tML-TABase:TroubleReportState>1</tML-TABase:TroubleReportState>

<tML-TABase:TroubleReportStatus>

<tML-TABase:Number>8</tML-TABase:Number>

</tML-TABase:TroubleReportStatus>

<tML-TABase:TroubleReportStatusTime>2002-09-12T13:25:00Z</tML-TABase:TroubleReportStatusTime>

</EventData>

</AttributeValueChangeNotification>

### Access Carrier and/or Retail Customers

<?xml version="1.0" encoding="UTF-8"?>

<AttributeValueChangeNotification

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<NotificationId>123</NotificationId>

<EventTime>2002-09-12T13:25:00Z</EventTime>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>VZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ABC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<EventData>

<tML-TABase:ActivityDurationList>

<tML-TABase:ActivityDurationItem>

<tML-TABase:Duration>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:Duration>

<tML-TABase:Billable>true</tML-TABase:Billable>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>true</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>true</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

</tML-TABase:ActivityDurationItem>

</tML-TABase:ActivityDurationList>

<tML-TABase:AdditionalTroubleStatusInfo>

<tML-TABase:AdditionalTroubleStatusInfoItem>testing...</tML-TABase:AdditionalTroubleStatusInfoItem>

<tML-TABase:AdditionalTroubleStatusInfoItem>dispatched</tML-TABase:AdditionalTroubleStatusInfoItem>

</tML-TABase:AdditionalTroubleStatusInfo>

<tML-TABase:AuthorizationList>

<tML-TABase:AuthorizationItem>

<tML-TABase:State>1</tML-TABase:State>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>false</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>false</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>false</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>false</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>true</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

</tML-TABase:AuthorizationItem>

<tML-TABase:AuthorizationItem>

<tML-TABase:State>2</tML-TABase:State>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>false</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>false</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

<tML-TABase:AuthTime>2002-09-12T13:25:00Z</tML-TABase:AuthTime>

<tML-TABase:AuthPerson>

<tML-TABase:Name>My Auth Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AuthPerson>

</tML-TABase:AuthorizationItem>

</tML-TABase:AuthorizationList>

<tML-TABase:CloseOutNarr>It is time to put an end on this…</tML-TABase:CloseOutNarr>

<tML-TABase:EscalationList>

<tML-TABase:EscalationItem>

<tML-TABase:State>2</tML-TABase:State>

<tML-TABase:EscTime>2002-09-12T13:25:00Z</tML-TABase:EscTime>

<tML-TABase:Level>2</tML-TABase:Level>

<tML-TABase:EscPerson>

<tML-TABase:Name>My Escalation Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:EscPerson>

</tML-TABase:EscalationItem>

</tML-TABase:EscalationList>

<tML-TABase:OutageDuration>

<tML-TABase:TimeInterval>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:TimeInterval>

</tML-TABase:OutageDuration>

<tML-TABase:RestoredTime>2002-09-14T13:25:00Z</tML-TABase:RestoredTime>

<tML-TABase:TroubleFound>

<tML-TABase:Number>2</tML-TABase:Number>

</tML-TABase:TroubleFound>

<tML-TABase:TroubleReportState>1</tML-TABase:TroubleReportState>

<tML-TABase:TroubleReportStatus>

<tML-TABase:Number>8</tML-TABase:Number>

</tML-TABase:TroubleReportStatus>

<tML-TABase:TroubleReportStatusTime>2002-09-12T13:25:00Z</tML-TABase:TroubleReportStatusTime>

</EventData>

</AttributeValueChangeNotification>

## Sample tML for Trouble Report Close Out Notification

### Trouble Report Close Out Notification

<?xml version="1.0" encoding="UTF-8"?>

<AttributeValueChangeNotification

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<NotificationId>123</NotificationId>

<EventTime>2002-09-12T13:25:00Z</EventTime>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<EventData>

<tML-TABase:TroubleFound>

<tML-TABase:Number>3</tML-TABase:Number>

</tML-TABase:TroubleFound>

<tML-TABase:ActivityDurationList>

<tML-TABase:ActivityDurationItem>

<tML-TABase:Duration>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:Duration>

<tML-TABase:Billable>true</tML-TABase:Billable>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>true</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>true</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

</tML-TABase:ActivityDurationItem>

</tML-TABase:ActivityDurationList>

<tML-TABase:CloseOutNarr>It is time to put an end on this</tML-TABase:CloseOutNarr>

<tML-TABase:OutageDuration>

<tML-TABase:TimeInterval>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:TimeInterval>

</tML-TABase:OutageDuration>

<tML-TABase:RestoredTime>2002-09-14T13:25:00Z</tML-TABase:RestoredTime>

<tML-TABase:TroubleFound>

<tML-TABase:Number>2</tML-TABase:Number>

</tML-TABase:TroubleFound>

<tML-TABase:TroubleReportState>3</tML-TABase:TroubleReportState>

<tML-TABase:TroubleReportStatus>

<tML-TABase:Number>26</tML-TABase:Number>

</tML-TABase:TroubleReportStatus>

<tML-TABase:TroubleReportStatusTime>2002-09-12T13:25:00Z</tML-TABase:TroubleReportStatusTime>

</EventData>

</AttributeValueChangeNotification>

## Sample tML for Retrieve Trouble Report Attributes

Other than retrieving Trouble Reports created in TAXI system,  this transaction can also be used to perform Trouble Ticket late bonding, please refer to Annex E	Trouble Ticket Late Bonding

### Local Customers

#### Retrieve Trouble Report Attributes Request

T1.278 standard failed to define elements under “<RetrieveAttribute>”.  As a result,  different partners implemented their own tags.  TAXI support following three forms of RetrieveAttributesByTroubleReportIdRequest.  The first of these forms are preferred over the other two.

- Preferred format

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveAttributesByTroubleReportIdRequest

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA tML-TA.xsd">

<RequestId>abc123</RequestId>

<Customer>

<tML-TABase:UserId>WSEATTL01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>CLEC</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<RetrieveAttributes>

<tML-TABase:AttributeIDItem>ActivityDuration</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AdditionalTroubleInfoList</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AdditonalTroubleStatusInfo</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AgentContactPerson</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ALocationAccessHours</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ALocationAccessAddress</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ALocationAccessPerson</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AuthorizationList</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CalledNumber</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CancelRequestedByManager</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CloseOutNarr</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CloseOutVerification</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CommitmentTime</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CommitmentTimeRequest</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CustomerTroubleTickNum</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CustomerWorkCenter</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>EscalationList</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>InitiatingMode</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ManagerObjectAccessHours</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ManagedObjectInstance</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ManagedObjectInstanceAliasList</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ManagerContactPerson</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>OutageDuration</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>PerceivedTroubleSeverity</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>PreferredPriority</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ReceivedTime</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>RepeatReport</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>RestoredTime</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleClearancePerson</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleDetectionTime</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleFound</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleReportState</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleReportStatus</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleReportStatusTime</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleReportStatusWindow</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleType</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TspPriority</tML-TABase:AttributeIDItem>

</RetrieveAttributes>

</RetrieveAttributesByTroubleReportIdRequest>

2,  Other forms of RetrieveAttributes transaction that Verizon also accept.  But their uses are discouraged.

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveAttributesByTroubleReportIdRequest

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA tML-TA.xsd">

<RequestId>abc123</RequestId>

<Customer>

<tML-TABase:UserId>WSEATTL01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>CLEC</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<AttributeList>

<tML-TABase:AttributeIDItem>ActivityDuration</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AdditionalTroubleInfoList</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AdditonalTroubleStatusInfo</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AgentContactPerson</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ALocationAccessHours</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ALocationAccessAddress</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ALocationAccessPerson</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AuthorizationList</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CalledNumber</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CancelRequestedByManager</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CloseOutNarr</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CloseOutVerification</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CommitmentTime</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CommitmentTimeRequest</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CustomerTroubleTickNum</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CustomerWorkCenter</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>EscalationList</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>InitiatingMode</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ManagerObjectAccessHours</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ManagedObjectInstance</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ManagedObjectInstanceAliasList</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ManagerContactPerson</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>OutageDuration</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>PerceivedTroubleSeverity</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>PreferredPriority</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ReceivedTime</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>RepeatReport</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>RestoredTime</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleClearancePerson</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleDetectionTime</tML-TABase:AttributeIDItem>

</AttributeList>

</RetrieveAttributesByTroubleReportIdRequest>

3.  Other forms of RetrieveAttributes transaction that Verizon also accept.  But their uses are discouraged.

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveAttributesByTroubleReportIdRequest

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA tML-TA.xsd">

<RequestId>abc123</RequestId>

<Customer>

<tML-TABase:UserId>WSEATTL01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>CLEC</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<RetrieveAttributes>

<ActivityDurationList>true<ActivityDurationList>

<AdditionalTroubleInfoList>true<AdditionalTroubleInfoList>

<AdditionalTroubleStatusInfo>true<AdditionalTroubleStatusInfo>

<AgentContactPerson>true<AgentContactPerson>

<AfterHrsRepairAuth>true<AfterHrsRepairAuth>

<ALocationAccessHours>true<ALocationAccessHours>

<ALocationAccessAddress>true<ALocationAccessAddress>

<ALocationAccessPerson>true<ALocationAccessPerson>

<AuthorizationList>true<AuthorizationList>

<CalledNumber>true<CalledNumber>

<CancelRequestedByManager>true<CancelRequestedByManager>

<CloseOutNarr>true<CloseOutNarr>

<CloseOutVerification>true<CloseOutVerification>

<CommitmentTime>true<CommitmentTime>

<CommitmentTimeRequest>true<CommitmentTimeRequest>

<CustomerTroubleTickNum>true<CustomerTroubleTickNum>

<CustomerWorkCenter>true<CustomerWorkCenter>

<EscalationList>true<EscalationList>

<OutageDuration>true<OutageDuration>

<PerceivedTroubleSeverity>true<PerceivedTroubleSeverity>

<PreferredPriority>true<PreferredPriority>

<ReceivedTime>true<ReceivedTime>

<RelatedTroubleReportList>true<RelatedTroubleReportList>

<RepairActivityList>true<RepairActivityList>

<RepeatReport>true<RepeatReport>

<ResponsiblePerson>true<ResponsiblePerson>

<RestoredTime>true<RestoredTime>

<TroubleClearancePerson>true<TroubleClearancePerson>

<TroubleDetectionTime>true<TroubleDetectionTime>

<TroubleReportId>true<TroubleReportId>

<TroubleReportFormatId>true<TroubleReportFormatId>

</RetrieveAttributes>

</RetrieveAttributesByTroubleReportIdRequest>

#### Retrieve Trouble Report Attributes Response

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveAttributesByTroubleReportIdResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<Normal>

<tML-TABase:ActivityDuration>

<tML-TABase:ActivityDurationItem>

<tML-TABase:Duration>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:Duration>

<tML-TABase:Billable>true</tML-TABase:Billable>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>true</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>true</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

</tML-TABase:ActivityDurationItem>

</tML-TABase:ActivityDuration>

<tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:AdditionalTroubleInfoItem>trouble narrative</tML-TABase:AdditionalTroubleInfoItem>

</tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:AdditionalTroubleStatusInfo>

<tML-TABase:AdditionalTroubleStatusInfoItem>repair is in progress</tML-TABase:AdditionalTroubleStatusInfoItem>

</tML-TABase:AdditionalTroubleStatusInfo>

<tML-TABase:AgentContactPerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AgentContactPerson>

<tML-TABase:ALocationAccessHours>

<tML-TABase:LocationAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:LocationAccessHoursItem>

</tML-TABase:ALocationAccessHours>

<tML-TABase:ALocationAccessAddress>

<tML-TABase:PremisesName>My ocean Beach Home</tML-TABase:PremisesName>

<tML-TABase:PremisesAddress>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:PremisesAddress>

</tML-TABase:ALocationAccessAddress>

<tML-TABase:ALocationAccessPerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:ALocationAccessPerson>

<tML-TABase:AuthorizationList>

<tML-TABase:AuthorizationItem>

<tML-TABase:State>1</tML-TABase:State>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>false</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>false</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

<tML-TABase:AuthTime>2002-09-12T13:25:00Z</tML-TABase:AuthTime>

<tML-TABase:AuthPerson>

<tML-TABase:Name>My Auth Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AuthPerson>

</tML-TABase:AuthorizationItem>

</tML-TABase:AuthorizationList>

<tML-TABase:CalledNumber>7039746778</tML-TABase:CalledNumber>

<tML-TABase:CloseOutNarr>It is time to put an end on this</tML-TABase:CloseOutNarr>

<tML-TABase:CloseOutVerification>1</tML-TABase:CloseOutVerification>

<tML-TABase:CommitmentTime>

<tML-TABase:OnsiteTime>2002-09-16T13:25:00Z</tML-TABase:OnsiteTime>

</tML-TABase:CommitmentTime>

<tML-TABase:CommitmentTimeRequest>

<tML-TABase:OnsiteTime>2002-09-12T13:25:00Z</tML-TABase:OnsiteTime>

</tML-TABase:CommitmentTimeRequest>

<tML-TABase:CustomerTroubleTickNum>CLECTicket123</tML-TABase:CustomerTroubleTickNum>

<tML-TABase:CustomerWorkCenter>abc</tML-TABase:CustomerWorkCenter>

<tML-TABase:EscalationList>

<tML-TABase:EscalationItem>

<tML-TABase:State>1</tML-TABase:State>

<tML-TABase:EscTime>2002-09-12T13:25:00Z</tML-TABase:EscTime>

<tML-TABase:RequestPerson>

<tML-TABase:Name>My Request Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:RequestPerson>

<tML-TABase:Level>2</tML-TABase:Level>

<tML-TABase:EscPerson>

<tML-TABase:Name>My Escalation Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:EscPerson>

</tML-TABase:EscalationItem>

</tML-TABase:EscalationList>

<tML-TABase:InitiatingMode>0</tML-TABase:InitiatingMode>

<tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:ManagedObjectAccessHoursItem>

</tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</tML-TABase:ManagedObjectInstance>

<tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagedObjectInstanceAliasItem>Service Alias Name</tML-TABase:ManagedObjectInstanceAliasItem>

</tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagerContactPerson>

<tML-TABase:Name>Manager Contact Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:ManagerContactPerson>

<tML-TABase:OutageDuration>

<tML-TABase:TimeInterval>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:TimeInterval>

</tML-TABase:OutageDuration>

<tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:Number>0</tML-TABase:Number>

</tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:PreferredPriority>3</tML-TABase:PreferredPriority>

<tML-TABase:ReceivedTime>2002-09-12T13:20:00Z</tML-TABase:ReceivedTime>

<tML-TABase:RepeatReport>2</tML-TABase:RepeatReport>

<tML-TABase:RestoredTime>2002-09-14T13:40:00Z</tML-TABase:RestoredTime>

<tML-TABase:TroubleClearancePerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:TroubleClearancePerson>

<tML-TABase:TroubleDetectionTime>2002-09-12T13:25:00Z</tML-TABase:TroubleDetectionTime>

<tML-TABase:TroubleFound>

<tML-TABase:Number>3</tML-TABase:Number>

</tML-TABase:TroubleFound>

<tML-TABase:TroubleReportState>0</tML-TABase:TroubleReportState>

<tML-TABase:TroubleReportStatus>

<tML-TABase:Number>2</tML-TABase:Number>

</tML-TABase:TroubleReportStatus>

<tML-TABase:TroubleReportStatusTime>2002-09-12T13:25:00Z</tML-TABase:TroubleReportStatusTime>

<tML-TABase:TroubleReportStatusWindow>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:TroubleReportStatusWindow>

<tML-TABase:TroubleType>

<tML-TABase:Number>100</tML-TABase:Number>

</tML-TABase:TroubleType>

<tML-TABase:TspPriority>5E</tML-TABase:TspPriority>

</Normal>

</RetrieveAttributesByTroubleReportIdResponse>

#### Retrieve Trouble Report Attributes Response – Partial Success

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveAttributesByTroubleReportIdResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<Normal>

<tML-TABase:ActivityDuration>

<tML-TABase:ActivityDurationItem>

<tML-TABase:Duration>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:Duration>

<tML-TABase:Billable>true</tML-TABase:Billable>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>true</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>true</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

</tML-TABase:ActivityDurationItem>

</tML-TABase:ActivityDuration>

<tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:AdditionalTroubleInfoItem>trouble narrative</tML-TABase:AdditionalTroubleInfoItem>

</tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:AdditionalTroubleStatusInfo>

<tML-TABase:AdditionalTroubleStatusInfoItem>repair is in progress</tML-TABase:AdditionalTroubleStatusInfoItem>

</tML-TABase:AdditionalTroubleStatusInfo>

<tML-TABase:AgentContactPerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AgentContactPerson>

<tML-TABase:ALocationAccessHours>

<tML-TABase:LocationAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:LocationAccessHoursItem>

</tML-TABase:ALocationAccessHours>

<tML-TABase:ALocationAccessAddress>

<tML-TABase:PremisesName>My ocean Beach Home</tML-TABase:PremisesName>

<tML-TABase:PremisesAddress>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:PremisesAddress>

</tML-TABase:ALocationAccessAddress>

<tML-TABase:ALocationAccessPerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:ALocationAccessPerson>

<tML-TABase:AuthorizationList>

<tML-TABase:AuthorizationItem>

<tML-TABase:State>1</tML-TABase:State>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>false</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>false</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

<tML-TABase:AuthTime>2002-09-12T13:25:00Z</tML-TABase:AuthTime>

<tML-TABase:AuthPerson>

<tML-TABase:Name>My Auth Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AuthPerson>

</tML-TABase:AuthorizationItem>

</tML-TABase:AuthorizationList>

<tML-TABase:CalledNumber>7039746778</tML-TABase:CalledNumber>

<tML-TABase:CommitmentTime>

<tML-TABase:OnsiteTime>2002-09-16T13:25:00Z</tML-TABase:OnsiteTime>

</tML-TABase:CommitmentTime>

<tML-TABase:CommitmentTimeRequest>

<tML-TABase:OnsiteTime>2002-09-12T13:25:00Z</tML-TABase:OnsiteTime>

</tML-TABase:CommitmentTimeRequest>

<tML-TABase:CustomerTroubleTickNum>CLECTicket123</tML-TABase:CustomerTroubleTickNum>

<tML-TABase:CustomerWorkCenter>abc</tML-TABase:CustomerWorkCenter>

<tML-TABase:EscalationList>

<tML-TABase:EscalationItem>

<tML-TABase:State>1</tML-TABase:State>

<tML-TABase:EscTime>2002-09-12T13:25:00Z</tML-TABase:EscTime>

<tML-TABase:RequestPerson>

<tML-TABase:Name>My Request Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:RequestPerson>

<tML-TABase:Level>2</tML-TABase:Level>

<tML-TABase:EscPerson>

<tML-TABase:Name>My Escalation Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:EscPerson>

</tML-TABase:EscalationItem>

</tML-TABase:EscalationList>

<tML-TABase:InitiatingMode>0</tML-TABase:InitiatingMode>

<tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:ManagedObjectAccessHoursItem>

</tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</tML-TABase:ManagedObjectInstance>

<tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagedObjectInstanceAliasItem>7039746778</tML-TABase:ManagedObjectInstanceAliasItem>

</tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagerContactPerson>

<tML-TABase:Name>Manager Contact Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:ManagerContactPerson>

<tML-TABase:OutageDuration>

<tML-TABase:TimeInterval>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:TimeInterval>

</tML-TABase:OutageDuration>

<tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:Number>0</tML-TABase:Number>

</tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:PreferredPriority>3</tML-TABase:PreferredPriority>

<tML-TABase:ReceivedTime>2002-09-12T13:20:00Z</tML-TABase:ReceivedTime>

<tML-TABase:RepeatReport>2</tML-TABase:RepeatReport>

<tML-TABase:RestoredTime>2002-09-14T13:40:00Z</tML-TABase:RestoredTime>

<tML-TABase:TroubleClearancePerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:TroubleClearancePerson>

<tML-TABase:TroubleDetectionTime>2002-09-12T13:25:00Z</tML-TABase:TroubleDetectionTime>

<tML-TABase:TroubleFound>

<tML-TABase:Number>3</tML-TABase:Number>

</tML-TABase:TroubleFound>

<tML-TABase:TroubleReportState>0</tML-TABase:TroubleReportState>

<tML-TABase:TroubleReportStatus>

<tML-TABase:Number>2</tML-TABase:Number>

</tML-TABase:TroubleReportStatus>

<tML-TABase:TroubleReportStatusTime>2002-09-12T13:25:00Z</tML-TABase:TroubleReportStatusTime>

<tML-TABase:TroubleReportStatusWindow>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:TroubleReportStatusWindow>

<tML-TABase:TroubleType>

<tML-TABase:Number>100</tML-TABase:Number>

</tML-TABase:TroubleType>

</Normal>

<Exception>

<tML-TABase:MissingData>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>xxxx</tML-TABase:Tag>

<tML-TABase:Value>TroubleReportStatusWindow</tML-TABase:Value>

</tML-TABase:ExceptionList>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>xxxx</tML-TABase:Tag>

<tML-TABase:Value>ManagedObjectInstanceAliasList</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:MissingData>

</Exception>

</RetrieveAttributesByTroubleReportIdResponse>

#### Retrieve Trouble Report Attributes Response – Exception

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveAttributesByTroubleReportIdResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<Exception>

<tML-TABase:ProcessingFailure>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>0003</tML-TABase:Tag>

<tML-TABase:Value>System Not Responding: Time Out Error</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:ProcessingFailure>

</Exception>

</RetrieveAttributesByTroubleReportIdResponse>

### Access Carrier and/or Retail Customers

#### Retrieve Trouble Report Attributes Request

T1.278 standard failed to define elements under “<RetrieveAttribute>”.  As a result,  different partners implemented their own tags.  TAXI support following three forms of RetrieveAttributesByTroubleReportIdRequest.  The first of these forms are preferred over the other two.

- Preferred format

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveAttributesByTroubleReportIdRequest

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA tML-TA.xsd">

<RequestId>abc123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>Carrier</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<RetrieveAttributes>

<tML-TABase:AttributeIDItem>ActivityDuration</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AdditionalTroubleInfoList</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AdditonalTroubleStatusInfo</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AgentContactPerson</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ALocationAccessHours</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ALocationAccessAddress</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ALocationAccessPerson</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AuthorizationList</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CalledNumber</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CancelRequestedByManager</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CloseOutNarr</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CloseOutVerification</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CommitmentTime</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CommitmentTimeRequest</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CustomerTroubleTickNum</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CustomerWorkCenter</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>EscalationList</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>InitiatingMode</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ManagerObjectAccessHours</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ManagedObjectInstance</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ManagedObjectInstanceAliasList</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ManagerContactPerson</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>OutageDuration</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>PerceivedTroubleSeverity</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>PreferredPriority</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ReceivedTime</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>RepeatReport</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>RestoredTime</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleClearancePerson</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleDetectionTime</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleFound</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleReportState</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleReportStatus</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleReportStatusTime</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleReportStatusWindow</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleType</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TspPriority</tML-TABase:AttributeIDItem>

</RetrieveAttributes>

</RetrieveAttributesByTroubleReportIdRequest>

2,  Other forms of RetrieveAttributes transaction that Verizon also accept.  But their uses are discouraged.

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveAttributesByTroubleReportIdRequest

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA tML-TA.xsd">

<RequestId>abc123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>Carrier</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<AttributeList>

<tML-TABase:AttributeIDItem>ActivityDuration</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AdditionalTroubleInfoList</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AdditonalTroubleStatusInfo</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AgentContactPerson</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ALocationAccessHours</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ALocationAccessAddress</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ALocationAccessPerson</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AuthorizationList</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CalledNumber</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CancelRequestedByManager</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CloseOutNarr</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CloseOutVerification</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CommitmentTime</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CommitmentTimeRequest</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CustomerTroubleTickNum</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>CustomerWorkCenter</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>EscalationList</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>InitiatingMode</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ManagerObjectAccessHours</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ManagedObjectInstance</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ManagedObjectInstanceAliasList</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ManagerContactPerson</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>OutageDuration</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>PerceivedTroubleSeverity</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>PreferredPriority</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>ReceivedTime</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>RepeatReport</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>RestoredTime</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleClearancePerson</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>TroubleDetectionTime</tML-TABase:AttributeIDItem>

</AttributeList>

</RetrieveAttributesByTroubleReportIdRequest>

3.  Other forms of RetrieveAttributes transaction that Verizon also accept.  But their uses are discouraged.

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveAttributesByTroubleReportIdRequest

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA tML-TA.xsd">

<RequestId>abc123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>Carrier</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<RetrieveAttributes>

<ActivityDuration>true<ActivityDuration>

<AdditionalTroubleInfoList>true<AdditionalTroubleInfoList>

<AdditionalTroubleStatusInfo>true<AdditionalTroubleStatusInfo>

<AgentContactPerson>true<AgentContactPerson>

<AfterHrsRepairAuth>true<AfterHrsRepairAuth>

<ALocationAccessHours>true<ALocationAccessHours>

<ALocationAccessAddress>true<ALocationAccessAddress>

<ALocationAccessPerson>true<ALocationAccessPerson>

<AuthorizationList>true<AuthorizationList>

<CalledNumber>true<CalledNumber>

<CancelRequestedByManager>true<CancelRequestedByManager>

<CloseOutNarr>true<CloseOutNarr>

<CloseOutVerification>true<CloseOutVerification>

<CommitmentTime>true<CommitmentTime>

<CommitmentTimeRequest>true<CommitmentTimeRequest>

<CustomerTroubleTickNum>true<CustomerTroubleTickNum>

<CustomerWorkCenter>true<CustomerWorkCenter>

<EscalationList>true<EscalationList>

<OutageDuration>true<OutageDuration>

<PerceivedTroubleSeverity>true<PerceivedTroubleSeverity>

<PreferredPriority>true<PreferredPriority>

<ReceivedTime>true<ReceivedTime>

<RelatedTroubleReportList>true<RelatedTroubleReportList>

<RepairActivityList>true<RepairActivityList>

<RepeatReport>true<RepeatReport>

<ResponsiblePerson>true<ResponsiblePerson>

<RestoredTime>true<RestoredTime>

<TroubleClearancePerson>true<TroubleClearancePerson>

<TroubleDetectionTime>true<TroubleDetectionTime>

<TroubleReportId>true<TroubleReportId>

<TroubleReportFormatId>true<TroubleReportFormatId>

</RetrieveAttributes>

</RetrieveAttributesByTroubleReportIdRequest>

#### Retrieve Trouble Report Attributes Response

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveAttributesByTroubleReportIdResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<Normal>

<tML-TABase:ActivityDuration>

<tML-TABase:ActivityDurationItem>

<tML-TABase:Duration>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:Duration>

<tML-TABase:Billable>true</tML-TABase:Billable>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>true</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>true</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

</tML-TABase:ActivityDurationItem>

</tML-TABase:ActivityDuration>

<tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:AdditionalTroubleInfoItem>trouble narrative</tML-TABase:AdditionalTroubleInfoItem>

</tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:AdditionalTroubleStatusInfo>

<tML-TABase:AdditionalTroubleStatusInfoItem>repair is in progress</tML-TABase:AdditionalTroubleStatusInfoItem>

</tML-TABase:AdditionalTroubleStatusInfo>

<tML-TABase:AgentContactPerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AgentContactPerson>

<tML-TABase:ALocationAccessHours>

<tML-TABase:LocationAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:LocationAccessHoursItem>

</tML-TABase:ALocationAccessHours>

<tML-TABase:ALocationAccessAddress>

<tML-TABase:PremisesName>My ocean Beach Home</tML-TABase:PremisesName>

<tML-TABase:PremisesAddress>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:PremisesAddress>

</tML-TABase:ALocationAccessAddress>

<tML-TABase:ALocationAccessPerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:ALocationAccessPerson>

<tML-TABase:AuthorizationList>

<tML-TABase:AuthorizationItem>

<tML-TABase:State>1</tML-TABase:State>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>false</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>false</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

<tML-TABase:AuthTime>2002-09-12T13:25:00Z</tML-TABase:AuthTime>

<tML-TABase:AuthPerson>

<tML-TABase:Name>My Auth Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AuthPerson>

</tML-TABase:AuthorizationItem>

</tML-TABase:AuthorizationList>

<tML-TABase:CalledNumber>7039746778</tML-TABase:CalledNumber>

<tML-TABase:CloseOutNarr>It is time to put an end on this</tML-TABase:CloseOutNarr>

<tML-TABase:CloseOutVerification>1</tML-TABase:CloseOutVerification>

<tML-TABase:CustomerTroubleTickNum>CLECTicket123</tML-TABase:CustomerTroubleTickNum>

<tML-TABase:CustomerWorkCenter>abc</tML-TABase:CustomerWorkCenter>

<tML-TABase:EscalationList>

<tML-TABase:EscalationItem>

<tML-TABase:State>1</tML-TABase:State>

<tML-TABase:EscTime>2002-09-12T13:25:00Z</tML-TABase:EscTime>

<tML-TABase:RequestPerson>

<tML-TABase:Name>My Request Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:RequestPerson>

<tML-TABase:Level>2</tML-TABase:Level>

<tML-TABase:EscPerson>

<tML-TABase:Name>My Escalation Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:EscPerson>

</tML-TABase:EscalationItem>

</tML-TABase:EscalationList>

<tML-TABase:InitiatingMode>0</tML-TABase:InitiatingMode>

<tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:ManagedObjectAccessHoursItem>

</tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</tML-TABase:ManagedObjectInstance>

<tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagedObjectInstanceAliasItem>Service Alias Name</tML-TABase:ManagedObjectInstanceAliasItem>

</tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagerContactPerson>

<tML-TABase:Name>Manager Contact Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:ManagerContactPerson>

<tML-TABase:OutageDuration>

<tML-TABase:TimeInterval>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:TimeInterval>

</tML-TABase:OutageDuration>

<tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:Number>0</tML-TABase:Number>

</tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:PreferredPriority>3</tML-TABase:PreferredPriority>

<tML-TABase:ReceivedTime>2002-09-12T13:20:00Z</tML-TABase:ReceivedTime>

<tML-TABase:RepeatReport>2</tML-TABase:RepeatReport>

<tML-TABase:RestoredTime>2002-09-14T13:40:00Z</tML-TABase:RestoredTime>

<tML-TABase:TroubleClearancePerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:TroubleClearancePerson>

<tML-TABase:TroubleDetectionTime>2002-09-12T13:25:00Z</tML-TABase:TroubleDetectionTime>

<tML-TABase:TroubleFound>

<tML-TABase:Number>3</tML-TABase:Number>

</tML-TABase:TroubleFound>

<tML-TABase:TroubleReportState>0</tML-TABase:TroubleReportState>

<tML-TABase:TroubleReportStatus>

<tML-TABase:Number>2</tML-TABase:Number>

</tML-TABase:TroubleReportStatus>

<tML-TABase:TroubleReportStatusTime>2002-09-12T13:25:00Z</tML-TABase:TroubleReportStatusTime>

<tML-TABase:TroubleReportStatusWindow>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:TroubleReportStatusWindow>

<tML-TABase:TroubleType>

<tML-TABase:Number>100</tML-TABase:Number>

</tML-TABase:TroubleType>

<tML-TABase:TspPriority>5E</tML-TABase:TspPriority>

</Normal>

</RetrieveAttributesByTroubleReportIdResponse>

#### Retrieve Trouble Report Attributes Response – Partial Success

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveAttributesByTroubleReportIdResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<Normal>

<tML-TABase:ActivityDuration>

<tML-TABase:ActivityDurationItem>

<tML-TABase:Duration>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:Duration>

<tML-TABase:Billable>true</tML-TABase:Billable>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>true</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>true</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

</tML-TABase:ActivityDurationItem>

</tML-TABase:ActivityDuration>

<tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:AdditionalTroubleInfoItem>trouble narrative</tML-TABase:AdditionalTroubleInfoItem>

</tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:AdditionalTroubleStatusInfo>

<tML-TABase:AdditionalTroubleStatusInfoItem>repair is in progress</tML-TABase:AdditionalTroubleStatusInfoItem>

</tML-TABase:AdditionalTroubleStatusInfo>

<tML-TABase:AgentContactPerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AgentContactPerson>

<tML-TABase:ALocationAccessHours>

<tML-TABase:LocationAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:LocationAccessHoursItem>

</tML-TABase:ALocationAccessHours>

<tML-TABase:ALocationAccessAddress>

<tML-TABase:PremisesName>My ocean Beach Home</tML-TABase:PremisesName>

<tML-TABase:PremisesAddress>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:PremisesAddress>

</tML-TABase:ALocationAccessAddress>

<tML-TABase:ALocationAccessPerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:ALocationAccessPerson>

<tML-TABase:AuthorizationList>

<tML-TABase:AuthorizationItem>

<tML-TABase:State>1</tML-TABase:State>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>false</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>false</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

<tML-TABase:AuthTime>2002-09-12T13:25:00Z</tML-TABase:AuthTime>

<tML-TABase:AuthPerson>

<tML-TABase:Name>My Auth Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AuthPerson>

</tML-TABase:AuthorizationItem>

</tML-TABase:AuthorizationList>

<tML-TABase:CalledNumber>7039746778</tML-TABase:CalledNumber>

<tML-TABase:CustomerTroubleTickNum>CLECTicket123</tML-TABase:CustomerTroubleTickNum>

<tML-TABase:CustomerWorkCenter>abc</tML-TABase:CustomerWorkCenter>

<tML-TABase:EscalationList>

<tML-TABase:EscalationItem>

<tML-TABase:State>1</tML-TABase:State>

<tML-TABase:EscTime>2002-09-12T13:25:00Z</tML-TABase:EscTime>

<tML-TABase:RequestPerson>

<tML-TABase:Name>My Request Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:RequestPerson>

<tML-TABase:Level>2</tML-TABase:Level>

<tML-TABase:EscPerson>

<tML-TABase:Name>My Escalation Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:EscPerson>

</tML-TABase:EscalationItem>

</tML-TABase:EscalationList>

<tML-TABase:InitiatingMode>0</tML-TABase:InitiatingMode>

<tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:ManagedObjectAccessHoursItem>

</tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</tML-TABase:ManagedObjectInstance>

<tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagedObjectInstanceAliasItem>7039746778</tML-TABase:ManagedObjectInstanceAliasItem>

</tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagerContactPerson>

<tML-TABase:Name>Manager Contact Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:ManagerContactPerson>

<tML-TABase:OutageDuration>

<tML-TABase:TimeInterval>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:TimeInterval>

</tML-TABase:OutageDuration>

<tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:Number>0</tML-TABase:Number>

</tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:PreferredPriority>3</tML-TABase:PreferredPriority>

<tML-TABase:ReceivedTime>2002-09-12T13:20:00Z</tML-TABase:ReceivedTime>

<tML-TABase:RepeatReport>2</tML-TABase:RepeatReport>

<tML-TABase:RestoredTime>2002-09-14T13:40:00Z</tML-TABase:RestoredTime>

<tML-TABase:TroubleClearancePerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:TroubleClearancePerson>

<tML-TABase:TroubleDetectionTime>2002-09-12T13:25:00Z</tML-TABase:TroubleDetectionTime>

<tML-TABase:TroubleFound>

<tML-TABase:Number>3</tML-TABase:Number>

</tML-TABase:TroubleFound>

<tML-TABase:TroubleReportState>0</tML-TABase:TroubleReportState>

<tML-TABase:TroubleReportStatus>

<tML-TABase:Number>2</tML-TABase:Number>

</tML-TABase:TroubleReportStatus>

<tML-TABase:TroubleReportStatusTime>2002-09-12T13:25:00Z</tML-TABase:TroubleReportStatusTime>

<tML-TABase:TroubleReportStatusWindow>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:TroubleReportStatusWindow>

<tML-TABase:TroubleType>

<tML-TABase:Number>100</tML-TABase:Number>

</tML-TABase:TroubleType>

</Normal>

<Exception>

<tML-TABase:MissingData>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>xxxx</tML-TABase:Tag>

<tML-TABase:Value>TroubleReportStatusWindow</tML-TABase:Value>

</tML-TABase:ExceptionList>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>xxxx</tML-TABase:Tag>

<tML-TABase:Value>ManagedObjectInstanceAliasList</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:MissingData>

</Exception>

</RetrieveAttributesByTroubleReportIdResponse>

#### Retrieve Trouble Report Attributes Response – Exception

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveAttributesByTroubleReportIdResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>abc123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<Exception>

<tML-TABase:ProcessingFailure>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>0003</tML-TABase:Tag>

<tML-TABase:Value>System Not Responding: Time Out Error</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:ProcessingFailure>

</Exception>

</RetrieveAttributesByTroubleReportIdResponse>

## Sample tML for Multiple Trouble Report Create

This transaction is implemented for TAXI Local customer only at this time.

#### Multiple Trouble Report Create Request

<?xml version="1.0" encoding="UTF-8"?>

<MultiTroubleReportCreationRequest xmlns="http://www.ansi.org/tML/TA/tML-TA" xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA" xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA tML-TA.xsd ">

<RequestId>TRCreate123</RequestId>

<Customer>

<tML-TABase:UserId>WSEANYC01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>CLEC</tML-TABase:ServiceProfile>

</Customer>

<ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>NYVZL</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ANYC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>13/TXNU/123456//NY/</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<TroubleType>

<tML-TABase:Number>100</tML-TABase:Number>

</TroubleType>

<AdditionalTroubleInfoList>

<tML-TABase:AdditionalTroubleInfoItem>1234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456789012345678901234567890123456</tML-TABase:AdditionalTroubleInfoItem>

</AdditionalTroubleInfoList>

<AdditionalCreateInfo>

<tML-TABase:TroubleReportFormatId>1</tML-TABase:TroubleReportFormatId>

<tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:AdditionalTroubleInfoItem>some remark text regarding lead circuit or over all comments</tML-TABase:AdditionalTroubleInfoItem>

</tML-TABase:AdditionalTroubleInfoList>

<tML-TABase:ALocationAccessAddress>

<tML-TABase:PremisesName>John Doe</tML-TABase:PremisesName>

<tML-TABase:PremisesAddress>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:PremisesAddress>

</tML-TABase:ALocationAccessAddress>

<tML-TABase:ALocationAccessHours>

<tML-TABase:LocationAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:LocationAccessHoursItem>

</tML-TABase:ALocationAccessHours>

<tML-TABase:ALocationAccessPerson>

<tML-TABase:Number>2019940302</tML-TABase:Number>

<tML-TABase:Name>John Smith</tML-TABase:Name>

</tML-TABase:ALocationAccessPerson>

<tML-TABase:AuthorizationList>

<tML-TABase:AuthorizationItem>

<tML-TABase:State>2</tML-TABase:State>

<tML-TABase:Type>

<tML-TABase:AfterHoursRepair>false</tML-TABase:AfterHoursRepair>

<tML-TABase:Standby>false</tML-TABase:Standby>

<tML-TABase:AfterHoursStandby>false</tML-TABase:AfterHoursStandby>

<tML-TABase:Test>true</tML-TABase:Test>

<tML-TABase:ManagerInitiatedTest>false</tML-TABase:ManagerInitiatedTest>

<tML-TABase:Dispatch>true</tML-TABase:Dispatch>

<tML-TABase:NoAccess>false</tML-TABase:NoAccess>

<tML-TABase:DelayedMaintenance>false</tML-TABase:DelayedMaintenance>

<tML-TABase:Release>false</tML-TABase:Release>

<tML-TABase:DeregulatedWork>false</tML-TABase:DeregulatedWork>

</tML-TABase:Type>

<tML-TABase:AuthTime>2002-09-12T13:25:00Z</tML-TABase:AuthTime>

<tML-TABase:AuthPerson>

<tML-TABase:Number>7039478382</tML-TABase:Number>

<tML-TABase:Name>Operator</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AuthPerson>

</tML-TABase:AuthorizationItem>

</tML-TABase:AuthorizationList>

<tML-TABase:CalledNumber>7039746778</tML-TABase:CalledNumber>

<tML-TABase:CommitmentTimeRequest>

<tML-TABase:OnsiteTime>2002-09-12T13:25:00Z</tML-TABase:OnsiteTime>

</tML-TABase:CommitmentTimeRequest>

<tML-TABase:CustomerTroubleTickNum>CLECTicket123</tML-TABase:CustomerTroubleTickNum>

<tML-TABase:CustomerWorkCenter>abc</tML-TABase:CustomerWorkCenter>

<tML-TABase:EscalationList>

<tML-TABase:EscalationItem>

<tML-TABase:State>1</tML-TABase:State>

<tML-TABase:EscTime>2002-09-12T13:25:00Z</tML-TABase:EscTime>

<tML-TABase:RequestPerson>

<tML-TABase:Number>7039478382</tML-TABase:Number>

<tML-TABase:Name>My Request Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:RequestPerson>

<tML-TABase:Level>2</tML-TABase:Level>

</tML-TABase:EscalationItem>

</tML-TABase:EscalationList>

<tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:ManagedObjectAccessHoursItem>

</tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagedObjectInstanceAliasItem>Service Alias Name</tML-TABase:ManagedObjectInstanceAliasItem>

</tML-TABase:ManagedObjectInstanceAliasList>

<tML-TABase:ManagerContactPerson>

<tML-TABase:Number>7039478382</tML-TABase:Number>

<tML-TABase:Name>Manager Contact Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:ManagerContactPerson>

<tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:Number>0</tML-TABase:Number>

</tML-TABase:PerceivedTroubleSeverity>

<tML-TABase:PreferredPriority>3</tML-TABase:PreferredPriority>

<tML-TABase:RepeatReport>2</tML-TABase:RepeatReport>

<tML-TABase:TroubleDetectionTime>2002-09-12T13:25:00Z</tML-TABase:TroubleDetectionTime>

<tML-TABase:TroubleReportStatusWindow>

<tML-TABase:Day>5</tML-TABase:Day>

<tML-TABase:Hour>15</tML-TABase:Hour>

<tML-TABase:Minute>30</tML-TABase:Minute>

<tML-TABase:Second>0</tML-TABase:Second>

<tML-TABase:Msec>0</tML-TABase:Msec>

</tML-TABase:TroubleReportStatusWindow>

<tML-TABase:TspPriority>E2</tML-TABase:TspPriority>

</AdditionalCreateInfo>

<AdditionalCircuitList>

<tML-TABase:AdditionalCircuitItem>

<tML-TABase:CircuitId>20/TXNU/654321//NY/</tML-TABase:CircuitId>

<tML-TABase:MeetPoint>SPLT-OVC-002-03-095</tML-TABase:MeetPoint>

<tML-TABase:AssociatedTN>2123334444</tML-TABase:AssociatedTN>

</tML-TABase:AdditionalCircuitItem>

</AdditionalCircuitList>

</MultiTroubleReportCreationRequest>

#### Multiple Trouble Report Create Response – Normal

<?xml version="1.0" encoding="UTF-8"?>

<MultiTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA" 	xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" 	xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZL</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ANYC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>23/TXNU/123456//NY</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Normal>

<tML-TABase:InitiatingMode>0</tML-TABase:InitiatingMode>

<tML-TABase:ReceivedTime>2002-09-12T13:20:00Z</tML-TABase:ReceivedTime>

<tML-TABase:TroubleReportId>WNY123456</tML-TABase:TroubleReportId>

<tML-TABase:TroubleReportState>1</tML-TABase:TroubleReportState>

<tML-TABase:TroubleReportStatus>

<tML-TABase:Number>8</tML-TABase:Number>

</tML-TABase:TroubleReportStatus>

<tML-TABase:TroubleReportStatusTime>2002-09-12T13:25:00Z</tML-TABase:TroubleReportStatusTime>

<tML-TABase:AgentContactPerson>

<tML-TABase:Number>7039409302</tML-TABase:Number>

<tML-TABase:Name>Joe SMith</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Loc>

<tML-TABase:CivicAddress>1320 N Court House Rd</tML-TABase:CivicAddress>

<tML-TABase:City>Arlington</tML-TABase:City>

<tML-TABase:State>VA</tML-TABase:State>

<tML-TABase:Zip>22201</tML-TABase:Zip>

</tML-TABase:Loc>

<tML-TABase:Email>id AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Respon>No</tML-TABase:Respon>

<tML-TABase:Pager>18003334444</tML-TABase:Pager>

</tML-TABase:AgentContactPerson>

<tML-TABase:CommitmentTime>

<tML-TABase:OnsiteTime>2002-09-14T13:25:00Z</tML-TABase:OnsiteTime>

</tML-TABase:CommitmentTime>

<tML-TABase:AdditionalTroubleTicketList>

<tML-TABase:AdditionalTroubleTicketItem>

<tML-TABase:TroubleReportId>VNY1230001</tML-TABase:TroubleReportId>

<tML-TABase:CommitmentTime>

<tML-TABase:OnsiteTime>2002-09-14T13:25:00Z</tML-TABase:OnsiteTime>

</tML-TABase:CommitmentTime>

<tML-TABase:CircuitID>20/TXNU/1234567//GTEC</tML-TABase:CircuitID>

<tML-TABase:ErrorCode>0000</tML-TABase:ErrorCode>

<tML-TABase:ErrorDescription>Processing Successful</tML-TABase:ErrorDescription>

</tML-TABase:AdditionalTroubleTicketItem>

<tML-TABase:AdditionalTroubleTicketItem>

<tML-TABase:TroubleReportId>VNY1230002</tML-TABase:TroubleReportId>

<tML-TABase:CommitmentTime>

<tML-TABase:OnsiteTime>2002-09-14T13:25:00Z</tML-TABase:OnsiteTime>

</tML-TABase:CommitmentTime>

<tML-TABase:CircuitID>20/TXNU/1234999//GTEC</tML-TABase:CircuitID>

<tML-TABase:ErrorCode>0000</tML-TABase:ErrorCode>

<tML-TABase:ErrorDescription>Processing Successful</tML-TABase:ErrorDescription>

</tML-TABase:AdditionalTroubleTicketItem>

</tML-TABase:AdditionalTroubleTicketList>

</tML-TABase:Normal>

</CreateResponse>

</MultiTroubleReportCreationResponse>

#### Multiple Trouble Report Create Response – Exception (Trouble Report Already Exists)

For further processing regarding TroubleReportAlreadyExists exception, please refer to Annex E	Trouble Ticket Late Bonding

<?xml version="1.0" encoding="UTF-8"?>

<MultiTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Exception>

<tML-TABase:TroubleReportAlreadyExists>

<tML-TABase:ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>VNYSD23422</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</tML-TABase:ManagedObjectInstance>

<tML-TABase:TroubleReportId>VNYSD23422</tML-TABase:TroubleReportId>

</tML-TABase:TroubleReportAlreadyExists>

</tML-TABase:Exception>

</CreateResponse>

</MultiTroubleReportCreationResponse>

#### Multiple Trouble Report Create Response – Exception (Req Attributes Missing)

<?xml version="1.0" encoding="UTF-8"?>

<MultiTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Exception>

<tML-TABase:TRMustBePresentAttributeMissing>

<tML-TABase:AttributeIDItem>TroubleType</tML-TABase:AttributeIDItem>

<tML-TABase:AttributeIDItem>AdditionalTroubleInfoList</tML-TABase:AttributeIDItem>

</tML-TABase:TRMustBePresentAttributeMissing>

</tML-TABase:Exception>

</CreateResponse>

</MultiTroubleReportCreationResponse>

#### Multiple Trouble Report Create Response – Exception (Fall Back Reporting)

<?xml version="1.0" encoding="UTF-8"?>

<MultiTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Exception>

<tML-TABase:FallBackReporting>

Please report the trouble to Verizon enterprise office by calling 1-800-888-9999

Monday through Friday from 1 am to 11:59 pm (National and Verizon holidays excluded)

</tML-TABase:FallBackReporting>

</tML-TABase:Exception>

</CreateResponse>

</MultiTroubleReportCreationResponse>

#### Multiple Trouble Report Create Response – Exception (Invalid Data Received)

<?xml version="1.0" encoding="UTF-8"?>

<MultiTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA

tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Exception>

<tML-TABase:InvalidDataReceived>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>0002</tML-TABase:Tag>

<tML-TABase:Value>TroubleType</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:InvalidDataReceived>

</tML-TABase:Exception>

</CreateResponse>

</MultiTroubleReportCreationResponse>

#### Multiple Trouble Report Create Response – Exception (Processing Failure)

<?xml version="1.0" encoding="UTF-8"?>

<MultiTroubleReportCreationResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC Account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>Service ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<CreateResponse>

<tML-TABase:Exception>

<tML-TABase:ProcessingFailure>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>0003</tML-TABase:Tag>

<tML-TABase:Value>Java Runtime Exception:Array Index Out of Bound</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:ProcessingFailure>

</tML-TABase:Exception>

</CreateResponse>

</MultiTroubleReportCreationResponse>

## Sample tML for Quick Test

This trasaction is offered for Access customer only.

### Request

<?xml version="1.0" encoding="UTF-8"?>

<QuickTestRequest

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest.xsd">

<RequestId>L123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>Carrier</tML-TABase:ServiceProfile>

</Customer>

<ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ABC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>	33/XHGS/103432//GTEN</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<tML-ServiceTestBase:Acknowledgement>Y</tML-ServiceTestBase:Acknowledgement>

<tML-ServiceTestBase:StatusMessage>Y</tML-ServiceTestBase:StatusMessage>

<tML-ServiceTestBase:FinalDetail>Y</tML-ServiceTestBase:FinalDetail>

</QuickTestRequest>

### Acknowledgement

<?xml version="1.0" encoding="UTF-8"?>

<QuickTestResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest">

<RequestId>L123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>Carrier</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>

33/XHGS/103432//GTEN

</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectInstance>

<Normal>

<tML-ServiceTestBase:ResultType>ACK</tML-ServiceTestBase:ResultType>

<tML-ServiceTestBase:ReturnCode>0000</tML-ServiceTestBase:ReturnCode>

<tML-ServiceTestBase:InfoMessage></tML-ServiceTestBase:InfoMessage >

<tML-ServiceTestBase:ErrorMessage></tML-ServiceTestBase:ErrorMessage >

</Normal>

</QuickTestResponse>

### Intermediate Status

<?xml version="1.0" encoding="UTF-8"?>

<QuickTestResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest">

<RequestId>L123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>Carrier</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>

33/XHGS/103432//GTEN

</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectInstance>

<Normal>

<tML-ServiceTestBase:ReturnCode>0000</tML-ServiceTestBase:ReturnCode>

<tML-ServiceTestBase:ResultType>S</tML-ServiceTestBase:ResultType>

<tML-ServiceTestBase:InfoMessage>TEST OK</tML-ServiceTestBase:InfoMessage>

<tML-ServiceTestBase:Status>

<tML-ServiceTestBase:CircuitDescription></tML-ServiceTestBase:CircuitDescription>

<tML-ServiceTestBase:SummaryText></tML-ServiceTestBase:SummaryText>

<tML-ServiceTestBase:Disposition></tML-ServiceTestBase:Disposition>

<tML-ServiceTestBase:DescriptorsNumber>2</tML-ServiceTestBase:DescriptorsNumber>

<tML-ServiceTestBase:Descriptors>

<tML-ServiceTestBase:Descriptor>

<tML-ServiceTestBase:Index>1</tML-ServiceTestBase:Index>

<tML-ServiceTestBase:TestIdentifer></tML-ServiceTestBase:TestIdentifer>

<tML-ServiceTestBase:TargetIdentifier></tML-ServiceTestBase:TargetIdentifier>

<tML-ServiceTestBase:MacroStatus></tML-ServiceTestBase:MacroStatus>

<tML-ServiceTestBase:MacroDescription></tML-ServiceTestBase:MacroDescription>

</tML-ServiceTestBase:Descriptor>

<tML-ServiceTestBase:Descriptor>

<tML-ServiceTestBase:Index>2</tML-ServiceTestBase:Index>

<tML-ServiceTestBase:TestIdentifer></tML-ServiceTestBase:TestIdentifer>

<tML-ServiceTestBase:TargetIdentifier></tML-ServiceTestBase:TargetIdentifier>

<tML-ServiceTestBase:MacroStatus></tML-ServiceTestBase:MacroStatus>

<tML-ServiceTestBase:MacroDescription></tML-ServiceTestBase:MacroDescription>

</tML-ServiceTestBase:Descriptor>

</tML-ServiceTestBase:Descriptors>

</tML-ServiceTestBase:Status>

<tML-ServiceTestBase:Analysis>

<tML-ServiceTestBase:AnalysisItem>

<tML-ServiceTestBase:DiagnosisCode></tML-ServiceTestBase:DiagnosisCode>

<tML-ServiceTestBase:ShortSummary></tML-ServiceTestBase:ShortSummary>

<tML-ServiceTestBase:LongSummary></tML-ServiceTestBase:LongSummary>

</tML-ServiceTestBase:AnalysisItem>

</tML-ServiceTestBase:Analysis>

<tML-ServiceTestBase:Details></tML-ServiceTestBase:Details>

</Normal>

</QuickTestResponse>

### Final Response

<?xml version="1.0" encoding="UTF-8"?>

<QuickTestResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest">

<RequestId>L123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>Carrier</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>

33/XHGS/103432//GTEN

</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectInstance>

<Normal>

<tML-ServiceTestBase:ReturnCode>0000</tML-ServiceTestBase:ReturnCode>

<tML-ServiceTestBase:ResultType>C</tML-ServiceTestBase:ResultType>

<tML-ServiceTestBase:InfoMessage>TEST OK</tML-ServiceTestBase:InfoMessage>

<tML-ServiceTestBase:Status>

<tML-ServiceTestBase:CircuitDescription></tML-ServiceTestBase:CircuitDescription>

<tML-ServiceTestBase:SummaryText></tML-ServiceTestBase:SummaryText>

<tML-ServiceTestBase:Disposition></tML-ServiceTestBase:Disposition>

<tML-ServiceTestBase:DescriptorsNumber>2</tML-ServiceTestBase:DescriptorsNumber>

<tML-ServiceTestBase:Descriptors>

<tML-ServiceTestBase:Descriptor>

<tML-ServiceTestBase:Index>1</tML-ServiceTestBase:Index>

<tML-ServiceTestBase:TestIdentifer></tML-ServiceTestBase:TestIdentifer>

<tML-ServiceTestBase:TargetIdentifier></tML-ServiceTestBase:TargetIdentifier>

<tML-ServiceTestBase:MacroStatus></tML-ServiceTestBase:MacroStatus>

<tML-ServiceTestBase:MacroDescription></tML-ServiceTestBase:MacroDescription>

</tML-ServiceTestBase:Descriptor>

<tML-ServiceTestBase:Descriptor>

<tML-ServiceTestBase:Index>2</tML-ServiceTestBase:Index>

<tML-ServiceTestBase:TestIdentifer></tML-ServiceTestBase:TestIdentifer>

<tML-ServiceTestBase:TargetIdentifier></tML-ServiceTestBase:TargetIdentifier>

<tML-ServiceTestBase:MacroStatus></tML-ServiceTestBase:MacroStatus>

<tML-ServiceTestBase:MacroDescription></tML-ServiceTestBase:MacroDescription>

</tML-ServiceTestBase:Descriptor>

</tML-ServiceTestBase:Descriptors>

</tML-ServiceTestBase:Status>

<tML-ServiceTestBase:Analysis>

<tML-ServiceTestBase:AnalysisItem>

<tML-ServiceTestBase:DiagnosisCode></tML-ServiceTestBase:DiagnosisCode>

<tML-ServiceTestBase:ShortSummary></tML-ServiceTestBase:ShortSummary>

<tML-ServiceTestBase:LongSummary></tML-ServiceTestBase:LongSummary>

</tML-ServiceTestBase:AnalysisItem>

</tML-ServiceTestBase:Analysis>

<tML-ServiceTestBase:Details></tML-ServiceTestBase:Details>

</Normal>

</QuickTestResponse>

### Quick Test Response (Exception)

<?xml version="1.0" encoding="UTF-8"?>

<QuickTestResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest">

<RequestId>L123</RequestId>

<TargetObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>

33/XHGS/103432//GTEN

</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectInstance>

<Exception>

<tML-TABase:ProcessingFailure>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>0003</tML-TABase:Tag>

<tML-TABase:Value>System Down</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:ProcessingFailure>

</Exception>

</QuickTestResponse>

## Performance Monitoring

This trasaction is offered for Access customer only.

### Request

<?xml version="1.0" encoding="UTF-8"?>

<PerformanceMonitoringRequest

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest.xsd">

<RequestId>L123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>

Carrier

</tML-TABase:ServiceProfile>

</Customer>

<ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>

33/XHGS/103432//GTEN

</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<tML-ServiceTestBase:Acknowledgement>Y</tML-ServiceTestBase:Acknowledgement>

<tML-ServiceTestBase:StatusMessage>Y</tML-ServiceTestBase:StatusMessage>

<tML-ServiceTestBase:FinalDetail>Y</tML-ServiceTestBase:FinalDetail>

<tML-ServiceTestBase:Frequency>DAILY</tML-ServiceTestBase:Frequency>

<tML-ServiceTestBase:Interval>7</tML-ServiceTestBase:Interval>

</PerformanceMonitoringRequest>

### Acknowledgement

<?xml version="1.0" encoding="UTF-8"?>

<PerformanceMonitoringResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest">

<RequestId>L123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>

Carrier

</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>	33/XHGS/103432//GTEN</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectInstance>

<Normal>

<tML-ServiceTestBase:ResultType>ACK</tML-ServiceTestBase:ResultType>

<tML-ServiceTestBase:ReturnCode>0000</tML-ServiceTestBase:ReturnCode>

<tML-ServiceTestBase:InfoMessage></tML-ServiceTestBase:InfoMessage >

<tML-ServiceTestBase:ErrorMessage></tML-ServiceTestBase:ErrorMessage >

</Normal>

</PerformanceMonitoringResponse>

### Intermediate Status

<?xml version="1.0" encoding="UTF-8"?>

<PerformanceMonitoringResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest">

<RequestId>L123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>Carrier</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>	33/XHGS/103432//GTEN</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectInstance>

<Normal>

<tML-ServiceTestBase:TroubleReportReferenceNumber></tML-ServiceTestBase:TroubleReportReferenceNumber>

<tML-ServiceTestBase:ReturnCode></tML-ServiceTestBase:ReturnCode>

<tML-ServiceTestBase:ResultType>S</tML-ServiceTestBase:ResultType>

<tML-ServiceTestBase:InfoMessage></tML-ServiceTestBase:InfoMessage>

<tML-ServiceTestBase:Status>

<tML-ServiceTestBase:CircuitDescription></tML-ServiceTestBase:CircuitDescription>

<tML-ServiceTestBase:SummaryText></tML-ServiceTestBase:SummaryText>

<tML-ServiceTestBase:Disposition></tML-ServiceTestBase:Disposition>

<tML-ServiceTestBase:Descriptors>

<tML-ServiceTestBase:DescriptorsNumber>1</tML-ServiceTestBase:DescriptorsNumber>

<tML-ServiceTestBase:Descriptor>

<tML-ServiceTestBase:Index>1</tML-ServiceTestBase:Index>

<tML-ServiceTestBase:TargetIdentifier></tML-ServiceTestBase:TargetIdentifier>

<tML-ServiceTestBase:MacroStatus></tML-ServiceTestBase:MacroStatus>

<tML-ServiceTestBase:MacroDescription></tML-ServiceTestBase:MacroDescription>

</tML-ServiceTestBase:Descriptor>

</tML-ServiceTestBase:Descriptors>

</tML-ServiceTestBase:Status>

<tML-ServiceTestBase:Analysis>

<tML-ServiceTestBase:AnalysisNumber>1<tML-ServiceTestBase:AnalysisNumber>

<tML-ServiceTestBase:AnalysisItem>

<tML-ServiceTestBase:DiagnosisCode></tML-ServiceTestBase:DiagnosisCode>

<tML-ServiceTestBase:ShortSummary></tML-ServiceTestBase:ShortSummary>

<tML-ServiceTestBase:LongSummary></tML-ServiceTestBase:LongSummary>

</tML-ServiceTestBase:AnalysisItem>

</tML-ServiceTestBase:Analysis>

<tML-ServiceTestBase:Details></tML-ServiceTestBase:Details>

</Normal>

</PerformanceMonitoringResponse>

### Final Response

<?xml version="1.0" encoding="UTF-8"?>

<PerformanceMonitoringResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest">

<RequestId>L123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>

Carrier

</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>	33/XHGS/103432//GTEN</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectInstance>

<Normal>

<tML-ServiceTestBase:TroubleReportReferenceNumber></tML-ServiceTestBase:TroubleReportReferenceNumber>

<tML-ServiceTestBase:ReturnCode></tML-ServiceTestBase:ReturnCode>

<tML-ServiceTestBase:ResultType></tML-ServiceTestBase:ResultType>

<tML-ServiceTestBase:InfoMessage></tML-ServiceTestBase:InfoMessage>

<tML-ServiceTestBase:Status>

<tML-ServiceTestBase:CircuitDescription></tML-ServiceTestBase:CircuitDescription>

<tML-ServiceTestBase:SummaryText></tML-ServiceTestBase:SummaryText>

<tML-ServiceTestBase:Disposition></tML-ServiceTestBase:Disposition>

<tML-ServiceTestBase:Descriptors>

<tML-ServiceTestBase:DescriptorsNumber>2</tML-ServiceTestBase:DescriptorsNumber>

<tML-ServiceTestBase:Descriptor>

<tML-ServiceTestBase:Index>1</tML-ServiceTestBase:Index>

<tML-ServiceTestBase:TestIdentifer></tML-ServiceTestBase:TestIdentifer>

<tML-ServiceTestBase:TargetIdentifier></tML-ServiceTestBase:TargetIdentifier>

<tML-ServiceTestBase:MacroStatus></tML-ServiceTestBase:MacroStatus>

<tML-ServiceTestBase:MacroDescription></tML-ServiceTestBase:MacroDescription>

</tML-ServiceTestBase:Descriptor>

<tML-ServiceTestBase:Descriptor>

<tML-ServiceTestBase:Index>2</tML-ServiceTestBase:Index>

<tML-ServiceTestBase:TestIdentifer></tML-ServiceTestBase:TestIdentifer>

<tML-ServiceTestBase:TargetIdentifier></tML-ServiceTestBase:TargetIdentifier>

<tML-ServiceTestBase:MacroStatus></tML-ServiceTestBase:MacroStatus>

<tML-ServiceTestBase:MacroDescription></tML-ServiceTestBase:MacroDescription>

</tML-ServiceTestBase:Descriptor>

</tML-ServiceTestBase:Descriptors>

</tML-ServiceTestBase:Status>

<tML-ServiceTestBase:Analysis>

<tML-ServiceTestBase:AnalysisItem>

<tML-ServiceTestBase:DiagnosisCode></tML-ServiceTestBase:DiagnosisCode>

<tML-ServiceTestBase:ShortSummary></tML-ServiceTestBase:ShortSummary>

<tML-ServiceTestBase:LongSummary></tML-ServiceTestBase:LongSummary>

</tML-ServiceTestBase:AnalysisItem>

</tML-ServiceTestBase:Analysis>

<tML-ServiceTestBase:Details></tML-ServiceTestBase:Details>

</Normal>

</PerformanceMonitoringResponse>

### Final Response (Exception)

<?xml version="1.0" encoding="UTF-8"?>

<PerformanceMonitoringResponse 	xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest">

<RequestId>L123</RequestId>

<TargetObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>

33/XHGS/103432//GTEN

</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectInstance>

<Exception>

<tML-TABase:ProcessingFailure>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>0003</tML-TABase:Tag>

<tML-TABase:Value>Performance Monitoring Transaction did not complete since the associated Trouble Rpoert creation was unsuccessful</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:ProcessingFailure>

</Exception>

</PerformanceMonitoringResponse>

## Set Loopback

This trasaction is offered for Access customer only.

### Set Loopback Request

<?xml version="1.0" encoding="UTF-8"?>

<SetLoopbackRequest

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest.xsd">

<RequestId>L123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>

Carrier

</tML-TABase:ServiceProfile>

</Customer>

<ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>

33/XHGS/103432//GTEN

</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<tML-ServiceTestBase:Acknowledgement>Y</tML-ServiceTestBase:Acknowledgement>

<tML-ServiceTestBase:StatusMessage>Y</tML-ServiceTestBase:StatusMessage>

<tML-ServiceTestBase:FinalDetail>Y</tML-ServiceTestBase:FinalDetail>

<tML-ServiceTestBase:Duration>120</tML-ServiceTestBase:Duration>

<tML-ServiceTestBase:Direction>A</tML-ServiceTestBase:Direction>

<tML-ServiceTestBase:Location>LPLOC NEAREST</tML-ServiceTestBase:Location>

</SetLoopbackRequest>

### Acknowledgement

<?xml version="1.0" encoding="UTF-8"?>

<SetLoopbackResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest">

<RequestId>L123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>

Carrier

</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>

33/XHGS/103432//GTEN

</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<Normal>

<tML-ServiceTestBase:TroubleReportReferenceNumber></tML-ServiceTestBase:TroubleReportReferenceNumber >

<tML-ServiceTestBase:ReturnCode>0000</tML-ServiceTestBase:ReturnCode>

<tML-ServiceTestBase:ResultType>A</tML-ServiceTestBase:ResultType>

<tML-ServiceTestBase:InfoMessage></tML-ServiceTestBase:InfoMessage>

</Normal>

</SetLoopbackResponse>

### Final Response (Success)

<?xml version="1.0" encoding="UTF-8"?>

<SetLoopbackResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest">

<RequestId>L123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>

Carrier

</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>

33/XHGS/103432//GTEN

</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<Normal>

<tML-ServiceTestBase:TroubleReportReferenceNumber></tML-ServiceTestBase:TroubleReportReferenceNumber >

<tML-ServiceTestBase:ReturnCode></tML-ServiceTestBase:ReturnCode>

<tML-ServiceTestBase:ResultType>C</tML-ServiceTestBase:ResultType>

<tML-ServiceTestBase:InfoMessage></tML-ServiceTestBase:InfoMessage>

<tML-ServiceTestBase:Status>

<tML-ServiceTestBase:CircuitDescription></tML-ServiceTestBase:CircuitDescription>

<tML-ServiceTestBase:SummaryText></tML-ServiceTestBase:SummaryText>

<tML-ServiceTestBase:Disposition></tML-ServiceTestBase:Disposition>

<tML-ServiceTestBase:Descriptors>

<tML-ServiceTestBase:DescriptorsNumber>2</tML-ServiceTestBase:DescriptorsNumber>

<tML-ServiceTestBase:Descriptor>

<tML-ServiceTestBase:Index>1</tML-ServiceTestBase:Index>

<tML-ServiceTestBase:TestIdentifer></tML-ServiceTestBase:TestIdentifer>

<tML-ServiceTestBase:TargetIdentifier></tML-ServiceTestBase:TargetIdentifier>

<tML-ServiceTestBase:MacroStatus></tML-ServiceTestBase:MacroStatus>

<tML-ServiceTestBase:MacroDescription></tML-ServiceTestBase:MacroDescription>

</tML-ServiceTestBase:Descriptor>

<tML-ServiceTestBase:Descriptor>

<tML-ServiceTestBase:Index>2</tML-ServiceTestBase:Index>

<tML-ServiceTestBase:TestIdentifer></tML-ServiceTestBase:TestIdentifer>

<tML-ServiceTestBase:TargetIdentifier></tML-ServiceTestBase:TargetIdentifier>

<tML-ServiceTestBase:MacroStatus></tML-ServiceTestBase:MacroStatus>

<tML-ServiceTestBase:MacroDescription></tML-ServiceTestBase:MacroDescription>

</tML-ServiceTestBase:Descriptor>

</tML-ServiceTestBase:Descriptors>

</tML-ServiceTestBase:Status>

<tML-ServiceTestBase:Analysis>

<tML-ServiceTestBase:AnalysisItem>

<tML-ServiceTestBase:DiagnosisCode></tML-ServiceTestBase:DiagnosisCode>

<tML-ServiceTestBase:ShortSummary></tML-ServiceTestBase:ShortSummary>

<tML-ServiceTestBase:LongSummary></tML-ServiceTestBase:LongSummary>

</tML-ServiceTestBase:AnalysisItem>

</tML-ServiceTestBase:Analysis>

<tML-ServiceTestBase:Details></tML-ServiceTestBase:Details>

</Normal>

</SetLoopbackResponse>

### Set Loopback Response (Exception)

<?xml version="1.0" encoding="UTF-8"?>

<SetLoopbackResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest">

<RequestId>L123</RequestId>

<TargetObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>

33/XHGS/103432//GTEN

</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectInstance>

<Exception>

<tML-TABase:ProcessingFailure>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>0003</tML-TABase:Tag>

<tML-TABase:Value>System Down</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:ProcessingFailure>

</Exception>

</SetLoopbackResponse>

## Release Loopback

This trasaction is offered for Access customer only.

### Request

<?xml version="1.0" encoding="UTF-8"?>

<ReleaseLoopbackRequest

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest.xsd">

<RequestId>L123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>

Carrier

</tML-TABase:ServiceProfile>

</Customer>

<ManagedObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>

33/XHGS/103432//GTEN

</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<tML-ServiceTestBase:TroubleReportReferenceNumber></tML-ServiceTestBase:TroubleReportReferenceNumber >

</ReleaseLoopbackRequest>

### Acknowledgement

<?xml version="1.0" encoding="UTF-8"?>

<ReleaseLoopbackResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest">

<RequestId>L123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>Carrier</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>	33/XHGS/103432//GTEN</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<Normal>

<tML-ServiceTestBase:TroubleReportReferenceNumber></tML-ServiceTestBase:TroubleReportReferenceNumber >

<tML-ServiceTestBase:ReturnCode>0000</tML-ServiceTestBase:ReturnCode>

<tML-ServiceTestBase:ResultType>A</tML-ServiceTestBase:ResultType>

<tML-ServiceTestBase:InfoMessage></tML-ServiceTestBase:InfoMessage>

</Normal>

</ReleaseLoopbackResponse>

### Release Loopback Response (Success)

<?xml version="1.0" encoding="UTF-8"?>

<ReleaseLoopbackResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest">

<RequestId>L123</RequestId>

<Customer>

<tML-TABase:UserId>WSAATXX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>

Carrier

</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>	33/XHGS/103432//GTEN</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</ManagedObjectInstance>

<Normal>

<tML-ServiceTestBase:TroubleReportReferenceNumber></tML-ServiceTestBase:TroubleReportReferenceNumber>

<tML-ServiceTestBase:ReturnCode></tML-ServiceTestBase:ReturnCode>

<tML-ServiceTestBase:ResultType></tML-ServiceTestBase:ResultType>

<tML-ServiceTestBase:InfoMessage></tML-ServiceTestBase:InfoMessage>

<tML-ServiceTestBase:Status>

<tML-ServiceTestBase:CircuitDescription></tML-ServiceTestBase:CircuitDescription>

<tML-ServiceTestBase:SummaryText></tML-ServiceTestBase:SummaryText>

<tML-ServiceTestBase:Disposition></tML-ServiceTestBase:Disposition>

<tML-ServiceTestBase:Descriptors>

<tML-ServiceTestBase:DescriptorsNumber>2</tML-ServiceTestBase:DescriptorsNumber>

<tML-ServiceTestBase:Descriptor>

<tML-ServiceTestBase:Index>1</tML-ServiceTestBase:Index>

<tML-ServiceTestBase:TestIdentifer></tML-ServiceTestBase:TestIdentifer>

<tML-ServiceTestBase:TargetIdentifier></tML-ServiceTestBase:TargetIdentifier>

<tML-ServiceTestBase:MacroStatus></tML-ServiceTestBase:MacroStatus>

<tML-ServiceTestBase:MacroDescription></tML-ServiceTestBase:MacroDescription>

</tML-ServiceTestBase:Descriptor>

<tML-ServiceTestBase:Descriptor>

<tML-ServiceTestBase:Index>2</tML-ServiceTestBase:Index>

<tML-ServiceTestBase:TestIdentifer></tML-ServiceTestBase:TestIdentifer>

<tML-ServiceTestBase:TargetIdentifier></tML-ServiceTestBase:TargetIdentifier>

<tML-ServiceTestBase:MacroStatus></tML-ServiceTestBase:MacroStatus>

<tML-ServiceTestBase:MacroDescription></tML-ServiceTestBase:MacroDescription>

</tML-ServiceTestBase:Descriptor>

</tML-ServiceTestBase:Descriptors>

</tML-ServiceTestBase:Status>

<tML-ServiceTestBase:Analysis>

<tML-ServiceTestBase:AnalysisNumber>1<tML-ServiceTestBase:AnalysisNumber>

<tML-ServiceTestBase:AnalysisItem>

<tML-ServiceTestBase:DiagnosisCode></tML-ServiceTestBase:DiagnosisCode>

<tML-ServiceTestBase:ShortSummary></tML-ServiceTestBase:ShortSummary>

<tML-ServiceTestBase:LongSummary></tML-ServiceTestBase:LongSummary>

</tML-ServiceTestBase:AnalysisItem>

</tML-ServiceTestBase:Analysis>

<tML-ServiceTestBase:Details></tML-ServiceTestBase:Details>

</Normal>

</ReleaseLoopbackResponse>

### Release Loopback Response (Exception)

<?xml version="1.0" encoding="UTF-8"?>

<ReleaseLoopbackResponse

xmlns="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTest="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest"

xmlns:tML-ServiceTestBase="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTestBase"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/ServiceTest/POTS/tML-ServiceTest">

<RequestId>L123</RequestId>

<TargetObjectInstance>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>serviceID</tML-TABase:Type>

<tML-TABase:Assertion>

33/XHGS/103432//GTEN

</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectInstance>

<Exception>

<tML-ServiceTestBase:TroubleReportReferenceNumber></tML-ServiceTestBase:TroubleReportReferenceNumber>

<tML-TABase:ProcessingFailure>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>0003</tML-TABase:Tag>

<tML-TABase:Value>Rlease Loopback failed because ticket creation failed due to system error</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:ProcessingFailure>

</Exception>

</ReleaseLoopbackResponse>

## Retrieve Local Contact by TroubleReportId

This trasaction is offered for Access customer only.

### RetrieveLocalContactByTroubleReportIdRequest

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveLocalContactByTroubleReportIdRequest

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA tML-TA.xsd">

<RequestId>TRCreate123</RequestId>

<Customer>

<tML-TABase:UserId>WSAABCX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>Carrier</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>VZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ABC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>TT340304</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

</RetrieveLocalContactByTroubleReportIdRequest>

### RetrieveLocalContactByTroubleReportIdResponse  (Normal)

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveLocalContactByTroubleReportIdResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA  tML-TA.xsd">

<RequestId>abc123</RequestId>

<Customer>

<tML-TABase:UserId>WSAABCX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>Carrier</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>NEVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ABC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>TT304930</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<Normal>

<tML-TABase:ALocationAccessAddress>

<tML-TABase:PremisesName>My ocean Beach Home</tML-TABase:PremisesName>

<tML-TABase:PremisesPhone>2129393939</tML-TABase:PremisesPhone>

<tML-TABase:PremisesAddress>

<tML-TABase:CivicAddress>1320 N Court House Rd, Arlington, VA 22203</tML-TABase:CivicAddress>

</tML-TABase:PremisesAddress>

</tML-TABase:ALocationAccessAddress>

<tML-TABase:ALocationAccessHours>

<tML-TABase:LocationAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:LocationAccessHoursItem>

</tML-TABase:ALocationAccessHours>

<tML-TABase:ALocationAccessPerson>

<tML-TABase:Name>My Name</tML-TABase:Name>

<tML-TABase:Phone>7039746778</tML-TABase:Phone>

<tML-TABase:Email>id@AT company.com</tML-TABase:Email>

<tML-TABase:Fax>7039746778</tML-TABase:Fax>

<tML-TABase:Pager>8003334444</tML-TABase:Pager>

</tML-TABase:ALocationAccessPerson>

<tML-TABase:CircuitId>33/HCGS/392943/SD</tML-TABase:CircuitId>

<tML-TABase:EscalationList>

<tML-TABase:EscalationItem>

<tML-TABase:Level>2</tML-TABase:Level>

<tML-TABase:Remark>This ticket was escalated</tML-TABase:Remark>

</tML-TABase:EscalationItem>

</tML-TABase:EscalationList>

<tML-TABase:ManagedObjectAccessHours>

<tML-TABase:ManagedObjectAccessHoursItem>

<tML-TABase:DaysOfWeek>

<tML-TABase:Sunday>false</tML-TABase:Sunday>

<tML-TABase:Monday>true</tML-TABase:Monday>

<tML-TABase:Tuesday>false</tML-TABase:Tuesday>

<tML-TABase:Wednesday>false</tML-TABase:Wednesday>

<tML-TABase:Thursday>false</tML-TABase:Thursday>

<tML-TABase:Friday>false</tML-TABase:Friday>

<tML-TABase:Saturday>false</tML-TABase:Saturday>

</tML-TABase:DaysOfWeek>

<tML-TABase:IntervalsOfDay>

<tML-TABase:IntervalsOfDayItem>

<tML-TABase:IntervalStart>10:30:00</tML-TABase:IntervalStart>

<tML-TABase:IntervalEnd>15:00:00</tML-TABase:IntervalEnd>

</tML-TABase:IntervalsOfDayItem>

</tML-TABase:IntervalsOfDay>

</tML-TABase:ManagedObjectAccessHoursItem>

</tML-TABase:ManagedObjectAccessHours>

</Normal>

</RetrieveLocalContactByTroubleReportIdResponse>

### RetrieveLocalContactByTroubleReportIdRequest  (Exception)

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveLocalContactByTroubleReportIdResponse

xmlns="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TA="http://www.ansi.org/tML/TA/tML-TA"

xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase"

xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA tML-TA.xsd">

<RequestId>abc123</RequestId>

<Customer>

<tML-TABase:UserId>WSAABCX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>Carrier</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>SP Network ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>SC account Name Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportID</tML-TABase:Type>

<tML-TABase:Assertion>Trouble Report ID Value</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<Exception>

<tML-TABase:ProcessingFailure>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>0003</tML-TABase:Tag>

<tML-TABase:Value>System Not Responding: Time Out Error</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:ProcessingFailure>

</Exception>

</RetrieveLocalContactByTroubleReportIdResponse>

## Sample tML for Retrieve Technician Notes

This transaction is implemented for TAXI Access customer.

#### RetrieveTechnicianNotesByTroubleReportIdRequest

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveTechnicianNotesByTroubleReportIdRequest xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA tML-TA.xsd" xmlns="http://www.ansi.org/tML/TA/tML-TA" xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance">

<RequestId>L123</RequestId>

<Customer>

<tML-TABase:UserId>WSAABCX01</tML-TABase:UserId>

<tML-TABase:ServiceProfile>Carrier</tML-TABase:ServiceProfile>

</Customer>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>VZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportId</tML-TABase:Type>

<tML-TABase:Assertion>VNYED29349</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

</RetrieveTechnicianNotesByTroubleReportIdRequest>

#### RetrieveTechnicianNotesByTroubleReportIDResponse  (Normal)

<?xml version="1.0" encoding="UTF-8"?>

<RetrieveTechnicianNotesByTroubleReportIdResponse xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA tML-TA.xsd" xmlns="http://www.ansi.org/tML/TA/tML-TA" xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance">

<RequestId>L123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportId</tML-TABase:Type>

<tML-TABase:Assertion>VNYED29349</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<Normal>

<tML-TABase:ActivityLog>

<tML-TABase:ActivityLogItem>

<tML-TABase:ActivityLogDate>2009-12-17T09:30:47.0Z</tML-TABase:ActivityLogDate>

<tML-TABase:ActivityDescription>String representing technician notes</tML-TABase:ActivityDescription>

</tML-TABase:ActivityLogItem>

<tML-TABase:ActivityLogItem>

<tML-TABase:ActivityLogDate>2009-12-17T09:35:47.0Z</tML-TABase:ActivityLogDate>

<tML-TABase:ActivityDescription>ESC TO LVL 2</tML-TABase:ActivityDescription>

</tML-TABase:ActivityLogItem>

<tML-TABase:ActivityLogItem>

<tML-TABase:ActivityLogDate>2001-12-17T19:30:47.0Z</tML-TABase:ActivityLogDate>

<tML-TABase:ActivityDescription>WORKED BY CTR TECH</tML-TABase:ActivityDescription>

</tML-TABase:ActivityLogItem>

</tML-TABase:ActivityLog>

</Normal>

</RetrieveTechnicianNotesByTroubleReportIdResponse>

#### RetrieveTechnicianNotesByTroubleReportIDResponse  (Exception)

<?xml version="1.0" encoding="UTF-8"?>

<!--Sample XML file generated by XMLSpy v2007 rel. 3 (http://www.altova.com)-->

<tML-TA:RetrieveTechnicianNotesByTroubleReportIdResponse xsi:schemaLocation="http://www.ansi.org/tML/TA/tML-TA tML-TA.xsd" xmlns="http://www.ansi.org/tML/TA/tML-TA" xmlns:tML-TABase="http://www.ansi.org/tML/TA/tML-TABase" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance">

<RequestId>L123</RequestId>

<TargetObjectName>

<tML-TABase:DistinguishedName>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>networkID</tML-TABase:Type>

<tML-TABase:Assertion>TXVZC</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>accountName</tML-TABase:Type>

<tML-TABase:Assertion>ACME</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

<tML-TABase:RDNSequenceItem>

<tML-TABase:Type>troubleReportId</tML-TABase:Type>

<tML-TABase:Assertion>VNYED29349</tML-TABase:Assertion>

</tML-TABase:RDNSequenceItem>

</tML-TABase:DistinguishedName>

</TargetObjectName>

<Exception>

<tML-TABase:ProcessingFailure>

<tML-TABase:ExceptionList>

<tML-TABase:Tag>1001</tML-TABase:Tag>

<tML-TABase:Value>Processing Failure</tML-TABase:Value>

</tML-TABase:ExceptionList>

</tML-TABase:ProcessingFailure>

</Exception>

</RetrieveTechnicianNotesByTroubleReportIdResponse>

# Environment Parameters

## SOAP

SOAP versions 1.1

## WSDL

WSDL 1.1

## Digital Certificate

### Inbound Digital Certificate for Verizon Customers (Telecommunications Companies)

Verizon requires all clients to use X.509 digital certificate to authenticate to Verizon web service.  The clients will get the “Client Digital Certificate” as well as the public key of Verizon CA from Verizon.  The Clients will “trust” Verizon CA as a “Trusted CA” in their application and use the “Client Certificate” issued by Verizon to connect to our web service.

### Outbound Digital Certificate

- Verizon will acquire Verizon client digital certificate .  Trading partners who subscribe to notification service are responsible to acquire and install Verisign server digital certificates on their system.

- Verizon will give credential of client digital certificate to trading partners.

- Trading partners will add Verizon’s credential in their authentication system.

### Verify Distinguish Name in Callback Message by Customers

A customer’s Web Service running as a callback server must verify the value of the Distinguished Name (DN) in the certificate presented by the callback session initiated from Verizon. The DN value must be equal to the following literal string (case sensitive) before they process the incoming callback:

cn=WEBSERVICES VERIZON,ou=people,ou=gsi,o=verizon,c=us

## Verizon TAXI URLs

### Local Customers

#### Document Style WSDL

#### 7.4.1.1.1	End Point URL

| TAPP | https://swholesalegw2.verizon.com/TA-Local-tapp/taservice/docstyleserviceuri |
| --- | --- |
| Production | https://wholesalewsg.verizon.com/TA-Local/taservice/docstyleserviceuri |

#### 7.4.1.1.2	WSDL URL

| TAPP | https://swholesalegw2.verizon.com/TA-Local-tapp/taservice/docStyleService/wsdl.jsp |
| --- | --- |
| Production | https://wholesalewsg.verizon.com/TA-Local/taservice/docStyleService/wsdl.jsp |

#### RPC  Style WSDL

#### 7.4.1.2.1	End Point URL

| TAPP | https://swholesalegw2.verizon.com/TA-Local-tapp/taservice/rpcstyleserviceuri |
| --- | --- |
| Production | https://wholesalewsg.verizon.com/TA-Local/taservice/rpcstyleserviceuri |

#### 7.4.1.2.2	WSDL URL

| TAPP | https://swholesalegw2.verizon.com/TA-Local-tapp/taservice/rpcStyleService/wsdl.jsp |
| --- | --- |
| Production | https://wholesalewsg.verizon.com/TA-Local/taservice/rpcStyleService/wsdl.jsp |

### Access Carrier and/or Retail Customers

#### Document Style WSDL

#### 7.4.2.1.1	End Point URL

| TAPP | https://swholesalegw2.verizon.com/TA-Access-tapp/taservice/docstyleserviceuri |
| --- | --- |
| Production | https://wholesalewsg.verizon.com/TA-Access/taservice/docstyleserviceuri |

#### 7.4.2.1.2	WSDL URL

| TAPP | https://swholesalegw2.verizon.com/TA-Access-tapp/taservice/docStyleService/wsdl.jsp |
| --- | --- |
| Production | https://wholesalewsg.verizon.com/TA-Access/taservice/docStyleService/wsdl.jsp |

#### RPC Style WSDL

#### 7.4.2.2.1	End Point URL

| TAPP | https://swholesalegw2.verizon.com/TA-Access-tapp/taservice/rpcstyleserviceuri |
| --- | --- |
| Production | https://wholesalewsg.verizon.com/TA-Access/taservice/rpcstyleserviceuri |

#### 7.4.2.2.2	WSDL URL

| TAPP | https://swholesalegw2.verizon.com/TA-Access-tapp/taservice/rpcStyleService/wsdl.jsp |
| --- | --- |
| Production | https://wholesalewsg.verizon.com/TA-Access/taservice/rpcStyleService/wsdl.jsp |

# References

- ANSI T1.262 (R2002), Operations, Administration, Maintenance, and Provisioning (OAM&P) – Extension to Generic Network Model for Interfaces across Jurisdictional Boundaries to Support the Service Test Function

- ANSI T1.227-2000, Operations, Administration, Maintenance, and Provisioning (OAM&P) – Extension to Generic Network Information Model for Interfaces between Operation Systems across Jurisdictional Boundaries to Support Fault Management (Trouble Administration)

- ANSI T1.228-1995, Operations, Administration, Maintenance, and Provisioning (OAM&P) – Services for Interfaces between Operation Systems across Jurisdictional Boundaries to Support Fault Management (Trouble Administration)

- ANSI T1.278, XML Schema Interface for Fault Management (Trouble Administration)

- ANSI T1.277, XML Schema Interface for POTS Service Test

# Annex A	TR <XX> <YY> Construction Rules

The purpose for TR <XX> <YY> at the very beginning of the first instance of AdditionalTroubleInfoItem is to facilitate the trouble report handling and processing if a previous service test has been performed on a given circuit id. Based on the Trouble Type selected by a customer when creating a trouble report, the test results and any recommendations, the customer would enter specific information in the first nine characters (in the format of TR <XX> <YY>) of the first instance of AdditionalTroubleInfoItem.

## A.1	<XX> vs. Test Result Code

The <XX> is a two character alpha-numeric string and is obtained from the Test Result Code (commonly referred as VER code) as part of AdditionalText field found in POTS service test response specified in §5.1 or obtained from a test result code (VER code) though other service test channel for a given circuit.

## A.2	<YY> vs. Dispatch Decision Chart

The <YY> is a two character numerical string and is the customer’s desired dispatch choice taken from the Dispatch Decision Chart listed below:

Table 35.  <YY> Value Mapping to Verizon Dispatch Decision Chart

| Dispatch Category | <YY> | Dispatch Code Used by Verizon | Description of Work |
| --- | --- | --- | --- |
| Outside Technician Dispatch Request | 01 | CLECAS | Dispatch Out for an Affected Service condition. |
|  | 02 | CLECOS | Dispatch Out for an Out of Service condition. |
|  | 03 | CLECPHYA | Dispatch Out for a known physical condition where the fault is in the drop wire, protector or network interface at the end user location and it is an Affected Service condition. |
|  | 04 | CLECPHYO | Dispatch Out for a known physical condition where the fault is in the drop wire, protector or network interface at the end user location and it is an Out of Service condition. |
| Central Office (inside) Dispatch Request | 05 | FRAMEAS | Frame faults where it is expected that a frame jumper needs to be checked or verified on an Affected Service condition. |
|  | 06 | FRAMEOS | Frame faults where it is expected that a frame jumper needs to be checked or verified on an Out of Service condition. |
|  | 07 | PDIAS2 | Single Line Switch Translation trouble where it is an Affected Service condition. Normally a vertical feature related condition (call waiting, call forwarding etc.) |
|  | 08 | PDIOS2 | Single Line Switch Translation trouble where it is an Out of Service condition. Normally a vertical feature related condition (call waiting, call forwarding etc.) |
|  | 09 | PDIAS3 | Central Office/Switch Dispatch (IN) for other than a single line translation condition where it is an Affected Service condition. For more complex services such as Centrex, DIDs, hunt groups etc. |
|  | 10 | PDIOS3 | Central Office/Switch Dispatch (IN) for other than a single line translation condition where it is an Out of Service condition. For more complex services such as Centrex, DIDs, hunt groups etc. |
|  | 11 | VMS | Voice Messaging Platform for troubles other than password related conditions. |
| Other Work Group Activity | 12 | ORDERAS | Recent Service Order related activity for an Affected Service condition. |
|  | 13 | ORDEROS | Recent Service Order related activity for an Out of Service condition. |
|  | 14 | EBHOLD | RCMC (Manual) assistance required to isolate the fault. |

# Annex B	Circuit Format Definition for Designed and Non-Designed Circuits

This section provides different circuits supported by Verizon for its customers. In general, circuits can be divided into different format and can be categorized as designed circuits or non-designed circuits. In general, designed circuits are used for special purpose such as dedicated lines, connections between different switches, etc. Designed circuits are commonly used for carrying digital signals. On the other hand, non-designed circuits are commonly used for carrying POTS signals among other signals.

The circuit id is used to populate the Assertion tag value of Type/Assertion pair in the last RDNSequenceItem under ManagedObjectInstance with Type tag value as serviceID for a Trouble Report Create request.

| Circuit Type | Note | Field Definition |
| --- | --- | --- |
| Serial | Serial can be either designed or non-designed circuit. Serial designed circuits include DS1 circuits as well as other high bandwidth digital circuits. Serial non-designed circuits includes, for examples, line sharing, commonly marked with URXX as service modifier; line splitting , commonly marked with SWXX as service modifier, circuits for caring both POTS and DSL signals on a same circuit, unbundled loop , so-called UNE loop with TXNU as service modifier. |  |
| Telephone | can be either designed or non-designed circuit. |  |
| Carrier Facility | exclusively designed circuits |  |
| Message Trunk | exclusively designed circuits |  |
| POT (Plain Old Telephone) | exclusively non-designed circuits | 2123012555 |

# Annex C	Trouble Code Definition for POTS Service Test with FTTP Infrastructure

## C.1	Trouble Code

For a POTS Service Test request issued by a service customer, Verizon test systems will try to detect faults for the POTS service id provided in the test request. For a given test request, there may be multiple Trouble Codes provided by Verizon test systems. A Trouble Code describes a fault in detailed information. If there is no fault found for a given test request, then no Trouble Code will be returned to the customer.

A Trouble Code is an eight character alpha-numeric code with three sub components. The definition for Trouble Code is:

TroubleCode:=<A1><A2><A3>, where

<A1>:= A two character Fault Category value,

<A2>:= A three character Fault Entity value,

<A3>:= A three character Fault Code value.

## C.2	Fault Category

A Fault category describes the type of error that has occurred within a tested network element.

Table 36.  Fault Category for Trouble Code

| Fault Category | Description |
| --- | --- |
| AL | Alarm Code |
| CF | Configuration Error |
| PM | Performance Monitoring Error |
| TS | Test Error |

## C.2	Fault Entity

A fault entity describes an equipment in which an error may have occurred.

Table 37.  Fault Entity for Trouble Code

| Fault Entity | Description |
| --- | --- |
| ATM | ATM Switch |
| OLT | Optical Line Terminal |
| ONT | Optical Network Terminal |
| GWR | Gateway Router |
| BGR | Beyond Gateway Router |
| C5S | Class 5 Switch |
| CUP | Customer’s Premise |
| G2A | Gateway Router to ATM Segment |
| A2O | ATM to OLT Segment |
| O2S | OLT to Class 5 Switch |
| L2N | OLT to ONT Segment |
| XXX | Default or Unknown Entity |

## C.3	Fault Code

A fault code describes a specific result/error in a tested network element.

There are four types of fault codes:

- GR909 Tests

- PON Alarm

- Gateway Router

- Wavesmith ATM Switch Alarms

### C.3.1	GR909 Tests Fault Codes

Table 38.  GR909 Tests Fault Codes

| Fault Code | Description |
| --- | --- |
| TOK | Test OK |
| DCF | DC FEMF Marginal |
| GRD | Ground Fault |
| OOB | Open Out Balanced |
| HAZ | Hazardous Potential |
| ACF | AC FEMF Marginal |
| SRT | Short Fault |
| ROH | Receiver Off Hook |

### C.3.2	PON Alarm Fault Codes

Table 39.  PON Alarm Fault Codes

| Fault Code | PON Alarm | Description |
| --- | --- | --- |
| AIS | AIS | Alarm Indication Signal |
| CSX | CS | Cell Starvation |
| DAC | DACTVD | Deactivated |
| EFG | EXT-FE-GRP | Far End Group Alarm |
| EFP | EXT-FE-PWR | Power or Misc failure on Far End |
| IGA | INT-GRP | Internal Group Alarm |
| INT | INT | Internal Failure |
| IPF | INT-PWR | Internal Power Failure |
| ISC | INCCCSMDII | Illegal signaling condition detected |
| LBE | LOPL-BED | Loss of Physical Layer Block Error Detected |
| LBV | LWBATVG | Low Battery Voltage |
| LCD | LOPL-LCD | Loss of Physical Layer Cell delineation |
| LCP | LOPL-CPE | Loss of Physical Layer Cell Phase Error |
| LLS | LOPL-LOS | Loss of Physical Layer Loss of Signal |
| LOA | LOPL-LOA | Loss of Physical Layer Loss of Acknowledgement |
| LOF | LOF | Loss of Frame |
| LOS | LOS | Loss of Signal |
| LSF | LOS-SFB | Loss of Signal Suspected Fiber Break |
| MAN | MAN | Maintenance Disabled |
| MEA | MEA | Mismatched Equipment Attributes |
| MIC | REPLUNIT MISS | In-service card is missing from assigned lot |
| PEE | LOPL-PEE | Loss of Physical Layer Physical Equipment Error |
| PLS | PWR-LOS | Power Loss |
| PSF | PS-FAIL | Power Supply Failure |
| PSM | PS-MISS | Power Supply Missing |
| REI | REI | Remote Error Indication |
| RIN | LOPL-RINH | Loss of Physical Layer Receive Alarm Inhibit |
| SUF | SUF | Start Up Failure |
| TBL | T-BERL | Threshold Bit Error Ratio Line |
| TBP | T-BERP | Threshold Bit Error Ratio Path |
| YEL | YEL | Multi frame Yellow Error |

### C.3.3	Gateway Router Fault Codes

Table 40.  Gateway Router Fault Codes

| Fault Code | Description |
| --- | --- |
| UPX | Normal |
| DWN | Down |
| TST | Testing |

### C.3.4	Wavesmith ATM Switch Alarms Fault Codes

Table 41.  Wavesmith ATM Switch Alarms Fault Codes

| Fault Code | Wavesmith Alarm | Description |
| --- | --- | --- |
| ACL | ALARM-CLR | Alarm Clear |
| ADN | ADMIN- DOWN | Admin Down |
| AIL | AIS-LINE | Alarm Indication Signal (path) |
| AIS | AIS | Alarm Indication Signal |
| ALF | ADMIN- LPBK-OFF | Admin Loopback Off |
| ALN | ADMIN- LPBK-ON | Admin Loopback On |
| ASB | APS-SBF | APS Switch Byte Protection Failure |
| ASC | APS-STATE- CHG | APS State Change |
| ASD | APS-SD | APS SD threshold exceeded |
| ASF | APS-SF | APS SF threshold exceeded |
| AUP | ADMIN-UP | Admin Up |
| BRT | BERT-TEST | BERT testing is currently in progress |
| CBM | CBIT-M23 | Alarm: CBIT-M23 mismatch |
| CFA | CFG-ABRT | Alarm: Config-Aborted |
| CON | CONNECTED | Connected |
| CRN | CKTM- REPORTS- NOBW |  |
| DRE | DRV-ERR | Drive Error |
| FCA | FE-CFG-ABRT | Alarm: FE Config-Aborted |
| FCS | FE-CFG-ABRT | Alarm: FE Start-up |
| FEB | FE-BLK | Alarm: FE Blocked |
| FIL | FE-INSUFF- LNK | FE Insufficient Links |
| FLN | FE-LNK-NOT- GRP | Alarm: FE Link Not In Group |
| FOF | FEAC-LPBK- OFF |  |
| FON | FEAC-LPBK- ON |  |
| FRU | FE-RX-UNUS ABLE | Alarm: FE RX Unusable |
| FTU | FE-TX-UNUS ABLE | Alarm: FE TX Unusable |
| GTM | GRP-TIMING- MISMATCH | Alarm: Group timing mismatch |
| IAL | INTERFACE- ALARM | Interface Alarm |
| IDB | INTERFACE- DISABLED | Interface Disabled |
| IDN | INTERFACE- DOWN | Interface Down |
| IEB | INTERFACE- ENABLED | Interface Enabled |
| ILB | INTERFACE- LPBK | Interface Loopback |
| ILK | INSUFF- LINKS | Insufficient number of links |
| IMS | ID-MIS MATCH | Path trace ID mismatch |
| INP | IN-PROGRESS |  |
| IPR | INTERFACE- PROVI SIONED | Interface Provisioned |
| ISG | IDLE-SIGNAL | Idle Signal |
| IUP | INTERFACE- UP | Interface Up |
| LBD | LPBK- DETECT | Loopback detected |
| LCD | LCD | Loss of cell delineation |
| LDN | LPORT-DOWN | LPORT Down |
| LDS | LNK-DLY- SYNC | Alarm: Link out of delay synchronization |
| LFP | LOF-PATH | Loss of Frame (path) |
| LIF | LOS-IMA | Loss of IMA Frame |
| LNG | LNK-NOT- GRP | Alarm: Link not in group |
| LOF | LOF | Loss of Frame |
| LOP | LOP-PATH | Loss of pointer |
| LOS | LOS | Loss of Signal |
| MLP | MFR-LNK- PARSE-ERR | Could not parse MFR link integrity protocol message |
| OTH | OTHER |  |
| PID | PARENT- INTERFACE- DOWN | Parent Interface Down |
| PLM | PTH-PAYLD- LBL-MIS MATCH | Alarm: Path Payload Label Mismatch (C2 bytes) |
| PSA | PA-SLOT- AVAIL | PA Slot Available |
| PSU | PA-SLOT- UNAVAIL | PA Slot Unavailable |
| PUQ | PATH- UNEQUIP | Path Unequipped |
| REI | REI-PATH | Remote Error Indication |
| RFI | RFI | Remote Failure Indication |
| RFM | RFI-IMA | Alarm: Remote Failure Indication (IMA) |
| RXM | RX-MISCON NECT | Alarm: RX misconnected |
| TMI | TIMEOUT- MFR-IPX | Timeout waiting for MFR link integrity protocol exchange |
| TXM | TX-MISCON NECT | Alarm: TX misconnected |
| WFI | WAIT-MFR- IPX | Waiting for MFR link integrity protocol exchange. |

# Annex D	Acronym List

| Name | Description |
| --- | --- |
| ACNA | Access Customer Name Abbreviation |
| ANSI | American National Standards Institute |
| AVC | Attribute Value Change |
| B2B | Business To Business |
| CLEC | Competitive Local Exchange Carrier |
| ECC | Exchange Carrier Code |
| FEP | Facility Equipment Provisioned |
| FTTP | Fiber To The Premise |
| GMT | Greenwich MeanTime |
| HTTP | Hypertext Transfer Protocol |
| HTTPS | Hypertext Transfer Protocol - Secure |
| IEC | Interexchange Carriers |
| NPA | Numbering Plan Area (Area Code) |
| NXX | Telephone Exchange Number |
| OAM&P | Operations, Administration, Maintenance and Provisioning |
| POTS | Plain Old Telephone Service |
| RPC | Remote Procedure Call |
| SOAP | Simple Object Access Protocol |
| TA | Trouble Administration |
| TAPP | Trouble Administration Pre-Production |
| TAXI | Trouble Administration XML Interface |
| TSP | Telephone Service Priority |
| URL | Uniform Resource Locator |
| WSDL | Web Services Description Language |
| XML | Extensible Markup Language |
| tML | telecommunications Markup Language |
| TLS | Transparent LAN Service |

# Annex E	Trouble Ticket Late Bonding

- Definition

Trouble Ticket Late Bonding process allowes customers to electronically bond a trouble ticket originally entered manually or via Verizon electronic trouble reporting sytems other than Verizon TAXI System.

A ticket created under Verizon's TAXI system is considered an Electronically Bonded Ticket, on which the customer to submit further electronic transactions and receive proactive notifications.

According to the Verizon’s business rules, a physical circuit can only have one ticket opened against it at any time.  A ticket can be opened by the customer via TAXI, EBTA, VTAG, LSI-TA, or a manual call into the center.  Additionally, a ticket can be opened by a Verizon technician if the trouble was detected before a customer ticket being openned.

If a customer was made aware of a ticket opened outside TAXI, and would like to make the ticket an “Electronically Bonded ticket”, the customer can choose to initiate Trouble Ticket Late Bonding by sending a RetrieveAttributesByTroubleReportIdRequest transaction, with the TroubleReportId and at least one attribute ID (e.g. AdditionalTroubleInfoList) in the retrieve attributes list.  If the transaction is successful, the ticket is considered bonded.

Once a ticket is bonded, a customer can submit additional transactions on that ticket and receive proactive notifications.

- Process Description

Scenario 1) Late Bond after receiving error “Trouble Report Already Exist” during a TAXI Create Request

Figure 2 Late Bond after receiving error "Trouble Report Already Exist" during a TAXI Create Request

During the trouble report creation processing in TAXI, if a trouble report already exists on the requested circuit, the customer will receive a “Trouble Report Already Exists” error from TAXI.  The error will contain the existing trouble report number.

This error code informs the customer there is an existing ticket on the requested circuit, and provides the ticket number.  However, it does not indicate whether the ticket was entered via TAXI or another system, nor does the ticket become an electronically bonded ticket.

If the customer encounters “Trouble Report Already Exists” error, the following two options are available:

- Do nothing:  If the existing ticket was previously entered via the TAXI system, the customer will continue to receive proactive statusing and events.  However, if the existing ticket was not previously entered via the TAXI system, the customer will not receive any status on this ticket.

- If a external customer would like to enjoy the electronic bonding feature provided by TAXI, the customer will need to send a RetrieveAttributesByTroubleReportIdRequest transaction, with the trouble report number provided on the TTR Already Exist error response, and at least one attribute ID (e.g. AdditionalTroubleInfoList) in the retrieve attributes list.

Scenario 2) Direct Late Bond

Figure 3 Direct Late Bond

If the customer was made aware of a trouble report number, either via phone or other means, the customer can late bond directly to that ticket without going through the create process.

Customer can issue RetrieveAttributesByTroubleReportIdRequest with the trouble report number that is known.   TAXI will attempt to late bond to the ticket.   If the late bond is successful, TAXI will send back the bonded trouble report number in the response.

It is important to note that the bonded trouble report number might be different than the original trouble report number sent on the RetrieveAttributesByTroubleReportIdRequest.  For example, if a customer sends in trouble ticket number "CC123456", the bonded trouble report number might be "WNYCC123456".This is implemented to address the formatting differences of trouble report ID among TAXI and other systems.

All subsequent transactions must be performed using the bonded trouble report number instead of the original trouble report number.  All subsequent status updates will use the bonded trouble report number.  It is imperative for the customer to store and use the bonded trouble report number after the late bond process.

Note:  In Scenario 1, the TAXI “Trouble Report Already Exists” exception will always return the bonded trouble report number.  Therefore, the subsequent trouble report number returned by the RetrieveAttributesByTroubleReportIdResponse will always remain the same.  In Scenario 2, the trouble report number submitted might differ from the bonded trouble report number returned by the

RetrieveAttributesByTroubleReportIdResponse.

Limitations

There are attributes that a late bond RetrieveAttributesByTroubleReportIdResponse will not return, as listed in the table below.  A late bond RetrieveAttributesByTroubleReportIdRequest will trigger a RetrieveAttributesByTroubleReportIdResponse with partial success result.  See sample XMLs at §6.8.2.3 Retrieve Trouble Report Attributes Response – Partial Success.

| Applicable Attributes, that could be returned if requested. TroubleReportID AdditionalTroubleInfoList CloseOutNarrative CommitmentTime CustomerTroubleTicketNum LastUpdateTime ManagedObjectInstanceAliasList ServiceID ManagerContactPerson ReceivedTime TroubleState TroubleStatus TroubleStatusTime TroubleType | Non Applicable Attributes, that will not be returned even if requested. ActivityDuration AdditionalTroubleStatusInfoList AgentContactPerson ALocationAccessHours ALocationAccessAddress ALocationAccessPerson ZLocationAccessHours ZLocationAccessAddress ZLocationAccessPerson AuthorizationList CalledNumber CancelRequestedByManager CloseoutVerification CommitmentTimeRequest CustomerWorkCenter EscalationList InitiatingMode MainServiceCharge ManagedObjectAccessHours OutageDuration PerceivedTroubleSeverity PreferredPriority RepeatReport RestoredTime TroubleClearancePerson TroubleDetectionTime TroubleLocation TroubleReportStatusWindow TspPriority |
| --- | --- |

"Trouble report has been bonded to TAXI Local"         (from Local URL) or

"Trouble report has been bonded to TAXI Access"      (from Access URL)

# Annex F  Escalation

Figure 4 Escalation Process Diagram

# Annex G  Authorization

Figure 5 Authorization Processing Diagram

# Annex H  Close Out Verification

Also known as  “EB Verify,” “EBV.”

Figure 6 Close Out Verification (EBV) Processing

# Footnotes

For value of <Verizon_Service_URL>, refer to §7.4.

<Service_Customer_Callback_URL>::= https://<to be determined> for production, and https://<to be determined> for CTE test. This is a callback service URL located on a service customer side for receiving an asynchronous response from Verizon.

<Service_Customer_Notification_URL>::= https://<to be determined> for production, and https://<to be determined> for CTE test. This is a notification service URL located on a service customer side for receiving an unsolicited event notification message from Verizon.

For value of <Verizon_Service_URL>, refer to §7.4.

<Service_Customer_Callback_URL>::= https://<to be determined> for production, and https://<to be determined> for CTE test. This is a callback service URL located on a service customer side for receiving an asynchronous response from Verizon.

<Service_Customer_Notification_URL>::= https://<to be determined> for production, and https://<to be determined> for CTE test. This is a notification service URL located on a service customer side for receiving an unsolicited event notification message from Verizon.

A field is labeld “Conditional/Required” (Cond/Req) when a field is only required on the condition that its parent field is present.  For example, PremiseName is required only when the parent field ALocationAccessAddress is present.  If ALocationAccessAddress was not present, the child field PremiseName would not be present at all, therefore not required.

Status Code 36 was approved 3/2001 by the Standard's organization, but has not been formally added to T1.227 yet.

Verizon will insure that Status Code 36 is included in the next T1.227 update.

Definition for Status Code 36 - Repaired Pending Validation - refers to the state where the Central Office Technician has Cleared a problem in the network and sent the ticket back to the Test Center where it is pending on the work list until a Tester is available.

# Text boxes

Verizon

TA Customer

Late bond

RequestTroubleReportCreationRequest

RetrieveAttributesByTroubleReportIdRequest

ID=WNYCC123456 or VNYBV00XXX1

RequestTroubleReportCreationResponse

Trouble Already Exist

ID=WNYCC123456 or VNYBV00XXX1

RetrieveAttributesByTroubleReportIdResponse

ID=WNYCC123456 or VNYBV00XXX1

RetrieveAttributesByTroubleReportIdResponse

ID=WNYCC123456 or VNYBV00XXX1

Trouble report number might be different from the request

Verizon

RetrieveAttributesByTroubleReportIdRequest

ID=CC123456 or NYBV00XXX1

TA Customer

Late bond

TA Customer

Verizon

Escalation Approved

Modify  Ticket=NYXXX00001,  EscalationList

State = 1 (request)

Level = 1

Modify Response only signifies acknowledgement

AttrivuteValueChange   Ticket = NYXXX0001

Escalation List

State = 2 (provided)

Level = 1

AttrivuteValueChange   Ticket = NYXXX0001

TroubleReportState = 1

TroubleReportStatus = 8

Modify  Ticket=NYXXX00001,  EscalationList

State = 2 (provided)

Activities = “afterHourRepair”, “NoAccess” ….

Modify Response only signifies acknowledgement

VerifyRepairCompletionRequest  Ticket=NYXXX00001,

CloseOutVerificatoin = 1 (verified)

Verizon

TA Customer

Verizon

TA Customer

Verification of

Repair

AttrivuteValueChange   Ticket = NYXXX0001

TroubleReportState = 4

TroubleReportStatus = 27

AttrivuteValueChange   Ticket = NYXXX0001

TroubleReportState = 3

TroubleReportStatus = 26

OutageDuration, CloseOutNarrative, TroubleFound …

Modify  Ticket=NYXXX00001,  EscalationList

State = 1 (request)

Level = 2

Modify Response only signifies acknowledgement

AttrivuteValueChange   Ticket = NYXXX0001

Escalation List

State = 3 (denied)

Level = 2

Escalation

Denied

Authorization

Approved

Create  Ticket=NYXXX00001,  AuthorizationList

State = 1 (provided)

Activities = “afterHourRepair”, “NoAccess” ….

AttrivuteValueChange   Ticket = NYXXX0001

AuthorizationList

State = 1 (requested)

Activities = “afterHourRepair”, “NoAccess” ….

VerifyRepairCompletionRequest  Ticket=NYXXX00001,

CloseOutVerificatoin = 2,3,4 (denied)

Verification of

Repair

AttrivuteValueChange   Ticket = NYXXX0001

TroubleReportState = 3

TroubleReportStatus = 26

OutageDuration, CloseOutNarrative, TroubleFound …

X

All modifies will be rejected