Wireless Supplement to 9-1-1 Activation Guide

September, 2003

# Table of Contents

1.0	Introduction	1

1.1	History	1

1.2	Notification Process	1

2.0	Ordering Wireless E 9-1-1 Services	1

2.1	Amendment to Interconnection Agreement	1

2.2	ASR Ordering Process	1

2.3	ESRD/ESRK	2

2.4	pANI Assignment	2

2.5	ESRD/ESRK Request Spreadsheet	2

3.0	ALI System Location Information	2

3.1	For Carriers deploying an NCAS or CAS Hybrid Solution, it is necessary to connect the Carrier’s Mobile Positioning Center (MPC) to the appropriate Verizon ALI systems.  Shown below is the ALI location and codes needed to establish data connectivity between the Carrier’s MPC and Verizon’s ALI:	2

4.0	Wireless E 9-1-1 Testing and Implementation Support	2

4.1	XXX	2

4.2	XXX	4

5.0	Methods to Provide Wireless 9-1-1 Services	4

5.1	Phase I	4

5.1.1	Call Path Associated Signaling (CAS)	4

5.2	Phase II	5

5.2.1	CAS Hybrid	5

5.2.2	Non Call Path Associated Signaling (NCAS)	5

6.0	Responsibilities of the parties	6

6.1	Wireless Carrier's Responsibilities and Functions in Interacting with Verizon	6

6.2	Verizon's Responsibilities and Functions with the Wireless Carrier	6

7.0	9-1-1 Selective Router Network Access	6

8.0	ATTACHMENT I - ESRD/ESRK REQUEST FORM	8

9.0	ATTACHMENT II - ESRD/ESRK REQUEST FORM	10

# Introduction

## History

FCC Docket No. 94-102 mandated the provisioning of 9-1-1 services within 180 days by wireless carriers when ordered by the Governmental Public Safety Agency.   The implementation of wireless 9-1-1 services is commonly provided in two phases.  Phase I provides the PSAP with a call back number of the wireless 9-1-1 caller and an approximate location of the call to the PSAP based on the location of the cell/site sector where the call originates.   Phase II also provides the call back number and cell/site sector where the call originates, and in addition provides more precise location information (latitude and longitude of the callers location).

## Notification Process

To enable either Wireless Phase I or II solutions, PSAPs must notify Wireless Carriers of their intent to provide Wireless Phase I or Phase II E 9-1-1 Services.  Once this notification is received by the Wireless Carrier, the Wireless Carrier may order Wireless E 9-1-1 Service from Verizon.  Verizon will then work with the carrier to implement service within 180 days of receiving a firm order commitment from the Carrier.   Verizon must also be provided  with written notification that a particular 9-1-1 jurisdiction has notified the Carrier that the Controlling 9-1-1 Authority has required Wireless Carriers to provide E-9-1-1 service within a jurisdiction served by Verizon.

# Ordering Wireless E 9-1-1 Services

## Interconnection Agreement

Before E 9-1-1 services can be ordered, terms and conditions relating to Wireless E 9-1-1 Phase I and Phase II must be effective in the interconnection agreement between Verizon and the Carrier in the applicable state.  If necessary, a separate amendment must be negotiated between Verizon and each Carrier for each State within Verizon’s serving area.

The Wireless Carrier should contact their Verizon Account Manager in order to arrange to amend their existing Interconnection Agreement with Verizon.

## ASR Ordering Process

Verizon’s standard ASR ordering process is the vehicle for ordering Verizon Wireless E 9-1-1 services (see the Verizon E 9-1-1 Activation Process Guide.)

## ESRD/ESRK

The use of the Emergency Service Routing Digit (ESRD) or Emergency Service Key (ESRK) makes wireless E 9-1-1 unique from other wholesale offerings.  The ESRD or ESRK is utilized to obtain wireless caller information.  These are commonly referred to as pseudo Automatic Number Identification (pANI) numbers.

## pANI Assignment

Verizon strongly recommends that carriers obtain and use pANI numbers assigned by Verizon’s pANI Administrator.  These pANI assignments use a format of “NPA-511-XXXX”, or “NPA-211-XXXX”, to distinguish wireless callers at the Public Safety Answering Point (PSAP).

## ESRD/ESRK Request Spreadsheet

The Verizon ESRD/ESRK Request Spreadsheet (see Attachment I) serves as the document used by our internal departments to establish wireless E 9-1-1 data services.  Whether using Verizon-assigned pANI numbers or numbers from existing carrier-owned numbering pools, it will be necessary for each wireless carrier (or their agent) to complete and forward the Verizon ESRK-ESRD Request Spreadsheet to w911.pani.request@verizon.com .  Verizon will typically respond with pANI assignments within three business days.

# ALI System Location Information

For Carriers deploying an NCAS or CAS Hybrid Solution, it is necessary for the carrier or their third party provider to ensure connectivity to the appropriate Verizon ALI systems.  See Attachment II for the ALI location and codes needed to establish data connectivity between the Carrier or their third party provider and Verizon’s ALI.

# Wireless E 9-1-1 Testing and Implementation Support

## E-Mail Request to Schedule Testing

To ensure that Verizon testing resources are available for testing steering/trunking/database elements, the wireless carrier must forward an email requesting testing assistance to 911.test.request@verizon.com.

The email must include the following minimum information:

Carrier Name

Testing Contact Name & Tel

Date & Time of Testing

PSAP Name & State

26 Code of Trunks to be tested

Conference Bridge # and Pass code

ESRK/ESRD Ranges Involved

## Timing

The test request email should be sent with sufficient lead time to allow scheduling prior to the planned testing date.

# Methods to Provide Wireless 9-1-1 Services

## Phase I

Call Path Associated Signaling (CAS)

When a wireless subscriber makes a 9-1-1 call, the Wireless carrier forwards this call to Verizon’s 9-1-1 Selective Router. The Wireless carrier passes the call back number, and the ESRD (the ESRD is a unique 10 digit Pseudo ANI assigned by the carrier to a particular cell site/sector location) of the originating cellular 9-1-1 call to the 9-1-1 Selective Router.  Upon receipt of the call, the 9-1-1 Selective Router selectively routes the call to the appropriate PSAP based on ESRD passed from the Mobile Switching Center (MSC). The 9-1-1 Selective Router forwards the call to the PSAP with the call back number and the ESRD.  The PSAP then queries the Verizon-controlled ALI database for the ALI associated with the ESRD.  Verizon responds to the query with the cell site and sector location associated with that ESRD.

This method of Wireless 9-1-1 service typically requires the Selective Router and/or PSAP to modify their hardware and software to receive twenty-digits and upgrade their enhanced MF trunks from the 9-1-1 Selective Router.

Non Call Path Associated Signaling (NCAS)

When a wireless subscriber makes a 9-1-1 call, the Wireless carrier forwards this call to Verizon’s 9-1-1 Selective Router.  The Wireless carrier passes an ESRK to the 9-1-1 Selective Router.  ESRKs are assigned geographically to a carrier based on the Emergency Service Zone (ESZ), after which, they are assigned on a call-by-call basis as 9-1-1 calls originate.  The 9-1-1 Selective Router selectively routes the call to the appropriate PSAP based on the ESRK of the call. The PSAP then queries the Verizon controlled ALI database for the ALI associated with the ESRK.   At the same time that the Wireless Carrier passes the ESRK to the E 9-1-1 Selective Router it also transmits the call-back number and the cell/sector location to the Wireless Carrier controlled database or one controlled by a third-party provider hired by the Wireless Carrier.

When the PSAP query is received at Verizon’s ALI database, the Verizon ALI database “steers” the query to the appropriate Carrier-controlled database for the call-back number and the Cell Site/Sector of the originating caller.  The Verizon ALI Database then formats this information into an ALI screen display and passes it on to the PSAP.

## Phase II

### CAS Hybrid

When a wireless subscriber makes a 9-1-1 call, the Wireless carrier forwards this call to Verizon’s 9-1-1 Selective Router.  The Wireless carrier passes the call-back number, and the ESRD to the 9-1-1 Selective Router.  Concurrently, the 9-1-1 selective Router .  The PSAP then queries the Verizon controlled ALI database with the call back number  for the associated ALI information.  Upon receiving this query, the Verizon ALI database queries the Wireless Carrier- controlled Mobile Positioning Center (MPC), extracts the latitude/ longitude of the callers location and responds to the PSAP with this information and the cell site/sector information associated with the ESRD retained in the Verizon-controlled ALI database.  If the latitude/longitude information is not available at the time of the initial query, the PSAP must manually initiate a re-bid query to obtain the geographic information.

This method of Wireless 9-1-1 service typically requires the Selective Router and/or PSAP to modify their hardware and software to receive twenty-digits and upgrade their enhanced MF trunks from the 9-1-1 Selective Router.

### Non Call Path Associated Signaling (NCAS)

When a wireless subscriber makes a 9-1-1 call, the Wireless Carrier forwards this call to Verizon’s 9-1-1 Selective Router.  The Wireless carrier passes an ESRK to the 9-1-1 Selective Router.  ESRKs are assigned geographically to a carrier, and then assigned on a call by call basis as 9-1-1 calls originate.  The 9-1-1 Selective Router selectively routes the call to the appropriate PSAP. The PSAP then queries the Verizon-controlled ALI database for the ALI associated with the ESRK.  At the same time that the Wireless Carrier passes the ESRK to the E 9-1-1 Selective Router, it also transmits the call-back number and the cell/sector location to the Wireless Carrier controlled database or one controlled by a third party provider hired by the Wireless Carrier.  When the PSAP query is received at Verizon’s ALI database, the Verizon ALI database “steers” the query to the appropriate Carrier-controlled database for the call back number, cell site/sector and latitude/longitude of the originating caller.  The Verizon ALI Database then formats this information into an ALI display and passes it on to the PSAP.  If latitude/longitude information is not available at the time of the initial query, the PSAP must manually initiate a re-bid query to obtain the geographic information.

# Responsibilities of the parties

## Wireless Carrier's Responsibilities and Functions

- Provide a copy of the PSAP’s notification letter to the Wireless Carrier requiring Phase I/II service to Verizon.

- Coordinate trunk requirements with Verizon and issue ASR to build trunks from the MSC to the 9-1-1 Selective Router(s).

- Coordinate circuit requirements from Mobile Switching Center (MSC) with NCAS provider, if applicable.

- Request pANI (ESRD/ESRK) numbers from the Verizon pANI Administrator.

- Perform pANI (ESRD/ESRK) assignment for cell tower/sectors in a given PSAP jurisdiction.

- If NCAS will be used, a Letter of Authorization must be submitted by the wireless carrier to Verizon’s Contract Administrator that states delegation of authority for data entry.

- A letter must also be submitted by the third party provider stating that they represent the wireless carrier for data entry to Verizon along with a letter of authorization from the Carrier.

- Initiate amendment of existing appropriate Wireless Interconnection Agreement.

## Verizon's Responsibilities and Functions with the Wireless Carrier

- Obtain pANI request from wireless carriers or database providers; assign and respond to carriers with assignments.

- Build trunk orders submitted by the wireless carriers.

# 9-1-1 Selective Router Network Access

All Wireless Carriers are required to provide 9-1-1 Trunks from their Mobile Switching Center to Verizon's 9-1-1 Selective Router switches.  All trunking to the Verizon 9-1-1 Selective Router switches will be type 2C or Feature Group D type Message trunking.

For more information pertaining to the access of Verizon's 9-1-1 network, please go to the web page at www.Verizon.com/wholesale   (then key on the E 9-1-1 portal).  It contains information on 9-1-1 Selective Routers; PSAPs subtended by those Selective Routers and other pertinent network access information.

# ATTACHMENT I - ESRD/ESRK REQUEST FORM

| Wireless Carrier Information | Required Entries |
| --- | --- |
| Wireless Carrier Name |  |
| Contact Name |  |
| Contact Tel |  |
| Contact Mailing Address |  |
| Contact E-Mail Address |  |
| Enter the NENA ID and Operating Company Number (OCN) |  |
| Service Phase (enter Phase I or II) |  |
| Service Type (enter CAS, NCAS or CAS Hybrid) |  |
| Authorizing 9-1-1 Jurisdiction Information |  |
| Jurisdiction Name |  |
| Jurisdiction State |  |
| Jurisdiction NPA |  |
| Contact Name |  |
| Contact Tel |  |
| Contact Mailing Address |  |
| Contact E-Mail Address |  |
| NCAS/CAS Database Provider Information |  |
| Company Name |  |
| Contact Name |  |
| Contact Tel |  |
| Contact Mailing Address |  |
| Contact E-Mail Address |  |
| Quantity of ESRK/ESRD Numbers Requested |  |
| List the PSAPs the wireless calls (p-ANIs) will be selectively routed to: |  |
| If an existing Log In ID will be used to transmit pANI records, enter the Log In ID here, otherwise enter "NEW" |
| If an existing NCAS port will be used, ENTER THE NAME OF THE ALI SERVER to be used for Steering, the Port Identity Number and 3rd Party owner here, otherwise enter "SEE BELOW" |
| To be completed only if a new NCAS port is being established |  |
| 3rd Party Data Tech Name |  |
| Contact Tel |  |
| Contact E-Mail Address |  |
| Router IP Address and Subnet |  |
| Facility IP Address and Subnet |  |
| Router Loopback IP Address |  |
| Frame Type |  |
| To Be Completed by Verizon pANI Administrator | Verizon Only Entry |
| ESRK-ESRD (pANI) Range Assigned |  |
| Date Assigned |  |

# ATTACHMENT II - ESRD/ESRK REQUEST FORM

ALI Locations and Codes

| ST | Site | Router or ALI CLLI | ALI Type |
| --- | --- | --- | --- |
| CA | Long Beach, CA Everett, WA | LNBHCAXSD02 EVRTWAXAD04 | ALISA |
| FL KY | Tampa, FL Ft. Wayne, IN | TAMPFLLXAIED FTWYINXF1ED | ALISA |
| NY NE | Pearl River, NY Burlington, MA | PRRVNYBP_E31 PRRVNYBP_E32 | ALISA |
| VA WV NJ MD D.C. | Freehold, NJ Silver Spring, MD | FRHDNJMA_EC31 FRHDNJMA_EC32 | ALISA |
| AL | Dothan C.O. | DTHNALXAHRA | HP3000 |
| IL | Bloomington C.O. | BLTNILXDHRA | HP3000 |
| IL | Carbondale C.O. | CRDLILXEHR6 | HP3000 |
| IL | De Kalb C.O. | DKLBILXAHR7 | HP3000 |
| IL | Jacksonville C.O. | JCVLILXCHR3 | HP3000 |
| IL | Macomb C.O. | MCMBILXDHR2 | HP3000 |
| IL | Marion C.O. | MARNILXEHR3 | HP3000 |
| IL | Mascoutah C.O. | MSCTILXEHR1 | HP3000 |
| IL | Olney C.O. | OLNYILXEHR2 | HP3000 |
| IN | Elkhart C.O. | EKHTINXAHR6 | HP3000 |
| IN | Ft. Wayne C.O. | FTWYINXAHRH | HP3000 |
| IN | Jasper C.O. | JSPRINXAHR6 | HP3000 |
| IN | Lafayette C.O. | LFYTINXAHR5 | HP3000 |
| IN | Portage C.O. | PRTGINXAHR5 | HP3000 |
| IN | Logansport C.O. | LGPTINXAHR2 | HP3000 |
| IN | Richmond C.O. | RCMDINXBHR5 | HP3000 |
| IN | Seymour C.O. | WYMRINXAHR4 | HP3000 |
| IN | Terre Haute C.O. | TRRHINXAHR4 | HP3000 |
| IN | Wabash C.O. | WBSHINXAHR2 | HP3000 |
| MI | Adrian C.O. | ADRNMIXGHR3 | HP3000 |
| MI | Alma C.O. | ALMAMIXGHR6 | HP3000 |
| MI | Bellaire C.O. | BLLRMIXGHR2 | HP3000 |
| MI | Muskegon C.O. | MSKGMIXKHR4 | HP3000 |
| MI | Roscommon C.O. | RSCMMIXHHR2 | HP3000 |
| MI | Three Rivers C.O. | THRRMIXTHR3 | HP3000 |
| MO | Branson C.O. | BASNMOXAHR5 | HP3000 |
| MO | Columbia C.O. | CLMAMOXAHR7 | HP3000 |
| MO | Wentzville C.O. | WNVLMOXAHR2 | HP3000 |
| MO | West Plains C.O. | WPLNMOXAHR1 | HP3000 |
| OH | Bowling Green C.O. | BELGOHXAHR5 | HP3000 |
| OH | Jackson C.O. | JCSNOHXAHR1 | HP3000 |
| OH | Marion C.O. | MARNOHXCHR6 | HP3000 |
| OH | Wilmington C.O. | WLMGOHXBHR3 | HP3000 |
| OR | McMinnville C.O. | MMVLORXXHR2 | HP3000 |
| OR | Beaverton C.O. | BVTNORXBHRA | HP3000 |
| SC | Georgetown | GRTWSCXAHR2 | HP3000 |
| TX | Denton C. O. | DNTNTXXAHR8 | HP3000 |
| TX | Garland C. O. | GRLDTXXAHR3 | HP3000 |
| WA | Kennewick C.O. | KNWCWAXBHR4 | HP3000 |
| WA | Mt Vernon C.O. | MTVRWAXXHRS | HP3000 |
| WA | Everett C.O. | EVRTWAXFHR7 | HP3000 |
| WI | Chilton C.O. | CITNWIXAHR1 | HP3000 |
| WI | Dodgeville C.O. | DGVLWIXAHR2 | HP3000 |
| WI | Portage C.O. | PRTGWIXAHR3 | HP3000 |
| WI | Wausau C.O. | WAUSWIXAHR8 | HP3000 |
| HI | Honolulu | SC/ALISA "A" is - HNLLHIMN3ED SC/ALISA "B" is - HNLLHIMN4ED | SCALISA |
| TX | Coppell/Longbeach | LB CLLI=LNBHCAXSD02 CP CLLI=LWVLTXXHD04 | SCALISA |